## Slide 1: Motivation on including 6Rx band in Basket WID NR_bands_xFeature_R20
3GPP TSG RAN WG4 Meeting #117 R4-2521293
Dallas, USA., 17th – 21st, Nov. 2025
Source: ZTE Corporation
Agenda Item: 13.1.2

## Slide 2: Backgroud
In the latest basket WID NR_bands_xFeature_R19 [1], it includes three objectives:
  Objective #1: UL-MIMO for a single band
    Specify PC3, PC2 UE for SUL bands, and specify PC5, PC3, PC2 and PC1.5 UE for NR bands with UL MIMO configuration in FR1
  Objective #2: 4Rx
    Support of 4Rx for the bands <2.6GHz added in this WI is optional
  Objective #3: 8Rx
    Support of 8Rx for the bands <2.6GHz added in this WI is optional
During the whole Rel-19, there are several new NR FR1 bands requested by the proponents. The latest status report for NR_bands_xFeature_R19 can be found in [2].
In Rel-20, proponents may request more new NR FR1 bands to support UL MIMO, 4Rx or 8Rx to provide higher throughput and better coverage. Therefore, a new WID NR_bands_xFeature_20 is needed.
.

## Slide 3: 6Rx in Rel-19
In R19 NR_ENDC_RF_Ph4 WID, 6Rx was included and all of the RF requirements have already been completed. The big CR to introduce requirements for 6Rx can be found in [3], wherein there are two following RF requirements defined:
  ΔTRxSRS: Defined as band agnostic
  ΔRIB,6R: Defined as band dependent.
For the supported bands, there were only 5 FR1 bands incorporated, which are n41, n77, n78, n79 and n104. In addition to that, 6Rx operation is supported for handheld UE and FWA form factor.
in [4], company would like to revise R19 NR_ENDC_RF_Ph4 WID scope to include two new FDD bands, i.e. n1 and n3. However, due to few of companies object to upscope the WID to include more bands, the original 6Rx scope was kept.

## Slide 4: Motivation on 6Rx bands in R20
As discussed in [4], the proportion of FDD network in current deployment is virtually identical to the one of TDD network, and FDD network is evolving towards more Tx number or even massive MIMO, the overall DL performance can be further improved when UE side enhancements happen. Therefore, it is essential to include FDD bands to support 6Rx operation.
There were only >2.6GHz TDD bands to support 6Rx operation in Rel-19, more TDD bands below 2.6GHz may be requested by operators to support 6Rx in Rel-20.
In order to avoid to use individual WIDs for different bands for the same feature, it is proposed to include 6Rx objective in NR_bands_xFeature_20 to include all possible bands requested by operators to support 6Rx in Rel-20.
For the 6Rx new bands, it can be foreseen that the work is only to define the ΔRIB,6R requirement for each band, which is the same with 4Rx and 8Rx.

## Slide 5: Proposal
Proposal 1: To include 6Rx objective in NR_bands_xFeature_R20 WID.
Proposal 2: The objective for 6Rx is proposed as below:
Specify the 6Rx REFSENS requirement for NR FR1 bands Support of 6Rx for the bands <2.6GHz added in this WI is optional Note 1: This scope is not subject to RAN4 block approval procedure Note 2: 6Rx bands of this WI are introduced in a REL-independent way starting from [release xx according to Table 5.4-1 of TS 38.307].However no changes to TS 38.307 are needed.

## Slide 6: REFSEN
[1] RP-252463, revised WID: Additional NR bands for NR features in Rel-19, ZTE, Huawei
[2] RP-252464 Status report for Additional NR bands for NR features in Rel-19, ZTE, Huawei
[3] R4-2511318, Big CR to TS38.101-1: Introduction of requirements for 6Rx, ZTE Corporation, Sanechips, Huawei, HiSilicon, AT&T, vivo, Apple, OPPO, Xiaomi, Ericsson
[4] RP-243012, Discussion on the scope of 6Rx, Huawei, HiSilicon

## Slide 7: Thank you