## Slide 1: Update on AI/ML Progress in 3GPP Core Groups
CMCC, Lenovo
3GPP TSG-RAN5 Meeting #108
Bengaluru, India, 25 – 29 August 2025 R5-253926

## Slide 2
Milestones
Work item was declared complete from RAN1 perspective in RAN1#121@May 2025. Need to finalize higher layer parameters and UE features for this project [1]
Study item was declared complete from RAN1 perspective in RAN1#121@May 2025 [5].

## Slide 3: Progress on WI NR_AIML_air during RAN4#115 (May 2025)

## Slide 4
RAN4: CSI reporting requirement framework for CSI prediction
Issue 1-1: Requirement considerations
Agreement:
The performance of AI based CSI prediction should not be worse than R16 etypeII.
The exact test procedure and configurations are FFS
The impact of different timeline between AI and R16 etype II should be also carefully analysed
Issue 1-3: Doppler handling
Agreement:
De-prioritize 100Hz Doppler in R19
  Consider 100Hz Doppler in the future release if needed

## Slide 5
RAN4: CSI reporting requirement framework for CSI prediction
Issue 1-5: SNR levels for training data and generalization
Agreement:
No need to capture anything explicit in RAN4 about training data in the spec,
For simulation calibration, SNR range alignment for training can be discussed separately
UE performance at more than one MCS should be tested
Model generalization can be discussed separately
Each individual test is expected to involve in single MCS
Issue 1-6: Simulation results and next steps
Agreement:
Updated simulation assumptions for CSI prediction are agreed in R4-2508102
Agreement:
LS on AI/ML functionality activation is agreed in R4-2508085

## Slide 6
RAN4: Testability and interoperability issues for beam management
Issue 2-2: Measurement period for inference
Agreement:
Case 1: The starting point is to use M, N, P (reference the values from an existing clause in the same version of the spec where the measurement period is defined)
Case 2: postpone discussion until RAN1 concludes
Issue 2-3: Rx beam knowledge and TCI handling
Agreement:
if the predicted Tx beam in Set A is QCL Type-D to a known Tx beam, the corresponding Rx beam is known.
If the predicted Tx beam in Set A is not QCL Type-D to a known Tx beam, depending on UE capability, the corresponding Rx beam may be known or unknown.
Known Rx beam means no additional Rx beam sweeping is needed
Unknown Rx beam means additional Rx beam sweeping is needed.
Rx beam is known mean TCI state is known if conditions below are also met

## Slide 7
RAN4: Testability and interoperability issues for beam management
Agreement (continued):
The following conditions related to whether the TCI state is known or unknown is defined as the starting point. Companies are invited to bring analysis.
The target TCI state is known when the following is met:
  The TCI state switch command is received within 1280 ms upon the last transmission of the RS resource for beam reporting or measurement and the UE has sent at least one L-1 RSRP report of the target TCI state (clause 8.10.2 of 38.133)
  Applies for case 1
  FFS for case 2
  Whether RS resource is only from set B should be clarified
    FFS on whether prediction also impacts if a TCI state is known or unknown
      Companies are invited to bring analysis on how prediction would impact whether a TCI state is known or unknown
      FFS on the time delay if prediction is used as a condition for a known TCI state
Issue 2-5: Simulation results
Agreement:
Updated simulation assumptions for beam prediction are agreed in R4-2508081

## Slide 8
RAN4: Requirements for positioning
Issue 3-1: Requirements for case 1
Agreement:
Discuss how to define a measurement delay requirement(reporting delay)
Do not define any positioning accuracy requirement
Issue 3-2: Report mapping for sample based timing measurement reporting
Agreement:
  Use the value of the legacy UL RTOA mapping for 1st sample
  FFS for the additional sample reporting
Issue 3-3: Requirements for case 3b
Agreement:
Reuse legacy path based Rx-Tx accuracy requirements for case 3b
Requirement applies only for the 1st path

## Slide 9: Progress on FS_NR_AIML_air_Ph2 during RAN4#115 (May 2025)

## Slide 10
RAN4: Two-sided CSI compression
For Option 3[2]
Agreements from RAN4#114bis
The encoder that corresponds to the standardized test decoder is stored within 3GPP
  TBC whether in a TR, or in any TS, whether in RAN4 or RAN5, or whether simply kept in a 3GPP database (with no reference from TR or TS)
  FFS whether several encoders would be captured (e.g. due to different complexity)
New agreement from RAN4#115:
The training dataset used to train the test decoder in 3GPP should be captured
  FFS whether channel, Eigenvectors or something else
Option3: Full decoder specification in standard.
Option4: TE vendor provides the test decoder.
Option 3 and 4 are similar[2]:
-An encoder, decoder and training dataset are always captured
-The difference is that for option 3, the TE vendor is mandated to use the standardized test decoder. In option 4 they could choose to use the reference test decoder or to create their own based on the standardized information.

## Slide 11
RAN4: Two-sided CSI compression
For Option 4a[2]
Agreements from RAN4#114bis
Dataset is specified for option 4a.
Assume reference decoder is captured.
New agreements from RAN4#115:
Reference encoder should be captured
FFS whether the labelled dataset is based on Eigenvector, channel estimation or something else
The study has only considered the case of a common assumption on model structure for the “own” test decoder. This corresponds to standardized model structure.
  Structure refers to backbone, numbers of layers, type of layers and all description of the model, but not the parameters.
  Interoperability in the case that the structure of the TE decoder is not specified has not been investigated

## Slide 12
RAN4: Two-sided CSI compression
For Option 4b[2]
Agreements from RAN4#114bis
Dataset is specified for option 4a.
FFS on dataset is captured for option 4b.
Assume reference decoder is captured.
FFS on reference encoder for option 4a
Test decoder structure is (i) fully specified or (ii) partially specified
NOTE: RAN4 understands that further decision on option 4a/4b and option 3 will be made in the future WI phase.
New agreements from RAN4#115:
Specify dataset to train frozen encoder and decoder
    TE vendor shall use the dataset to train the test decoder
    This is the same dataset as used to train the frozen encoder
    FFS whether the datasets consist of Eigenvector, channel or something else
The study has only considered the case of a common assumption on model structure for the “own” test decoder. This corresponds to standardized model structure.
  Structure refers to backbone, numbers of layers, type of layers and all description of the model, but not the parameters.
  Interoperability in the case that the structure of the TE decoder is not specified has not been investigated

## Slide 13
RAN4: Two-sided CSI compression
Other Agreements[2]:
If RAN1 direction C agreed, RAN4 and RAN1 should co-ordinate on model structure etc. for direction C due to the similarities between option 3/4 and direction C
Duplicated work is to be avoided
At the current moment in time, neither option 3 track 2, nor option 4a or 4b should be ruled out for a WI. Option 3 track 1 can be ruled out.
Option 3 and 4 are similar:
An encoder, decoder and training dataset are always captured
The difference is that for option 3, the TE vendor is mandated to use the standardized test decoder. In option 4 they could choose to use the reference test decoder or to create their own based on the standardized information.
Note:
n Direction C has been agreed and captured in R20 WI during RAN1#121@May 2025
RAN1 Direction C[3]:
Fully standardized reference model(s) and parameters with specified CSI generation part and/or CSI reconstruction part.
Notes: Agreements:
If RAN1 direction C agreed, RAN4 and RAN1 should co-ordinate on model structure etc. for direction C due to the similarities between option 3/4 and direction C
-Duplicated work is to be avoided

## Slide 14
RAN4: LCM requirements
Agreements[2]:
Activation delay:
Activation delay requirements created for the periodic, semi-persistent and aperiodic CSI reporting for beam prediction
  It is FFS for CSI prediction
For Option A, RAN4 will send LS to RAN2 to clarify the related mechanism.
[Note: RAN4 already sent LS R4-2508085 to RAN2]
For semi-persistent CSI reporting
  Activation delay starts at the reception of the MAC-CE/DCI
For aperiodic CSI reporting
  Activation delay starts at the reception of the DCI
Switching delay and Fallback delay:
Deprioritize the discussion on switching and fallback delay requirements and focus on activation/deactivation delay requirement, including both AI/nonAI, discussion.
Notes: Agreements:
If RAN1 direction C agreed, RAN4 and RAN1 should co-ordinate on model structure etc. for direction C due to the similarities between option 3/4 and direction C
-Duplicated work is to be avoided

## Slide 15
RAN4: LCM requirements
Agreements[2]:
Monitoring reporting delay and accuracy:
Discuss how to define delay and accuracy requirements for UE sided monitoring where the UE reports the metric:
BM-Case1 and possibly BM-Case 2
o Performance monitoring type 1 option 2
If it proves to be not possible to define, then reverse the agreement
Note: For BM-Case2, it may not be completed in Rel-19. If it is not covered in Rel-19, there would not be a monitoring delay requirement. If it would be in Rel-19, a monitoring delay requirement is needed.
CSI prediction:
CSI prediction, the details are subject to RAN1 decision
RAN4 will further study the feasibility to specify the corresponding delay and/or accuracy requirements for UE sided monitoring
Notes: Agreements:
If RAN1 direction C agreed, RAN4 and RAN1 should co-ordinate on model structure etc. for direction C due to the similarities between option 3/4 and direction C
-Duplicated work is to be avoided

## Slide 16
RAN4: Generalization
Agreements[2]:
The high level and general guidelines for the generalization test are provided as follow. The exact decisions are to be made case by case.
Study and , if feasible, define requirements for each AI/ML functionality
Define one test per UE capability as a minimum
  o FFS >1 test per UE capability
Define a minimum set of test configurations (including NW sided conditions if any) as mandatory for testing of AI/ML-enabled Feature
Potential areas to consider for generalization testing:
gNB array parameters: port layouts, array size, antenna virtualization
propagation conditions
Deployment scenarios: Carrier frequencies; Speeds; Indoor/outdoor; Bandwidths
SNR
Notes: Agreements:
If RAN1 direction C agreed, RAN4 and RAN1 should co-ordinate on model structure etc. for direction C due to the similarities between option 3/4 and direction C
-Duplicated work is to be avoided

## Slide 17
RAN4: Post-deployment
Agreements[2]:
Option 2 (Post-deployment post-activation functionality testing based on performance monitoring) is prioritized.
it should be further investigated/established that reliable and testable monitoring procedures can be established for all use cases
Notes: Agreements:
If RAN1 direction C agreed, RAN4 and RAN1 should co-ordinate on model structure etc. for direction C due to the similarities between option 3/4 and direction C
-Duplicated work is to be avoided

## Slide 18: Progress on WI NR_AIML_air during RAN2#130 (May 2025)

## Slide 19
RAN2: LCM for UE-sided model for Beam Management use case
Agreements for Discussion on inference configurations and related procedures[1]:
When UE indicates that a periodic CSI-ReportConfig is not applicable, the gNB is expected to release the configuration (i.e., UE autonomous release is not supported).
The UE continues to perform the inference and reporting until the configuration is released. It is up to network implementation what to do with UE reported beam predicted reporting after UE indicates that a CSI-ReportConfig is not applicable.
The UE shall report when CSI-ReportConfig becomes not applicable
RAN2 assumes applicability report for Option B (sets of inference related parameters) can be included in both RRCReconfigurationComplete and UAI (i.e., same as Option A). This can be revisited based on RAN1 conclusions/final signaling design
On how to handle RRC configuration in IDLE/INACTIVE/RLF, follow the legacy UE behaviour in TS 38.331 on whether to release or keep the RRC configuration in CSI-MeasConfig (for inference configuration) and OtherConfig (for applicability reporting and UE data collection preference configurations). FFS Whether applicability reporting via RRCReestablishmentComplete and RRCResumeComplete is supported (if it comes for free)
RAN2 confirm that option A and option B can be configured in the same RRCReconfiguration message with the unified applicability report procedure.
    Option A: one or more of CSI-ReportConfig for inference configuration (wherein the associated ID may be configured in CSI framework as working assumption applied) [4]
    Option B: One set or multiple sets of inference related parameters for applicability report only (not for inference) [4]

## Slide 20
RAN2: LCM for UE-sided model for Beam Management use case
Agreements for Discussion on UE-side data collection configuration and related procedures[1]:
Introduce “release configuration” flag instead of inapplicability cause to indicate UEs preference to release a configuration (e.g. due to model in availability in the local device FFS reason to be specified)
Introduce a flag in OtherConfig indicating whether applicability reporting via UAI is enabled or disabled. Assume this applies to Option A and B, FFS if anything different needs to be done for option B (if specified)
The UE doesn’t need to measure the candidate data collection configuration(s). This will be specified in RAN2 specs.
For beam management, candidate data collection configuration includes at least:
  CSI-ResourceConfigId of Set A
  CSI-ResourceConfigId of Set B
  One/two associated IDs (up to whether Set B is equal/subset of Set A or not) according to RAN1 agreements
  FFS the details of how this is signalled (e.g. CSIReport config or simplified signaling).

## Slide 21
RAN2: NW-side data collection for the beam management use case
Agreements[1]:
As a starting point, the data logging is captured in RRC specs.
1-bit indication on whether to release or retain un-retrieved data in RRCReconfiguration with synch is introduced. In case of HO, the source sends the 1-bit indication to target cell in HO preparation message. This 1-bit indication is included in HO command by target cell (if the target cell wants to keep the data). We should have single UE behaviour, when it receives the indication it keeps it, otherwise it removes it. Notify RAN3
Buffer threshold to trigger data availability indication should be set based on specific size, e.g., KB instead of percentage
UAI related to buffer status or low power state is triggered only once when specific conditions are met (e.g., buffer full/threshold, and low power state). A prohibit timer is not necessary for UAI related to buffer status or low power state
No additional signaling from the UE is required when the low power issue is resolved
No additional signaling from the UE is required when the buffer full issue is resolved
Data is collected on per data logging configuration basis and UE indicates data logging configuration ID. An indication of the “gap” is needed. “Gap” is time interval larger than the configured logging periodicity. FFS if timestamp and relative time stamp for each group is needed per “group”.
The UE should report the CGI of the serving cell whenever feasible. If CGI is unavailable, the UE shall log PCI-ARFCN as a fallback
RAN2 confirms that previous agreement excluded SN being configured for OAM centric data collection.

## Slide 22
RAN2: LCM for UE-sided model for Positioning use case
Agreements[1]:
The field dl-PRS-ResourcePrioritySubset in IE NR-DL-PRS-Info should be ignored for NR AI/ML positioning. Remove corresponding 'Editor's Note' from the running CR
Regarding the applicability of IE NR-DL-PRS-ProcessingCapability to NR AI/ML positioning Case 1, wait for further RAN1 input and keep the current "Editor's Note" in the running CR for now.
Regarding the applicability of IE NR-DL-PRS-QCL-ProcessingCapability to NR AI/ML positioning Case 1, wait for further RAN1 input and keep the current "Editor's Note" in the running CR for now.
Regarding the applicability of IE NR-DL-PRS-ResourcesCapability to NR AI/ML positioning Case 1, wait for further RAN1 input and keep the current "Editor's Note" in the running CR for now.
The IE NR-On-Demand-DL-PRS-Configurations-Selected-IndexList is also applicable to NR AI/ML positioning Case 1. The corresponding Editor's Notes in clause 6.4.3, 6.5.10.1, and 6.5.11.1 can be removed.
The IE NR-AI-ML-PositioningProvideAssistanceData contains (at least) all assistance data elements from UE-based DL-TDOA as starting point. This will be revised when additional RAN1 input is available. The current Editor's Note is kept for now.
The IE NR-AI-ML-PositioningRequestAssistanceData contains (at least) all assistance data elements from UE-based DL-TDOA as starting point. This will be revised when additional RAN1 input is available. The current Editor's Note is kept for now.

## Slide 23
RAN2: LCM for UE-sided model for Positioning use case
Agreements (Continued) [1]:
The IE NR-AI-ML-PositioningRequestLocationInformation contains (at least) the AssistanceAvailability flag. Additional details/information can be discussed via company contributions.
The IE NR-AI-ML-PositioningProvideCapabilities contains (at least) all capabilities from UE-based DL-TDOA as starting point, except the capability related to DL-PRS processing (see #LPP-2/3/4). This will be revised when additional RAN1 input is available. The current Editor's Note is kept for now.
A target UE can obtain the "ground-truth label" information via existing MO-LR procedures. No additional RAN2 specification impacts are foreseen
Reuse the existing NR-DL-TDOA-LocationServerErrorCauses structure for AI/ML positioning Case 1, and do not introduce additional error causes in NR-DL-AI-ML-LocationServerErrorCauses.
Introduce ‘DL AIML positioning not available’ as new target device error cause for AI/ML positioning case 1, to indicate UE cannot perform positioning method (e.g. model not available and performance monitoring outcome not available).
positioning Integrity is supported for AI/ML positioning Case 1
No new LPP message is introduced for performance monitoring purposes
The IE NR-PRU-DL-Info is also applicable to NR AI/ML positioning Case 1. The corresponding Editor's Notes in clause 6.4.3 can be removed. FFS if more PRUs are needed to be included for training purposes
NR-SelectedDL-PRS-IndexList is applicable to AI/ML positioning Case 1.
To ensure the consistency between training and inference, the UE should be able to request assistance data associated with a specific group of TRPs. FFS the request associated information in on demand prs request..

## Slide 24: Progress on FS_NR_AIML_air_Ph2 during RAN2#130 (May 2025)

## Slide 25
RAN2: UE-side data collection & AI_ML model delivery options
Agreements[5]:
RAN2#130 discussed the topic of UE-side data collection and in particular on the impact of control plane solutions for the transfer of UE-side data from the UE. It was agreed to capture in the TR, the issues related to CP solutions when a large amount of data (if there is a large amount of data) are to be transferred from a UE (e.g. need for segmentation and its implications)
On this topic the following post email discussion was agreed:
[POST130][033][AI PHY] UE Side data collection (Ericsson)
Intended outcome: TP capture CP analysis
Deadline: 4 weeks
RAN2#130 discussed the topic of AI_ML model delivery options focusing in particular on the principles. However, no agreements were reached.

## Slide 26
Observations and Proposals
Observation 1: R19 AIML WI in RAN1 was declared complete in RAN1#121@May 2025, while higher layer parameters and UE features for this project still need to finalized in RAN2/RAN4.
Observation 2: R19 AIMI SI in RAN1 was declared complete in RAN1#121@May 2025.
Observation 2: Progress for R19 AIML WI/SI has been observed in RAN2#130@May 2025, and probably will be declared complete in RAN2#131.
Observation 3: Progress for R19 AIML WI/SI has been observed in RAN4#115@May 2025, but still quite a few open issues are identified/unresolved yet.
Proposal 1: RAN5 continues to look for opportunity to start contributing to topics that could speed up the work of Rel-19 AIML core WI.
Proposal 2: Besides the areas below, RAN5 continues to identify more areas where RAN5 expertise may help to progress core group work.
    AIML conformance test framework.
    MU/TT analysis based on RAN4 test parameters and test setup.
    UE lab conformance aspects of post-deployment testing.
Notes: Work item was declared complete from RAN1 perspective in RAN1#121@May 2025 [1]
Need to finalize higher layer parameters and UE features for this project [1]

## Slide 27
Reference
RP-251185, SR for WI on AI/ML for NR air interface, 3GPP TSG RAN meeting #108, Prague, Czech Republic, June 9-13
R4-2508051, WF on AI/ML part 2, 3GPP TSG-RAN WG4 Meeting#115, Malta, 19th – 23rd May, 2025
R1-2410922, LS on signalling feasibility of dataset and parameter sharing, 3GPP TSG RAN WG1 #119, Orlando, US, November 18th – 22nd, 2024
R1-2410898, Reply LS on applicable functionality reporting for beam management UE-sided model, 3GPP TSG RAN WG1 #119, Orlando, US, November 18th – 22nd, 2024
RP-251184, SR for Study on AI/ML for NR air interface phase 2, 3GPP TSG RAN meeting #108, Prague, Czech Republic, June 9-13

## Slide 28: Thank you !