## Slide 1
3GPP TSG RAN5#108 R5-254881
Bengaluru, India, Aug 25-29, 2025
Agenda item: 4.2.3
Source: Qualcomm Inc
Title: AIML status update
Document for: Information

## Slide 2
AIML status update – CSI prediction and CSI Compression
AIML usecase | Rel18 agreements | Rel18 pending items | Rel19 agreements | Rel19 pending items
CSI prediction | N/A | N/A | TDL channel model to be considered for Rel19 tests RAN4’s legacy framework of throughput ratio w.r.t Rel15 Type I codebook to be reused to verify AIML based predicted PMI Channel condition will not change during the middle of the test | All the current agreements need to go into TS 38.101-4. Pending discussion on test config details for FDD and TDD
CSI compression | Study Item phase | Study Item phase | Study Item phase Evaluated the feasibility of fully specified decoder and partially specified decoder Agreed parameters that need to be specified in the spec for fully and partially specified decoder | Study Item phase Design structure and parameters of encoder-decoder for direction C and direction A, sub-direction 3a-1 of RAN1 Design performance tests for fully specified test decoder
Notes: Building Blocks – Code translating Specs into excel

## Slide 3
AIML status update – Beam Management
AIML usecase | Rel18 agreements | Rel18 pending items | Rel19 agreements | Rel19 pending items
BM – Spatio-Temporal prediction | Study Item Phase RAN4 agreed that the ground truth for the predicted RSRP is the ideal measurement of RSRP on the predicted Tx beam | Study Item Phase Selection of beam prediction metrics Decision of whether UE knows Rx beam of predicted Tx beam Evaluation period of spatio-temporal beam prediction | Agreed L1-RSRP accuracy and beam prediction accuracy to be the performance metrics Introduced UE capability that allows UE to indicate whether it knows Rx beam of predicted Tx beam Use CDL-based channel model as starting point | Evaluation period of spatio-temporal beam prediction. Testing methodology of spatio-temporal beam prediction Decide test setup: single AoA or Multi-AoA setup No test expected to be defined in Rel19
BM – Spatial beam prediction | Study Item Phase Same as above | Study Item Phase Selection of beam prediction metrics Decision of whether UE knows Rx beam of predicted Tx beam Evaluation period of spatial only beam prediction | Agreed L1-RSRP accuracy and beam prediction accuracy to be the performance metrics Defined some details of L1-RSRP accuracy and beam prediction accuracy metrics. Reuse evaluation period of legacy beam management as the eval period of reference resources in AIML based beam prediction Introduced UE capability that allows UE to indicate whether it knows Rx beam of predicted Tx beam Use CDL-based channel model as starting point | Inference time of spatial beam prediction. Does absolute L1-RSRP accuracy metric apply to all inferred beams Whether to define relative L1-RSRP accuracy for inferred beams Exact definition of TCI state switch in AIML BM. How to define performance tests Decide test setup: single AoA or Multi-AoA setup
Notes: Building Blocks – Code translating Specs into excel

## Slide 4
AIML status update - Mobility
AIML usecase | Rel18 agreements | Rel18 pending items | Rel19 agreements | Rel19 pending items
Mobility | N/A | N/A | Study Item Phase Ground truth definition of L3-RSRP prediction Absolute L3 predicted RSRP Definition of Relative L3-RSRP accuracy | Study Item Phase Ground truth definition of event prediction Overall test method for FR1 (FR2 is de-prioritized)
Notes: Building Blocks – Code translating Specs into excel

## Slide 5
AIML status update – Positional Accuracy
AIML usecase | Rel18 agreements | Rel18 pending items | Rel19 agreements | Rel19 pending items
Positioning Accuracy | Study Item Phase RAN4 scoped the five cases that RAN4 plenary considered for AIML based positioning | Study Item Phase Selection and details of the cases for which RAN4 requirements will be defined | RAN4 decided not to define requirement for case 2a and case 2b [out of Rel19 scope as per RAN plenary] | Whether and how to define requirement for case 1 Whether and how to define tests for case 3a and 3b
Notes: Building Blocks – Code translating Specs into excel

## Slide 6: Summary
Observation1: RAN4 still have not included requirements for any of the AIML scenarios in the core spec.
Observation2: There is no request from core group for RAN5 involvement at this time.
Observation3: As per the various AIML core group WI timeline, the earliest timeframe RAN5 can start its own WI is March 2026
Unique_ID | Name | Acronym | Release | Resource Names | Start | Finish | % Complete | Hyperlink
1081085 | Core part: AIML or NR air interface Phase 2 | NR_AIML_air_Ph2-Core | Rel-20 | R1 | 06/06/25 | 03/03/27 | 0% | RP-251870
1082085 | Perf. Part: AIML for NR air interface Phase 2 | NR_AIML_air_Ph2-Perf | Rel-20 | R4 | 06/06/25 | 09/09/27 | 0% | RP-251870
1081087 | Core part: AIML for mobility in NR | NR_AIML_Mob-Core | Rel-20 | R2 | 06/06/25 | 03/03/27 | 0% | RP-251864
1082087 | Perf. Part: AIML for mobility in NR | NR_AIML_Mob-Perf | Rel-20 | R4 | 06/06/25 | 06/06/27 | 0% | RP-251864
1060078 | Study on Artificial Intelligence (AI)/Machine Learning (ML) for NR air interface Phase 2 | FS_NR_AIML_air_Ph2 | Rel-19 | R1 | 14/10/24 | 09/09/25 | 90% | RP-250308
1020084 | Study on Artificial Intelligence (AI)/Machine Learning (ML) for mobility in NR | FS_NR_AIML_Mob | Rel-19 | R2 | 07/03/19 | 09/09/25 | 90% | RP-242393
1021093 | Core part: Artificial Intelligence (AI)/Machine Learning (ML) for NR air interface | NR_AIML_air-Core | Rel-19 | R1 | 13/12/23 | 09/09/25 | 85% | RP-250792
1022093 | Perf. part: Artificial Intelligence (AI)/Machine Learning (ML) for NR air interface | NR_AIML_air-Perf | Rel-19 | R4 | 18/08/24 | 03/03/26 | 10% | RP-250792
940084 | Study on Artificial Intelligence (AI)/Machine Learning (ML) for NR air interface | FS_NR_AIML_air | Rel-18 | R1 | 13/12/21 | 12/12/23 | 100% | RP-251186