3GPP TSG RAN5 Meeting #102	[DRAFT] R5-240020

Athens, Greece, 26 Feb – 01 Mar, 2024

Title:	[DRAFT] Reply-LS on Prohibition of GEA1 & GEA2 Support in all releases

Response to:	LS (SP-231782) on Prohibition of GEA1 & GEA2 Support in all releases from SA

Source:	3GPP RAN WG5

To:	3GPP SA, GCF Steering Group

Cc:	3GPP SA WG3, 3GPP RAN, PTCRB

Contact Person:

Name:	Petra Rauer

E-mail Address:	Petra dot Rauer at Vodafone dot com

Send any reply LS to:	3GPP Liaisons Coordinator, mailto:3GPPLiaison@etsi.org

Attachments:	none

1. Overall Description:

RAN5 would like to thank TSG-SA for the liaison statement notifying updates made to the latest version of all releases of TS 43.020 and TS 03.20 to prohibit the implementation of GEA1 and GEA2 in Mobile Stations of all releases. RAN5 also noted SA request to facilitate verification of non-support of GEA1 and GEA2 through RAN5 test specifications.

RAN5 is pleased to inform that Change Requests (CRs) proposing removal of GEA1 and GEA2 from common test environment as well as test cases verifying non-support of GEA1 and GEA2 in all RAN5 test specifications have been agreed by RAN5#102 Meeting. RAN5 had already defined the Test Case (TC) 44.2.5.2.5 in TS 51.010-1 to verify non-support of GEA1. A CR proposing to update TC 44.2.5.2.5 to also verify non-support of GEA2 has been agreed by RAN5#102 Meeting.

RAN5 agreed CRs shall be submitted for approval to TSG-RAN#103 Plenary meeting scheduled March 17 – 21 2024 at Maastricht. RAN5 expects TC 44.2.5.2.5 verifying non-support of GEA1 and GEA2 to be included in the next version of TS 51.010-1 scheduled to be published in March 2024 following TSG-RAN#103 meeting.

2. Actions:

To 3GPP SA Group.

ACTION: 	None.

To GCF Steering Group.

ACTION: 	3GPP RAN5 asks GCF Steering Group to take the above information into account.

3. Date of Next 3GPP RAN5 Meetings:

TSG RAN5 Meeting#103 	20th – 24th May 2024	Fukuoka, Japan.

TSG RAN5 Meeting#104 	19th – 23th August 2024	Maastricht, NL.