3GPP TSG-RAN5 Meeting #102	R5-241472

Athens, Greece, February 26th – March 1st, 2024

3GPP TSG RAN Meeting #103	RP-24xxxx

Maastricht, Netherlands, March 18-21, 2024

# Source:	Samsung, Huawei, Hisilicon, China Telecom

# Title:	New WID on UE Conformance – NR MIMO Evolution for Downlink and Uplink

# Document for:	Endorsement

Agenda Item:	7.5.1

3GPP™ Work Item Description

Information on Work Items can be found at http://www.3gpp.org/Work-Items 
See also the 3GPP Working Procedures, article 39 and the TSG Working Methods in 3GPP TR 21.900

Title:  UE Conformance – NR MIMO Evolution for Downlink and Uplink

Acronym: NR_MIMO_evo_DL_UL-UEConTest

Unique identifier:

| This WID includes a Testing part | X |
| --- | --- |
| and it addresses the following 3GPP work area: | Radio Access | X |
|  | Core Network |  |
|  | Services |  |

Potential target Release:	Rel-18

# 1	Impacts

| Affects: | UICC apps | ME | AN | CN | Others (specify) |
| --- | --- | --- | --- | --- | --- |
| Yes |  |  |  |  |  |
| No | X | X | X | X |  |
| Don't know |  |  |  |  |  |

# 2	Classification of the Work Item and linked work items

### 2.1	Primary classification

This work item is a

| Normative Work Item: tick applicable boxes below |
| --- |
|  | Stage 1 |
|  | Stage 2 |
|  | Stage 3 |
| X | Other (e.g. testing) |

### 2.2	Parent Work Item

The following lists of RAN1 work items that will be tested in this RAN5 work item will be maintained in future revisions of this WI description:

| Parent Work / Study Items |
| --- |
| Acronym | Working Group | Unique ID | Title (as in 3GPP Work Plan) |
| NR_MIMO_evo_DL_UL |  | 940096 | NR MIMO evolution for downlink and uplink |
| NR_MIMO_evo_DL_UL-Core | R1 | 940196 | Core part: NR MIMO evolution for downlink and uplink |
| NR_MIMO_evo_DL_UL-Perf | R1 | 940296 | Perf. part: NR MIMO evolution for downlink and uplink |

### 2.3	Other related Work Items and dependencies

| Other related Work/Study Items (if any) |
| --- |
| Acronym | Unique ID | Title | Nature of relationship |
|  |  |  | {optional free text} |

# 3	Justification

MIMO is one of the key technologies in NR systems and is successful in commercial deployment. In Rel-15/16/17, MIMO features were investigated and specified for both FDD and TDD systems, of which major parts were for downlink MIMO operation. In Rel-18, it is important to identify and specify necessary enhancements for uplink MIMO, while necessary enhancements on downlink MIMO that facilitate the use of large antenna array, not only for FR1 but also for FR2, would still need to be introduced to fulfil the request for evolution of NR deployments. This comprises the following areas of enhancement.

First, significant loss of performance for a UE at high/medium speed has been observed in commercial deployments especially in multi-user MIMO (MU-MIMO) scenarios. As the performance loss is partly caused by outdated CSI, enhancements on CSI acquisition to alleviate such loss can be beneficial. Second, the unified TCI framework was introduced in Rel-17 which facilitates streamlined multi-beam operation targeting FR2. As Rel-17 focuses on single-TRP use cases, extension of unified TCI framework that focuses on multi-TRP use cases is beneficial. Third, due to the increasing need for multiplexing capacity of downlink and uplink demodulation reference signal (DMRS) from various use cases, there is a need for increasing the number of orthogonal ports for DMRS. Fourth, features for facilitating multi-TRP deployments have been introduced in Rel-16/17 focusing on non-coherent joint transmission (NC-JT). As coherent joint transmission (CJT) improves coverage and average throughput in commercial deployments with high-performance backhaul and synchronization, enhancement on CSI acquisition for FDD and TDD, targeting FR1, can be beneficial in expanding the utility of multi-TRP deployments. Fifth, as advanced UEs (e.g. CPE, FWA, vehicle, industrial devices) become more relevant, introducing necessary enhancements to support for 8 antenna ports as well as 4 and more layers for UL transmission can offer the needed improvement for UL coverage and average throughput. Sixth, with the introduction of features for UL panel selection in Rel-17, advanced UEs (e.g. CPE, FWA, vehicle, industrial devices) can benefit from higher UL coverage and average throughput with simultaneous UL multi-panel transmission. Finally, some further enhancement to facilitate UL multi-TRP deployments via two timing advances (TAs) and enhanced UL power control can offer additional UL performance improvement.

The Rel-18 WI NR_MIMO_evo_DL_UL-Core has been 100% completed and NR_MIMO_evo_DL_UL-Perf has been 25% completed at RAN#102 meeting. According to the requirements of NR network deployment and performance optimization, it is justified now to start the work on the corresponding UE conformance test specifications for NR MIMO evolution for DL and UL features in 3GPP RAN WG5 to meet the market requirements in time.

# 4	Objective

### 4.1	Objective of SI or Core part WI or Testing part WI

The objective of this work item is to define the UE conformance requirements corresponding to ‘WI NR_MIMO_evo_DL_UL’, by analysing the test case impact, applicability and test environment, and updating the relevant conformance specifications.  This work item will cover Signaling, RF, Demod and RRM conformance test specifications for NR_MIMO_evo_DL_UL.

### 4.2	Objective of Performance part WI

N/A

### 4.3	RAN time budget request (not applicable to RAN5 WIs/SIs)

N/A

# 5	Expected Output and Time scale

| New specifications {One line per specification. Create/delete lines as needed} |
| --- |
| Type | TS/TR number | Title | For info at TSG# | For approval at TSG# | Remarks |

NOTE:	If this is a RAN WI including Core and Perf. part, then all new Core part specs have to be listed first and then all new Perf. part specs. Indicate "Core part" or "Perf. part" under Remarks for each spec.
By default a new specs can only be new for one of both parts.

| Impacted existing TS/TR {One line per specification. Create/delete lines as needed} |
| --- |
| TS/TR No. | Description of change | Target completion plenary# | Remarks |
| TS 38.508-1 | Introduction of common test environment for RF/RRM/Demod test cases for R18 NR_MIMO_evo_DL_UL. | TSG RAN#110 (Dec-25) |  |
| TS 38.508-2 | Introduction of common implementation conformance statement (ICS) for R18 NR_MIMO_evo_DL_UL. | TSG RAN#110 (Dec-25) |  |
| TS 38.523-1 | Introduction of protocol test cases for R18 NR_MIMO_evo_DL_UL. | TSG RAN#110 (Dec-25) |  |
| TS 38.523-2 | Applicability statements R18 NR_MIMO_evo_DL_UL test cases. | TSG RAN#110 (Dec-25) |  |
| TS 38.523-3 | Introduction of test model R18 NR_MIMO_evo_DL_UL test cases. | TSG RAN#110 (Dec-25) | Note: Progress of TTCN development of the new protocol test cases is tracked in MCC TF160 reports to RAN5/RAN. |
| TS 38.521-2 | Introduction of RF test cases for R18 NR_MIMO_evo_DL_UL. | TSG RAN#110 (Dec-25) |  |
| TS 38.521-4 | Introduction of Demod test cases for R18 NR_MIMO_evo_DL_UL. | TSG RAN#110 (Dec-25) |  |
| TS 38.533 | Introduction of the RRM test cases for R18 NR_MIMO_evo_DL_UL. | TSG RAN#110 (Dec-25) |  |
| TS 38.522 | Applicability statements of the R18 NR_MIMO_evo_DL_UL. | TSG RAN#110 (Dec-25) |  |
| TR 38.903 | Introduction of the analysis of MU and TT for R18 NR_MIMO_evo_DL_UL. | TSG RAN#110 (Dec-25) |  |
| TR 38.905 | Introduction of test points for R18 NR_MIMO_evo_DL_UL test cases. | TSG RAN#110 (Dec-25) |  |

NOTE:	If this is a RAN WI including Core and Perf. part, then all new Core part specs have to be listed first and then all new Perf. part specs. Indicate "Core part" or "Perf. part" under Remarks for each spec.
If an existing spec is affected by both (Core part and Perf. part), then it has to be listed twice with appropriate approval dates.

# 6	Work item Rapporteur(s)

Tang, Runsen, Samsung, runsen.tang@samsung.com

Zhang, Yaping, Huawei, zhangyaping13@huawei.com

Wu, Jingzhou, China Telecom, wujingzhou@chinatelecom.cn

# 7	Work item leadership

RAN5

# 8	Aspects that involve other WGs

None

# 9	Supporting Individual Members

Supporting IM name

Samsung

HiSilicon

Huawei

China Telecom

AT&T

China Unicom

Ericsson

Lenovo

Mediatek

Motorola Mobility

NTT DOCOMO

Orange

Verizon

Vodafone

ZTE