## Slide 1: HPUE in NR TDD 4.9GHz Band for US Operation
Agenda Item: 9.4.1
Source: AT&T, FirstNet, APCO, Fujitsu, Qualcomm
Document for: Discussion/Decision
3GPP TSG RAN Meeting #109 RP-252450
Beijing, CN, 15th – 18th September 2025

## Slide 2: Background
Regarding the WI of NR TDD 4.9GHz Band for US Operation,
  The proposed 4.9GHz band is allocated for nationwide public safety coverage in the US.
  Public safety applications require higher UE TX power than PC3. Support for HPUE (PC1, PC1.5, and PC2) is therefore important to the proposed 4.9GHz band.
The proposed 4.9GHz band overlaps with part of n79.
  PC1.5 and PC2 are defined for n79
  Simulation assumptions used for n79 can be reused for the proposed 4.9GHz band

## Slide 3: Proposal
Update the WI objective of NR TDD 4.9GHz Band for US Operation as follows:
  Specify the UE RF requirements for the new bands including HPUE (PC1, PC1.5 and PC2). Reuse NR band n79 UE hardware assumption if possible