## Slide 1: (e)Redcap enhancement in Rel-20
Sony, Nordic Semiconductor ASA, Anterix
3GPP TSG RAN Meeting #109
Beijing, China, September 15-18, 2025
RP‑252583
Agenda item:9.1.4.4

## Slide 2: Objectives for (e)Redcap enhancement in Rel-20
Background
Proposed objective
Further enhancement on (e)Redcap in Rel-20 has been discussed, and the following objective for Rel-20 has been endorsed in RAN#107[1]:
  (e)RedCap UE enhancement
    RLM/BFD relaxation based on the conclusions of R17 UE power saving WI
    Less than 5MHz for (e)RedCap, including both 1Rx and 2Rx, based on the conclusions of R18 LT5 WI
      This also include example bands, UE RF scope including potential complexity reduction, UE demod
Two areas in (e)Redcap enhancement has been endorsed, and in particularly, the complexity reduction will be considered in the UE RF scope.
In this contribution, we propose detailed objective on (e)RedCap UE enhancement in Rel-20 and also offer the key motivation of it
Based on the endorsed WF, the following objectives for Rel-20 (e)Redcap enhancement is proposed:
Specify 3Mhz CBW for TN and NTN (e)RedCap, including both 1Rx and 2Rx
  For RF complexity reduction, study and specify 3MHz only (e)RedCap for HD-FDD mode in Rel-20.
    Study feasibility to support 3MHz only (e)Redcap for both UL and DL directions or UL direction only.
  Work from less than 5MHz WIs in previous releases shall be reused as much as possible
  Taking band n106 as example band to start the work, target to support all frequency bands in FR1 in Rel-20
Specify relaxed RLM/BFD evaluation period requirements for (e)Redcap devices, including both 1Rx and 2Rx
  Relaxation criteria (i.e. good serving cell- and low mobility criteria) from Rel-17 relaxed RLM/BFD work for non-RedCap UEs shall be reused.
[1] RP-251879 Way forward on RAN4 R20 package RAN4 Chair (Apple)

## Slide 3: Why 3MHz only (e)Redcap devices?
For HD-FDD (e)Redcap devices, the SAW filter-less implementation is a very attractive design:
  Enable single SKU design by removing the band/regional specific SAW filters, cost reduction over streamlined production, reduced inventory costs.
  Reduce the complexity and footprint size, with improves the power efficiency of the RF front end.
  Achieves economies of scale through higher production volumes by enabling the (e)Redcap device towards low-end IoT applications,
SAW-less design has been widely adopted in 4G IoT devices, e.g., cat-M1/NB-IoT thanks to their smaller BWs (1.4MHz and 200 kHz).
Rel-17/18 (e)Redcap device needs to support UE CBW at least 5MHz, which is not possible to meet all RF requirement (e.g., emission limit) without SAW filters.
With 3MHz UE CBW, a UE can meet all the emission requirements without the need of SAW filter thanks to narrower spectrum shape.
a fully SAW-less implementation of HD-FDD (e)Redcap devices can therefore be realized if it only needs to support 3MHz UE CBW, especially in the UL direction.
HD-FDD (e)Redcap only need to support 3MHz UE CBW can be fully SAW-less, which enable a single SKU design for global operation
(e)Redcap with SAW-filters
SAWless (e)Redcap device