## Slide 1
Way Forward on LS on “Harmonised framework on aerial UE usage in MFCN harmonised bands”
RP-252704
TSG RAN#109
15-18 September 2025, Beijing, China
Source: Qualcomm
Agenda Item: 7

## Slide 2: Background
In 2024, SA and RAN received an LS from ETSI TFES regarding CEPT ECC requirements for the support of NTZs (No Transmit Zones).
This triggered a work task in the SA2 UAS study (Rel-19 SI UAS_Ph3) and technical discussion in RAN WGs (mostly RAN2).
SA2 proceeded to consider a series of technical solutions which involved the mobile network in receiving NTZ information and enforcing it.
After some discussion in RAN, following was concluded (RP-241658) and notified to SA2 (RP-241668 /S2-2407430) :
The RAN network should not be involved in the process of informing the UE on Non Transmit Zone(s)
The RAN network should not be involved in the process of enforcing UE behavior when it is located within the NTZ(s).
The UE is responsible of following any applicable the NTZ(s) regulations.
The RAN network should not receive the NTZ(s) information.
Any solution that breaks the above principles should be excluded from SA2 discussions.
As a result, SA2 concluded that UAV UEs are solely responsible for enforcement of the NTZ and will need to be properly (pre)configured prior to entering NTZ zones in order to be able to enforce such restrictions

## Slide 3: LS reply from CEPT ECC Plenary
3GPP (SA2 and CT1) has now received reply LS from CEPT ECC plenary in document S2-2506117 (ECC(25)023 ANNEX 07) which has raised the following concerns:
  “..The ECC noted the comments from ETSI TC MSG/TFES on mechanism ensuring that an aerial UE respects the no-transmit zones, in particular the information that “it was concluded that NTZ enforcement related impacts is limited to UAV UE only. No additional impacts are expected in RAN and CN.”
  The ECC perceives that an approach that consolidates this information into the Aerial UE would conflict with the confidentiality constraints of some national administrations in handling consolidated information on NTZ for S-band radars (2.7-2.9 GHz).
  One possible solution would be to manage the NTZ at the network level, and its functionalities, rather than in the aerial UE in future harmonised standards in order to support the use of the 2.6 GHz band throughout Europe.
  In consequence, CEPT invites ETSI for information on the roadmap for related aerial UE standardisation
  development. Europe should benefit from the harmonised standards developed in this framework.”

## Slide 4: Incoming SA2 LS & Action to RAN
From S2-2508014:
Rel-19 Stage 2 is frozen at Dec. 2024 and Stage 3 will be frozen at Sep. 2025, so SA2 does not consider any changes to take place on Rel-19 solutions.
Any potential future work identified by the issues raised by the CEPT ECC plenary in their LS, spanning across 3GPP system, needs a decision by RAN and SA plenaries.
Action (to RAN and SA):
SA2 kindly requests RAN and SA plenary to make a decision regarding the concerns and request to address the requirements raised by CEPT ECC plenary.

## Slide 5: Proposed Way forward
No additional RAN work is pursued for Rel-19 (frozen)
Potential RAN work can be considered for future releases, based on 3GPP member companies’ inputs / proposal(s) and TU budget
Send an LS to SA to inform of the RAN discussion’s outcome
  SA can discuss their impacts/aspects and provide a unified 3GPP reply to CEPT ECC Plenary