## Slide 1: 6G Data framework —motivation and work split
China Mobile, Mediatek

## Slide 2: Observation 1: Big New Value Opportunity for the Industry
Requirement from SA1( TR22.870 clause 5.9.2)
  New services like AI and sensing: 6G AI-native architecture and integrated communication-sensing services require massive heterogeneous data, demanding dedicated 6G data handling capabilities.
  Sensing data, AI data, energy efficiency data, positioning, and other network data, all of these require data handling mechanism including data collection, data distribution, data processing, data storage, and data exposure.
  Data will become a new important opportunity for operators, vendors, and terminals in the 6G era. How to efficiently manage and uniformly expose data has become a key aspect.
  6G data framework can effectively address the issue of data sharing across multiple domains (terminal, network, and application), facilitating multidimensional data fusion processing and exposure.
  Observation1：6G Data framework is a main drive opportunity for all the parties in the industry.
Notes: 对运营商、设备商的好处 终端厂家的好处
不够显著，benefit，
6G data 可能是6G的一个main drive opportunity for all the parties or industry

## Slide 3: Observation 2: Work in SA2 Require A Unified Architecture Design
Data collection and transmission: In SA2, the NWDAF has utilizes DCCF and ADRF for AI training data collection and storage. However, the interface between NWDAF and NF using SBI may not be suitable for large data transmission (e.g., UPF event exposure data per UE can be 1~5Mbps, while the SBI signalling is generally Kbps), therefore the data collection mechanism should be upgraded to support large AI training data collection.
R20 AIML KI#1: the discussion of how to retrieve UE side training data is under discussion, and the requirement for core network is the training data can be visible or controllable by core network.
Sensing data transmission and exposure: In SA2 5G-A R20 sensing architecture design, two typical requirements are to study Sensing Data and the Associated Information Collection and Transport (KI#4), and Sensing Result Exposure (KI#5).
Energy Efficiency: SA2 5G-A R19 the EIF is designed to calculate energy consumption information for specific traffic (per UE/PDU session/Traffic flow) based on finer granularity data volume, Node level data volume, and Node level energy consumption information(from OAM).
Observation 2: In 5G era, SA2 introduced multiple data handling mechanisms. In 6G, it is expected to define a unified data framework to simplify the network architecture design and more efficient to provide data as a service.
SA2 has related work in R18 and R19, which were based on different scenario, but lack of unified architecture design for data framework.
Notes: SA2 have related work in R18 and R19, but lack of unified architecture design,,需求从RAN时不时按场景来，但是缺统一架构设计。
RAN最新的LS关于模型传输的

## Slide 4: Observation 3: Big Gap on Data Framework
6G data framework should solve some gaps in 5G data design includes:
  1) Fragmented Data Processing Mechanisms: In 5G, data handling relies on service-specific solutions, increasing standardization complexity and hinders cross-service data reuse
  2)Centralized Processing Bottlenecks: 5G’s centralized data processing (e.g., NWDAF) causes bandwidth waste and latency issues when transmitting large volumes of raw data
  3) Inadequate UE/RAN Involvement: In 5G, UE and RAN data are mostly collected via "indirect channels" like OAM or DCAF, failing to meet the low-latency requirements of 6G real-time service
  4)Missing Cross-Working-Group (WG) Collaboration: requires coordination among SA2, SA3, SA5, and RAN
  Observation 3：6G data framework design should consider to solve the gaps between 6G requirement and 5G data handling.
Notes: 用 gap

## Slide 5: Observation 4: Data management work in SA5
Data management Ph2(R17&R19) | Study on Management data collection control and discovery, including producing and reporting management data, coordination management data production, storing management data, managing external management data, discovery of management data | TS 28.537
Other related items (Until R19) | Performance measurements and key performance indicators (KPIs) | TS 28.552/554
 | UE level measurements (aggregated for the UEs to a measured object (e.g., a cell), extended the Trace mechanisms in 5GC, MDT mechanisms in NG-RAN) | TS 28.558
 | Management Data Analytics (MDA) | TS 28.104
 | Trace metrics, including trace messages, MDT measurements and RRC reports | TS 32.423
 | QoE measurements collection(collection of QoE information from UEs via the management system to the traffic network.) | TS28.404/5/6
For R20 :
Study for Data management phase 3:
  WT1: Study solutions for request and report of external management data.
  WT2: Investigate reporting format of management data regarding
  WT3: Study enhancements of UE data collection in 5G advanced (with or without AI/ ML adoption) to address future RAN decisions on this topic.
  WT4: Study ways to clarify interaction or relation of specified mechanisms to discover, request and retrieve management data considering 3GPP internal and external data sources.
Study on Service Based Management Architecture enhancement phase 4: contains “WT-1: Streaming of management data based on message bus” which will investigate introduction of a message bus for mgmt. data.
Observation 4: SA5 started the handling of management data aspect from R17

## Slide 6: Observation 5: SA2 and SA5 Work Differently
Observation 5: SA2 and SA5 works on different types of data, different operation and processing purposes.
 | SA2 | SA5
TOR (Terms of Reference) | SP-210266 Architecture model and concepts: data storage; End-to-end Procedures: Data collection and storage | SP-241885 Data collection for Management, Orchestration and Charging. Examples of data being collected: alarms, performance measurements, KPIs, QoE, trace, MDT data and charging information.
Data type | AI model/training data; sensing data; Energy related data; other dynamic policy/configuration information | Management data, including configuration/performance data, NF status data/information, KPIs, Network level EE related data
Purpose | Service Data Control: Efficient service data transmission; service data storage and processing; service data exposure based on AF/UE requirement. | Management data control: Management data/historical management data discovery, collection, store and reporting.
Data source | UE, RAN, CN(e.g., UPF and other CP NFs) | RAN, CN; UE level measurements
Handling feature | Collection, transmission, Store, processing, exposure etc; | Collection, storage, processing, reporting, discovery, etc;
 | Consumer: AF, UE or RAN | Consumer: NWDAF, RAN, operator management system or AF
Comparison between SA2 and SA5
Notes: NF变CN

## Slide 7: Observation from Another Angle

## Slide 8: Proposed Way forward
It is proposed to discuss the paper. Maybe Update the table in Page 6 &7. Try to reach a common understanding and send LS to SA2, SA5 and RAN.
Way forward:
SA2 defines overall data framework, improving user experience and supporting new services;
SA5 focus on management data aspect.
Data collection (UE->RAN) is in the remit of RAN WGs