## Slide 1
Way forward for WT 1.3
Source: Qualcomm
S2-259181

## Slide 2: State of the art
3GPP has been working on integrating Non-3GPP access in 3GPP CN since Rel. 7 (ca. 2002)​
Non-3GPP access: Wi-Fi, fixed line broadband​, cdma2000, WiMax
An array of technologies has been developed throughout the years operating at almost every conceivable “protocol layer”​
Solutions have spanned from minimal integration between 3GPP and non-3GPP to deep integration at RAN level (e.g., RAN assisted WLAN interworking and LTE WLAN Aggregation – LWA, in Rel-13)​
Why has this work been done in 3GPP? The main goals for operators were: ​
Extend support of 3GPP services over certain specific non-3GPP accesses with service continuity ​
   Unsuccessful because MNOs main service they want to extend over WiFi is voice/SMS ​
Support aggregation between cellular and fixed accesses​
   Partly deployed using proprietary aggregation solutions​
Extend coverage for the provided services indoor​
   VoWiFi is a big success story​ since it allows the MNO to “extend” the coverage of the service it provides indoor
TSG SA WG2 Meeting #171
13-17 October 2025, Wuhan, China
S2-259181

## Slide 3: Some realities
Use cases apply to certain device-access technology combination:
  Fixed Residential Gateways (RGs) are not moving, so no need for service continuity
  Smartphones may be moving in and out of WiFi, i.e., service continuity is needed
WiFi vs. cellular connection selection largely in hands of OS vendors and not in 3GPP layers
Generic “internet access” is already “offloaded” to WiFi since mainstream OS by default prefer WiFi vs. cellular
Service continuity has value only for specific services (e.g. voice over WiFi, OTT voice) and for the majority of internet services is not perceived by the user
Software stack in smartphone vs. RG is different
TSG SA WG2 Meeting #171
13-17 October 2025, Wuhan, China
S2-259181

## Slide 4: Lessons learned from 5G
VoWiFi is up to date the most successful scenario for integration
Aggregation for Residential Gateways (RGs)
Possible commercial sense as transition scenario, e.g., areas where only DSL is available in EU
Will it be valid in 5-10 years? It may be taken over by “full FWA” or “full fibre”
Data aggregation for smartphones:
No real use cases identified, and…yes, the industry has tried hard to find them
“One solution fits all” approach (aka N3IWF/TNGF) was not a commercial success
TSG SA WG2 Meeting #171
13-17 October 2025, Wuhan, China
S2-259181

## Slide 5: Existing and possibly promising use cases for 6G (view from the authors)
Existing:
VoWiFi
Integration and aggregation for Residential Gateways (RGs)
  Possible commercial sense as transition scenario, e.g., to offer cellular plus DSL in areas where only DSL is available in EU.
  Will it still be a valid use case in 5-10 years? It may be taken over by FWA (i.e. 6G only) or fibre.
Promising
3) IP Continuity for selected services
  OTT VoIP service, e.g., MS Teams, Webex, etc. is likely the most popular real-time, mobile service where mobility related impairments are regularly experienced.
TSG SA WG2 Meeting #171
13-17 October 2025, Wuhan, China
S2-259181

## Slide 6: Way forward for FS_6G_ARC WT#1.3
For 6G, a “generic” non-3GPP interworking architecture that fulfils all use cases should not be the pre-conceived assumption.
Instead, 3GPP SA2 should focus on developing key issues and tailored solutions that satisfy specific MNO use cases
SA2 should not focus on abstract requirements but actual operators’ needs
MNOs should provide use cases they want to be fulfilled in this context and believe have or will have market traction
Proposal: Adopt a pragmatic solution that avoids the drawbacks of 5G solutions while enabling the realistic use cases.
Text proposal in S2-2508754
TSG SA WG2 Meeting #171
13-17 October 2025, Wuhan, China
S2-259181

## Slide 7
Thank you