SA WG2 Meeting #162	S2-2404259

April 15 – 19, 2024, Changsha, China

Source:	Ericsson

Title:	Interim conclusions for KI#1

Document for:	Approval

Agenda Item:	19.1

Work Item / Release:	FS_5GSAT_Ph3_ARCH / Rel-19

Abstract of the contribution: This contribution proposes an evaluation and interim conclusions for KI#1.

# 1. 	Discussion

Void

# 2. 	Summary of findings / Way forward

Void

# 3. 	Proposal

It is proposed to update TR 23.700-29 as follows:

**** First Change ****

# 8	Conclusions

Editor's note:	This clause will list conclusions that have been agreed during the course of the study item activities.

### 8.2.X 	Interim conclusions for KI#1

The conclusion for supporting gNB/eNB on-board the satellite is based on the following principles:

- 	A procedure to disconnect/ suspend the N2 and S1 interfaces when the gNB/eNB leaves an area served by an AMF/MME (e.g. when setting over the horizon) should be supported. Whether existing procedure(s) can be re-used or new procedure(s) is needed is to be determined by RAN3.

- 	gNB/eNB IP address change due to feeder link switch can be supported using existing N2 and S1 procedures. There are no normative impacts to SA2 specifications due to this.

- 	The AMF/MME can treat the Mapped Cell ID as per rel-17, e.g. the AMF/MME can provide a Mapped Cell ID to a gNB/eNB independent of the gNB/eNB ID in the Mapped Cell ID. There are no normative impacts to SA2 specifications due to this.

The above interim conclusions need to be discussed and verified by RAN3.

**** End of Changes ****