## Slide 1: Interim Conclusions for KI#1 and #2
CATT, China Mobile,

## Slide 2: Overview for KI#1
Sub Key Issues | Solutions for each sub-KI
KI#1-1: N2/S1 connections management | #1, #2, #3, #4, #9, #10
KI#1-2: Enhanced TA/Cell management considering the change of supported TA list for a RAN node on-board | #2, #4
KI#1-3: Handling feeder link switch with AMF/MME change | #5, #6, #35
KI#1-4: User Plane Management considering RAN node mobility | #7, #35, #36
KI#1-5: PCC/QoS control enhancement considering Regenerative-based satellite access | #8
KI#1-6: AMF discovery | #34

## Slide 3: Interim conclusion for KI#1-1
Solution groups for KI#1-1 | Solution#
G1: N2/S1 connection setup/disconnect | #1
G2: N2/S1 connection suspend/resume | #2, #3, #4
G3: Proxy/agent for managing N2/S1 connection | #9, #10
Proposal:
  Opt1: NG/S1 connection shall be suspend if the gNB/eNB moves out of current AMF/MME service area, and resumed if the gNB/eNB moves into the service area again.
  Opt2: NG/S1 connection shall be removed if the gNB/eNB moves out of current AMF/MME service area, and re-established if the gNB/eNB moves into the service area again.
  NOTE: RAN3 makes final decision on which option will be adopted.

## Slide 4: Interim conclusion for KI#1-2
Solution groups for KI#1-2 | Solution#
G1: TA "timetable“ is calculated per RAN node by AMF/MME based on satellite ephemeris | #2
G2: TA "timetable“ is provided to AMF/MME per RAN node ID | #4
G3: Proxy/agent for managing N2/S1 connection | #9, #10
Proposal:
  The RAN node and AMF/MME can be configured by O&M with the TAI timetable per RAN node ID.
  The Mapped Cell IDs are independent of the gNB/eNB that generated them, i.e. the AMF/MME can provide a Mapped Cell ID to a gNB/eNB regardless of the gNB/eNB ID in the Mapped Cell ID.
  NOTE: RAN3 confirmation is needed.

## Slide 5: Interim conclusion for KI#1-3
Solution groups for KI#1-3 | Solution#
G1: new TAU/TAU trigger due to feed link switchover | #5, #6
G2: two (logical) gNBs/eNBs connecting to both old and new CN nodes simultaneously | #35
G3: Configure different TAI for different AMF/MME for same area | #35
Proposal:
  No new issue identified, and then no normative work.
The scenario addressed by the solution#5&6 is that, a TA area can be served by two AMF/MME but the RAN serving this area can only connect to one of the AMF/MME.
This scenarios is questionable, if the area belongs to both AMF/MME service areas, then the RAN node shall establish NG/S1 connections toward both AMF/MME simultaneously even via same feeder link, then the RAN node shall route the UE signalling toward the AMF/MME which is serving the UE, which mean no TAU is needed

## Slide 6: Interim conclusion for KI#1-4
Solution groups for KI#1-4 | Sol#
G1: explicit indication from RAN to AMF and finally to SMF regarding feeder link change, then the UPF buffers DL data | #7
G2: ANF detects gNB TNL IP address change and notify the SMF, so that the SMF can instruct the UPF to update the DL tunnel | #35
G3: AMF notifies the SMF of the gNB leaving its service area, so that SMF can treat GTP-U error notifications correctly | #36
Proposal:
  G2 is preferred, i.e., the AMF notify the SMF to update the DL N3 tunnel using existing procedure.
NOTE: As analyzed in KI#1-3, if UE served by the RAN node can still be served by old AMF/SMF, It is not clear why the RAN node can not maintain the old TNL association via new feeder link during the feeder link change

## Slide 7: Interim conclusion for KI#1-5 & 6
KI#1-5:
Solution#8 is the only solution, which introduces two new RAT type since regenerative-based satellite access has different Uu delay from transparent mode satellite access
Proposal:
  New RAT types need to be introduced for regenerative payload NGSO satellite access.
KI#1-6:
Solution#34 is the only solution
Proposal:
  AMF discovery is based on the configurations on the gNB.

## Slide 8: Overview
Architecture options for KI#2 | A-Single Satellite | B-Multiple Satellite
G1: eNB onboard only | #20 | #X(HW)
G2a: eNB + partial MME onboard (NF different NAS security on the ground) | #14 | #11
G2b: eNB + partial MME onboard (+ MME on Ground) same as G4 for SMS and CP # different NFs on board than G2a (NAS security on board satellite) | #13 | #12
G3: eNB + whole MME onboard | #13, #22 | #12
G4: eNB + partial C-SGN onboard – same as G2b for SMS and CP (+ do not prevent support of UP) | - | #15
G5: eNB + whole C-SGN onboard | #16 | -
G6: eNB + C-SGN with new function (SFCF) | #17 | -
G7: eNB + whole MME + HSS onboard | #18 | #Y(OPPO)
G8: eNB + whole CN + EndPoint Proxy onboard | #19 | #Z(HW/QC)

## Slide 9: Evaluation Criteria
It is proposed to discuss evaluation criteria first, the criteria shall be defined based on capability, performance and feasibility
Following initial criteria are proposed:
  C1: Support of SMS service, CIoT small data transmission (CP) at least
  C2: Delay for the UE to obtain network services, e.g., sending the first UL data packet (comment: multiple vs single)
  C3: Compute and storage requirements on satellite considering limitation of satellite payload, which can be estimated based on NFs deployed on the satellite.
  C4: Support of roaming
  C5: 3GPP procedures which would require change or new definition
  C6: proprietary NFs needed to support SSF
  C7: Not preventing support of legacy UEs

## Slide 10: Way forward for KI#2
Architectures only supporting single satellite have too much delay to obtain network services, and then shall not be considered for further work.
Sending LS to SA3 to check whether the architecture with eNB onboard can prevent security issue, e.g. FBS and DDoS
Sending LS to SA3 to check whether the architecture with HSS onboard can support roaming

## Slide 11: ANNEX

## Slide 12: KI#2: Support of Store and Forward Satellite operation

## Slide 13: Solution Evaluation
Architecture options | Further Classification | Sol # | C1 | C2 | C3
G1: eNB only onboard | G1-1: Single-sat | #20 | SMS, CIoT | 3 times of satellite orbiting before sending the first UL packet: 24*3 = 72 hours* *24 hours for same satellite to serve the UE again at worst case | eNB is required to S&F UL/DL data
 | G1-2: Multi-sat | #X(HW) | SMS, CIoT | 3 times of satellite orbiting: 1.5*3 = 4.5 hours* *when multi-satellites are involved, each time of signalling S&F requires approximately 1.5 -2hours | eNB is required to S&F UL/DL data and calculate serving eNB list
G2: eNB + partial MME onboard | G2-1: Single-sat | #14 | SMS, CIoT | 1 time, 24 hours | MME-SAT processes attach request
 | G2-2: Multi-sat | #11 | SMS, CIoT | 3 times, 4.5 hours | MME-SAT doesn’t process attach procedure
G3: eNB + whole MME onboard | G3-1: Single-sat | #13, #22 | SMS, CIoT | 1 time, 24 hours | MME on board processes attach procedure
 | G3-2: Multi-sat | #12 | SMS, CIoT | 1 time, 1.5 hours | MME on board processes attach procedure with the help of anchor MME on the ground
G4: eNB + partial C-SGN onboard | Multi-sat | #15 | SMS, CIoT | 2 times, 3 hours | partial C-SGN on-board process attach request with the help of C-SGN on the ground
G5: eNB + whole C-SGN onboard | Single-sat | #16 | SMS, CIoT | 2 times, 48 hours | C-SGN on-board processes attach request
G6: eNB + C-SGN with new function onboard | Single-sat | #17 | SMS, CIoT | immediately, 24hours at most to receive DL signalling/data | C-SGN on-board processes attach request A new SFCF is introduced to manage UE subscription
G7: eNB + whole MME + HSS onboard | Single-sat? | #18 | SMS, CIoT | immediately, 24hours at most to receive DL signalling/data | MME and HSS are deployed on the satellite.
G8: eNB + whole CN + Proxy onboard | Single-sat?? | #19 | SMS, CIoT, IMS? … | immediately, | Whole CN and a new application layer end point proxy are deployed on the satellite.

## Slide 14: Evaluation
For C4:
  Architecture G1-G5 can support roaming as HSS is on the ground
  Architecture G6-G8 can also support roaming if the HSS on board can store UE credential per PLMN:
Further analysis to the evaluation results:
  Architecture options G1-2, G2-2, G3-2, G4, G6, G7 and G8 have rational delay to obtain network services;
  The nature of G2-2, G3-2 and G4 are same, i.e. MME functionalities are deployed on the satellite and ground;
  G1-2 would be vulnerable to DDoS attack, further evaluation in SA3 is needed.
  G6 and G8 introduce new function on board and then have much more system impact and satellite resource consumption

## Slide 15: Interim conclusions for KI#2
Architecture with the split of MME function into satellite part and ground part is considered to support S&F, including:
  SA3 is responsible for further study on preventing DDoS attack to satellite and other security issues
Architecture with both MME and HSS onboard is also considered to support S&F, further work include:
  To allow the UE to send/receive application layer response/confirmation in time, the UE shall be able to attach to multiple satellites to send/receive DL data.
  The HSS onboard shall only store necessary material for completing UE attach.
  The HSS shall store necessary material for support roaming.
  To support the S&F traffic transmission through User Plane, the S-GW/P-GW can be also onboard. Then the Architecture option can also be applied to 5GC deployment (i.e. AMF, SMF, UPF,UDM onboard).