## Slide 1: Discussion on new NF vs existing NF to handle the energy related functionalities
China Mobile

## Slide 2: New Functionalities
Collection and exposure at different granularities of energy related information (NF, network slice, UE, UE+service, PDU Session, QoS flow)
Collection and exposure of renewable energy
Energy related information calculation
Energy related information analysing
Energy related policy control
Energy related network adjustment

## Slide 3: Comparison
 | New NF | NWDAF | SMF
Existing functionality | - | analysing based on AI | session control
New functionalities | all energy related functionalities: collection, calculation, policy control, exposure | all energy related functionalities: collection, calculation, policy control, exposure | energy related information collections
Granularity | NF, network slice, UE, UE+service, PDU Session, QoS flow | NF, network slice, UE, service | PDU Session, QoS flow
Interface | interface with NFs and OAM | reuse existing interface with NFs and OAM | reuse existing interface with UPFs and OAM
Parameters | reuse existing EE info from OAM on network slice and NF level; renewable info from OAM; EE related info from NFs on finer level | reuse existing EE info from OAM on network slice and NF level; renewable info from OAM; EE related info from NFs on finer level | reuse existing EE info from OAM on network slice and NF level; EE related info from NFs on finer level

## Slide 4: Analysis and proposal
New NF should support all energy related functionalities (described above) as well as Energy Consumption Credit Control, and it concentrates on energy related capabilities, NWDAF is lack of such control;
New NF such as EECF (name can be updated) is self-contained; better for forward compatibility easy for evolution and enhancement;
Energy related functionalities are not bond to NWDAF, since NWDAF is designed for data analysing, and analysing is optional for energy related functionalities.
It is suggest to avoid the Giant NF design to cause the bottleneck problem. NWDAF will be too heavy with all these functionalities together;
SMF is for session control, and should not be used to handle the energy related processing.
Proposal: It’s suggested to introduce a new NF to handle the energy related functionalities, and this new NF can be co-located with the other NFs if needed.

## Slide 5: Thank you!

## Slide 6: Annex: statistic on existing solutions
Solution | KI#2 | KI#3 | Decision made by
#7 | x |  | EECF
#8 | x |  | EECF
#9 | x |  | PCF
#10 | x |  | EECF
#21 | x |  | EENF/NWDAF
#22 | x |  | EECF
#23 | x |  | EECF
#24 | x |  | RAN
#25 | x |  | EECF/NWDAF
#26 | x |  | EECF+NWDAF
#27 | x |  | EECF/NWDAF
#28 | x |  | SMF
#31 | x |  | AF
#11 | x | x | NWDAF
#15 | x | x | NWDAF+(O)NEMF
#12 |  | x | NWDAF
#13 |  | x | EECF
#14 |  | x | PCF
#29 |  | x | NRF
#30 |  | x | EECF/NWDAF/ECNF
#32 |  | x | EECF+NWDAF
Solution | Energy related information collected by
#1 | EECF
#2 | EESSF
#3 | NWDAF
#4 | NWDAF
#5 | NWDAF
#6 | EEF
#16 | EBF
#17 | EECF or SMF+NWDAF
#18 | ECF
#19 | SMF
#20 | SMF
new NF: 13
NWDAF: 6
either: 5
other: 8