3GPP TSG-SA WG2 Meeting #162	S2-240xxxx

Changsha, China, April 15 – 19, 2024

Source:	CATT

Title:	KI#2 new solution of policy control for multiple accesses based on network energy related information

Document for:	Approval

Agenda Item:	19.4

Work Item / Release:	FS_EnergySys / Rel-19

Abstract of the contribution: The contribution proposes a new solution of policy control for multiple accesses based on network energy related information for KI#2.

1. Introduction

The UE can register to the network over multiple access networks (e.g. both 3GPP access and non-3GPP access) and transmit data simultaneously or non-simultaneously over different accesses, either via different PDU Sessions or the same PDU Session (i.e. MA PDU Session). This offers both the UE and network more flexibility and higher capacity for data transmission, improving service experience. However, it may require more energy consumption in the network and the UE.

Therefore policies in the network and for the UE need to be carefully designed in the scenario of multiple accesses, when energy efficiency and energy saving are used as service criteria.

It is proposed that the PCF takes into account network energy related information when making policy decisions for control of multiple accesses.

2. Proposal

It is proposed to agree the following changes to 3GPP TR 23.700-66.

* * * Start of Change * * * *

## 6.x	Solution #X: Policy control for multiple accesses based on network energy related information

### 6.x.1	Key Issue mapping

This solution addresses Key Issue #2 "Subscription and policy control to support energy efficiency and energy saving as service criteria".

### 6.x.2	Functional Description

The UE can register to the network over multiple access networks (e.g. 3GPP access, non-3GPP access, different RATs of 3GPP access) and transmit data simultaneously or non-simultaneously over different accesses, either via different PDU Sessions or the same PDU Session (i.e. MA PDU Session). This offers both the UE and network more flexibility and higher capacity for data transmission, improving service experience. However, it may require more energy consumption in the network and the UE.

Therefore policies in the network and for the UE need to be carefully designed in the scenario of multiple accesses, when energy efficiency and energy saving are used as service criteria.

It is proposed that the PCF takes into account network energy related information when making policy decisions for control of multiple accesses, which may include the following existing policies:

-	access and mobility related policy, e.g. RFSP Index.

-	Access Type preference in the URSP rule.

-	MA PDU Session Control information in the PCC rule.

Based on operator policy, when the energy consumption over 3GPP access in 5GS in 1) a PLMN, 2) a network slice or 3) for specific application(s) in a PLMN or a network slice reaches or is higher than a threshold, or when the energy efficiency over 3GPP access in 1) a PLMN, 2) a network slice or 3) for specific application(s) in a PLMN or a network slice reaches or is lower than a threshold, the PCF may decide to:

-	modify the Access Type preference in the URSP rules to offload some traffic from 3GPP access to non-3GPP access, e.g. changing the Access Type preference from "3GPP" to "non-3GPP" or "Multi-Access" for specific application(s) as specified in TS 23.503 [4]; and/or

-	modify the MA PDU Session Control information in the PCC rule, e.g. lower the percentage of SDF traffic sent over 3GPP access using Load-Balancing steering mode or prioritizing non-3GPP access over 3GPP access using Priority-based steering mode for specific application(s) as specified in TS 23.501 [2] and TS 23.503 [4].

Based on operator policy, when the energy consumption over 5G access in 1) a PLMN, 2) a network slice or 3) for specific application(s) in a PLMN or a network slice reaches or is higher than a threshold, or when the energy efficiency over 5G access in 1) a PLMN, 2) a network slice or 3) for specific application(s) in a PLMN or a network slice reaches or is lower than a threshold, the PCF may decide to modify the RFSP Index, e.g. prioritizing EPC/E-UTRAN access over 5G access for specific UEs with optionally a RFSP Index in Use Validity Time as specified in TS 23.503 [4].

NOTE 1:	Energy related information, as a new criteria/factor for policy decision making, is different from load level information. For example, when the load level of a network slice or the traffic volume of specific application(s) in a PLMN or a network slice is still acceptable, but the energy consumption of the network slice or specific application(s) is higher than expected, the above policy control can be applied.

NOTE 2:	Energy saving for other accesses (e.g. EPC/E-UTRAN) than 5G access is not in the scope of this TR.Also, the PCF may provide the following policy for a UE or a MA PDU session to the SMF based on OAM configuration, network energy related information, UE subscription data, and/or information provisioned by the AF, etc:

-	energy consumption and/or energy efficiency threshold per Access Type or RAT Type (e.g. 3GPP access, 5G access, NR, NR satellite access) in 5GS.

-	temporal and/or spatial validity conditions.

Editor's note:	It is FFS whether energy saving for NR satellite access is considered, which may depend on e.g. whether the solar energy is sufficient for the satellite providing NR satellite access.

NOTE 3:	This solution focuses on Energy saving over 3GPP access. Energy saving and measurement for non-3GPP access (e.g. traffic offloading from non-3GPP access to 3GPP access considering the energy consumption over non-3GPP access) is not supported.

Based on the policy and network energy related information, when the energy consumption (/energy efficiency) of the network for the UE or the MA PDU Session reaches or is higher (/lower) than the energy consumption (/energy efficiency) threshold over a specific Access Type or RAT Type, the SMF may reject the PDU Session establishment or user plane activation request, or initiates the PDU Session modification or user plane deactivation over this access or RAT to the UE and/or for the MA PDU Session, to limit or reduce the data traffic transmitted over this access or RAT under validated conditions (i.e. in the validity time window and/or area).

To support policy decisions/enforcements as described above, the following network energy related information needs to be obtained:

-	energy consumption, energy efficiency and/or other energy related information (e.g. data volume, resource usage) over specific access type(s) or RAT Type(s) (e.g. 3GPP access, 5G access, NR, NR satellite access) in 5GS in 1) a PLMN, 2) a network slice or 3) for specific application(s) in a PLMN or a network slice.

-	energy consumption, energy efficiency and/or other energy related information (e.g. data volume, resource usage) over specific access type(s) or RAT Type(s) for a UE or a MA PDU Session.

NOTE 4:	The information can be collected for a specific area (i.e. Area of Interest) and/or specific time window.

Editor's note:	Whether the energy related information over specific access type(s) or RAT Type(s) for a UE or a MA PDU Session can be obtained and provided by the RAN is FFS, and coordination with RAN WGs is needed.

The network energy related information can be obtained by the PCF and the SMF from the NWDAF (via network data analytics, i.e. statistics or prediction of the network energy related information) or other 5GC NF(s), e.g. the EMF (Energy Management Function) as a new 5GC NF introduced for network energy management.

NOTE 5:	Measurement/calculation of energy consumption and energy efficiency by OAM is defined in TS 28.310 [7].

### 6.x.3	Procedures

Figure 6.x.3-1: Policy control based on network energy related information procedure

1.	The PCF obtains network energy related information from the NWDAF (via network data analytics) or the EMF.

The network energy related information is described in clause 6.x.2.

NOTE 1:	How the NWDAF provides analytics of network energy related information is described in Solution #12. In addition, the access type and/or RAT type associated with other input data are collected, and analytics of the network energy related information as described in clause 6.x.2 are outputted by the NWDAF.

NOTE 2:	The PCF can obtain the network energy related information before or after receiving the AM/SM/UE policy association request.

2.	Based on OAM configuration, the network energy related information obtained in step 1, UE subscription data, and/or information provisioned by the AF, etc., the PCF makes policy decisions taking into account of energy consumption (/energy efficiency) over specific access(es) / RAT type(s) as described in clause 6.x.2.

3.	The PCF provisions or updates the policies, which can be the existing policies or new policy (i.e. energy consumption / energy efficiency threshold per access or RAT type, validity conditions) as described in clause 6.x.2, to the AMF, SMF and UE  as specified in TS 23.502 [3].

4.	The AMF, SMF and UE enforces the policies received from the PCF as described in TS 23.502 [3] and clause 6.x.2.

### 6.x.4	Impacts on existing services, entities and interfaces

PCF:

-	Obtains network energy related information from the NWDAF or EMF, and makes policy decisions taking into account of energy consumption (/energy efficiency) over specific access(es) / RAT type(s) as described in clause 6.x.2.

SMF:

-	Enforces new policy (i.e. energy consumption / energy efficiency threshold per access or RAT type, validity conditions) as described in clause 6.x.2.

NWDAF:

-	Provides analytics of network energy related information.

EMF:

-	Provides network energy related information as described in clause 6.x.2.

* * * End of Change * * * *

# Comments

@Alessio:

TS 23.503 clause 6.1.2.1 “The management of the RFSP Index enables the PCF to modify the RFSP Index used by the AMF to perform radio resource management functionality as described in clause 5.3.4 of TS 23.501 [2]. …”

clause 5.3.4 of TS 23.501:“To support radio resource management in NG-RAN the AMF provides the parameter 'Index to RAT/Frequency Selection Priority' (RFSP Index) to NG-RAN across N2. The RFSP Index is mapped by the RAN to locally defined configuration in order to apply specific RRM strategies, taking into account any available information in RAN.”

@Alessio: 5G access can offer even better service experience than WiFi. So it is viable to use URSP to instruct the UE to use 5G even when WiFi is available.

@Bahador: Here I further clarify the granularities of EC, which are in scope of SA1.

To address these granularities by adjusting EC per access, I think it is architectural requirement in scope of SA2 instead of SA1.

@DongYeon: This can be updated after the MA PDU Session is established, see TS 23.501 clause 5.32.3 “The ATSSS rules are sent to UE with a NAS message when the MA PDU Session is created or updated by the SMF, e.g. after receiving updated/new PCC rules from the PCF.”

@Bahador: This is added to clarify the difference from load control.

@Marco: This is added to limit the scope.

@Marco: added also to clarify the scope.

@Marco: addressing the NR satellite access

Added to address Bahador’s comment

Added to address Bahador’s comment