3GPP TSG-SA WG2 Meeting #162	S2-2403935r01

Changsha, China, April 15 – 19, 2024

Source:	CATT, vivo?, ZTE?, MediaTek Inc.?, DISH Network?

Title:	Conclusions for KI#2

Document for:	Approval

Agenda Item:	19.4

Work Item / Release:	FS_EnergySys / Rel-19

Abstract of the contribution: The contribution proposes conclusions for KI#2 "Subscription and policy control to support energy efficiency and energy saving as service criteria".

1. Introduction

Conclusions on KI#2 "Subscription and policy control to support energy efficiency and energy saving as service criteria" are proposed in this contribution based on the evaluations of existing solutions on KI#2. Further updates to the conclusions are to be done to accommodate possible new solutions, solution updates and further discussions.

2. Proposal

It is proposed to agree the following changes to 3GPP TR 23.700-66.

* * * Start of Change * * * *

## 8.x	Key Issue #2: Subscription and policy control to support energy efficiency and energy saving as service criteria

For KI#2, the following enhancements on subscription and policy control are agreed for normative work to support energy efficiency and energy saving as service criteria in the 5GS:

1)	Enhancements on UE subscription information

-	The following energy related subscription data are supported:

-	Energy credit (e.g., energy consumption, Renewable energy ratio, Carbon emission information) per UE, network slice, DNN, application ID.

-	Validity conditions (i.e. validity time and/or area) for the energy credit.

-	Energy saving authorization information (e.g. Green Subscription Indication in Access and Mobility Subscription information) per UE, depending on operator policy.

Editor's note:	Other information in the energy credit is FFS.

-	The following existing subscription data are enhanced with associated validity conditions (i.e. validity time and/or area):

-	Configured NSSAI, Allowed NSSAI, Subscribed UE-AMBR, Subscribed QoS profile, Subscribed-Session-AMBR, ATSSS information.

-	The AF may provide service specific energy related subscription data, i.e. energy credit with optional validity conditions as described above.

-	The energy related subscription data is stored in UDM/UDR.

Editor's note:	Whether the energy credit is store in the UDM or CHF is FFS.

-	Change of the Green subscription (e.g., preference indication from a UE, deactivate request the green subscription from UE) by a UE is out of scope of this release.

2)	Enhancements on policies control

-	The PCF may take into account energy related information (energy credit in subscription data, energy related information received from the EECF, Energy related analysis from NWDAF, etc.) when making policy decisions, including the following existing policies/policy parameters and procedures:

-	AM policy, e.g. UE-AMBR, UE-Slice-MBR, allowed TAIs, RFSP Index.

-	SM policy, e.g. Session-AMBR, default 5QI/ARP, QoS profile, QoS parameters (e.g. PDB, PER).

-	URSP, e.g. S-NSSAI, Access Type preference.

-	the list of DNAI(s) in PCC rule for traffic routing.

-	MA PDU Session Control information in the PCC rule.

-	selecting and negotiating data transfer policy with the AF.

-	configuring PCRTs based on energy related information.

-	Validity conditions (i.e. validity time and/or area) can be provided along with the above policies (if not supported yet) by the PCF based on energy related information.

-	The AF may take into account energy related information when selecting and negotiating data transfer policy with the PCF.

-	The AF may indicate adaptability/flexibility in terms of QoS level and transfer time during AF session setup with required QoS.

3)	What network energy related information is required for subscription and policy control and how it is obtained.

-	The following network energy related information needs to be obtained for subscription and policy control:

-	energy consumption;

-	energy efficiency;

-	ratio of renewable energy

-	carbon emission information.

-	energy consumption related information, e.g. data volume, bit rate, NF load level.

-	The following granularities can be supported for the above network energy related information depending on the use cases:

-	per UE;

-	per 5GC NF;

-	per NG-RAN node;

-	per network slice, DNN, or combination of S-NSSAI and DNN;

-	per application ID.

-	The network energy related information can be collected from the OAM, 5GC NF, NG-RAN, NWDAF (i.e. Energy related analysis) or EECF depending on the use cases.

Editor's note:	Coordination with SA WG5 and RAN WGs is required for the collection of network energy related information. Whether NG-RAN can obtain per UE network energy consumption information and provide it to the 5GC is FFS.

Editor's note:	Whether CHF is enhanced to control energy credit limit of subscribers and notifies PCF (for possible policy adjustment) depends on the decision of SA WG5.

* * * End of Change * * * *