3GPP TSG-SA WG2 Meeting #162	S2-2405145

Changsha, China, April 15 – 19, 2024

Source:	CATT, vivo?, ZTE?, MediaTek Inc.?, DISH Network?

Title:	Conclusions for KI#2

Document for:	Approval

Agenda Item:	19.4

Work Item / Release:	FS_EnergySys / Rel-19

Abstract of the contribution: The contribution proposes conclusions for KI#2 "Subscription and policy control to support energy efficiency and energy saving as service criteria".

1. Introduction

Conclusions on KI#2 "Subscription and policy control to support energy efficiency and energy saving as service criteria" are proposed in this contribution based on the evaluations of existing solutions on KI#2. Further updates to the conclusions are to be done to accommodate possible new solutions, solution updates and further discussions.

2. Proposal

It is proposed to agree the following changes to 3GPP TR 23.700-66.

* * * Start of Change * * * *

## 8.x	Key Issue #2: Subscription and policy control to support energy efficiency and energy saving as service criteria

For KI#2, the following enhancements on subscription and policy control are agreed for normative work to support energy efficiency and energy saving as service criteria in the 5GS:

1)	Enhancements on UE subscription information

Editor's note:	It is FFS whether and what energy credit (e.g., energy consumption) per UE is to defined and used, which depends on whether and what energy related information per UE can be obtained as concluded in KI#1.

-	The following energy related subscription data are supported:

-	Energy credit (e.g., energy consumption) per UE, or per network slice, DNN and/or application ID per UE, optionally with validity conditions (i.e. validity time and/or area).

-	Energy saving authorization information (e.g. Green Subscription Indication in Access and Mobility Subscription information) per UE, depending on operator policy.

-	The energy related subscription data is stored in UDM/UDR.

2)	Enhancements on policies control

-	The PCF may take into account energy related information when making policy decisions on the AM, SM and UE policies. Validity conditions (i.e. validity time and/or area) may be provided along with the policies (if not supported yet) based on energy related information.

Editor's note:	It is FFS what parameters in the AM, SM and UE policies can be determined and updated based on energy related information.

-	The energy related information that the PCF may take into account for policy control includes:

-	energy consumption per network slice or per 5GC NF as defined in TS 28.554 [6];

-	energy efficiency per network slice as defined in TS 28.554 [6];

-	energy related analytics provided by NWDAF (concluded in KI#3)

-	The AF and PCF may take energy related information into account for selecting and negotiating data transfer policies in terms of transfer time and/or QoS aspects.

Editor's note:	Whether the ratio of renewable energy and carbon emission information can be considered by the PCF for policy control is FFS, which depends on whether the information can be obtained as concluded in KI#1.

Editor's note:	Whether energy related information (e.g. energy consumption) per Application ID, PDU Session or QoS flow can be considered by the PCF for policy control is FFS, which depends on whether the information can be obtained as concluded in KI#1.

* * * End of Change * * * *