3GPP TSG-SA WG2 Meeting #162	S2-2405484

Changsha, China, April 15 – 19, 2024

Source:	CATT, China Mobile, vivo, ZTE, MediaTek Inc., DISH Network, InterDigital Inc., Huawei, HiSilicon, LGE, Lenovo, KDDI, NTT DOCOMO, Toyota, NEC

Title:	Conclusions for KI#2

Document for:	Approval

Agenda Item:	19.4

Work Item / Release:	FS_EnergySys / Rel-19

Abstract of the contribution: The contribution proposes conclusions for KI#2 "Subscription and policy control to support energy efficiency and energy saving as service criteria".

1. Introduction

Conclusions on KI#2 "Subscription and policy control to support energy efficiency and energy saving as service criteria" are proposed in this contribution based on the evaluations of existing solutions on KI#2. Further updates to the conclusions are to be done to accommodate possible new solutions, solution updates and further discussions.

2. Proposal

It is proposed to agree the following changes to 3GPP TR 23.700-66.

* * * Start of Change * * * *

## 8.x	Key Issue #2: Subscription and policy control to support energy efficiency and energy saving as service criteria

For KI#2, the following enhancements on subscription and policy control are agreed as interim conclusions to support energy efficiency and energy saving as service criteria in the 5GS:

-	The following are supported:

-

-	Energy saving authorization information to allow the network to perform energy saving for the UE.

Editor's note:	It is FFS whether and what energy related limits (e.g., energy consumption limits) per UE is to defined, controlled and used, which depends on whether and what energy related information per UE can be obtained as concluded in KI#1.

Editor's note:	It is FFS whether the energy saving authorization information per UE is needed.

Editor's note:	Whether the energy credit is stored in UDM/UDR or handled by the charging subsytem is FFS (decided in cooperation with SA WG5).

-	The PCF may take into account energy related information including subwhen making policy decisions on the AM, SM and UE policies.

Editor's note:	It is FFS what information in the AM, SM and UE policies can be determined and provided/updated for enforcement based on energy related information or subscription data.

Editor's note:	Whether the ratio of renewable energy and carbon emission information can be considered by the PCF for policy control is FFS, which depends on whether the information can be obtained as concluded in KI#1.

Editor's note:	Whether energy related information (e.g. energy consumption) per Application ID, UE, PDU Session or QoS flow can be considered by the PCF for policy control is FFS, which depends on whether the information can be obtained as concluded in KI#1.

Editor's note:	Whether energy related analytics provided by NWDAF can be considered by the PCF for policy control is FFS, which depends on the conclusion in KI#3.

Editor’s note:	Whether the interaction with CHF for policy enforcement and charging is FFS.

* * * End of Change * * * *

# Comments

Removed as the energy credit may be handled in charging subsystem

Suggested by Lenovo/Costas

Removed as the energy credit may be handled in charging subsystem, see the EN.