3GPP TSG-WG SA2 Meeting #162	S2-2405677

Changsha, China, April 15th – 19th, 2024	(revision of S2-2404817)

# Title:	KI#1:New Solution for DualSteer

# Source:	ZTE

# Document for:	Approval

Agenda Item:	19.13

Abstract:	This contribution provides a new solution for DualSteer

It is proposed to approve the following solution in TR 23.700-54.

* * * First Change * * * *

## 6.0	Mapping of Solutions to Key Issues

Table 6.0-1: Mapping of DualSteer Solutions to Key Issues

|  | Key Issues for DualSteer |
| --- | --- |
| Solution# | Key Issue #1.1 | Key Issue #1.2 | Key Issue #1.3 | Key Issue #1.4 |
| #X | x | x | x | x |

Table 6.0-2: Mapping of ATSSS_Ph4 Solutions to Key Issues

|  | Key Issues for ATSSS_Ph4 |
| --- | --- |
| Solution# | Key Issue #2.1 | Key Issue #2.2 |
| #2.1 | X |  |
| #2.2 |  | X |
| #2.3 | X |  |
| #2.4 | X |  |
| #2.5 | X |  |
| #2.6 |  | X |
| #2.7 |  | X |
| #2.8 |  | X |

* * * Next Change * * * *

## 6.X	Solution #X: Alternative SUPI in UE suubscription

### 6.X.1	Description

This solution is for key issue #1.1, #1.2, #1.3 and #1.4.

This solution focus on a DualSteer Device containing two separated UEs and supporting simultaneous data transmission over two network.Editor’s Note:	How to support non-simultaneous transmission (e.g. DualSteer Device containing insing UE or due to operator policy) is FFS.

In order to support DualSteer between PDU Sessions of two UEs, two subscriptions/SUPI (e.g. SUPI 1 and SUPI 2) are associated in the UDM. In this solution an Alternative SUPI IE is added in each subscription. Therefore each subscription are associated with two SUPIs, i.e. an existing SUPI and an Alternative SUPI.

Each UE performs Registration procedure separately, and the UDM stores the serving AMF for each UE. These two UEs may be registered in different PLMNs. In this case the AMF2 is assumed to be in the V-PLMN and the SMF, UDM, Anchor UPF is assumed to be in the H-PLMN.

Editor’s Note: It is FFS whether HPLMN policy is needed to trigger the registration of the additional access.

The PCF provides separated URSP rules to the UEs. The Access Type preference can be set to 3GPP access or Multiple Accesses.

When the UE in the DualSteer Device establishes a PDU Session, the SMF/SM PCF provides DualSteer rules to the UE. If the DualSteer rule indicates that DualSteer is possible for the application traffic (i.e. the other UE is registered in the other 3GPP Access), it triggers another UE in the DualSteer Device to establish a secondary PDU Session with same PDU Session ID via the other 3GPP Access. Same SMF, SM PCF and Anchor UPF are selected for the secondary PDU Session. The SMF allocate same IP addresses for the secondary PDU Session. The SMF use same N4 session towards the UPF and same SM association towards the PCF. However the PCF may provide different PCC rules to the SMF to support different QoS handling on different 3GPP Access.

The DualSteer rule indicates how to route the application traffic between two 3GPP Acceses. The DualSteer rule may reuse similar structure of the ATSSS rule, for example include Rule identifier, Traffic Descriptor and Access Selection Descriptor. DualSteer rule indicates the preferred 3GPP Access. Since the DualSteer does not support splitting of SDF, the DualSteer rule only supports the following Steering Modes: "Active-Standby", "Smallest Delay". When "Smallest Delay" is used the UE and Anchor UPF performs RTT measurement by using PMF message via different 3GPP Access.

Editor’s NOTE:	It is FFS how to identify the preferred 3GPP Access in DualSteer rule.

Editor’s NOTE:	Details on DS steering policies and DS switching policies and how they are applied is FFS

Editor’s NOTE:	It is FFS how to measure the delay on another leg as a service can only use a single leg.Editor’s NOTE:	How to ensure both USIM are used within the same DS device is FFS.

Editor’s NOTE:	How to limit the impact of establishing a secondary PDU Session for the same service at the earliest possible time is FFS

### 6.X.2	Procedures

The following is the high level procedure for DualSteer.

Figure 6.x.2-1: Examples on DualSteer Procedures

Step 0, The UDM is configured with the association between SUPI1 and SUPI2 as described in clause 6.x.1. For SUPI1 subscription, SUPI2 is added as Alternative SUPI. For SUPI2 subscription, SUPI1 is added as Alternative SUPI.

Step 1, The UE1/SUPI1 performs UE registration in AMF1 with the following enhancement:

-	None.

Step 2, The UE1/SUPI1 establishes first PDU Session 1 towards the S-NSSAI and DNN, with the following enhancements;

-	The UE includes a DualSteer request, PDU Session ID1 in the PDU Session Establishment message.

-	The AMF1 selects the SMF supporting DualSteer.

-	The Session Management Subscription data received from the UDM also includes the SUPI2 as Alternative SUPI. -	The SMF selects Anchor UPF and SM PCF supporting DualSteer.

-	The SMF sends DualSteer indication in SM Association Establishment request to PCF. The PCF generates DualSteer Rule in the PCC rule and notify the SMF. The SMF further provide DualSteer Rule towards the UE1.

Step 3, The UE2/SUPI2 performs UE registration in the AMF2 with the following enhancement:

-	The UE context in SMF data received from the UDM includes the SMF ID of PDU Session 1.

Step 4, The UE2/SUPI2 establishes secondary PDU Session 2 towards the S-NSSAI and DNN, with the following enhancements:

-	Based on the DualSteer rule received in step 2, the UE1/SUPI1 trigger the UE2/SUPI2 to establish PDU Session 2.

NOTE 1:	The interaction between UE1/SUPI1 and UE2/SUPI2 is up to UE internal implementation.

-	The UE2/SUPI2 includes DualSteer request, PDU Session ID1 in the PDU Session Establishment message.

-	Based on UE context in SMF data received from the UDM the AMF2 selects the same SMF for the PDU Session 2 as the PDU Session 1 of the UE1/SUPI1

-	AMF2 sends DualSteer request, PDU Session ID1 in Namf_CreateSMContext_Request message to SMF.

-	The Session Management Subscription data received from the UDM also includes the SUPI1 as Alternative SUPI.

-	Based on the Alternative SUPI, and the UE support of DualSteer, the SMF determines to associate the PDU Session 1 and PDU Session 2 and continue the establishment of PDU Session 2 as following:

-	The SMF selects same Anchor UPF and use existing N4 session towards the Anchor UPF.

-	The SMF selects same SM PCF and use existing SM association for the PDU Session 2.

NOTE 1:	SUPI2 is not forwarded to the Anchor UPF and SM PCF.

Editor’s NOTE:	Further impact on N4 Association and SM Assoication is FFS.

Step 5, The UE1/UE2 and Anchor UPF perform the DualSteer based on the received DualSteer rules as follows:

-	For uplink traffic, the DualSteer Device evaluates the DualSteer rule to determine which 3GPP Access is used and then forwards the uplink traffic via this 3GPP Access.

-	For down traffic, the DualSteer UPF evaluates the DualSteer rule to determine which 3GPP Access is used and then forwards the downlink traffic via this 3GPP Access.

NOTE 2:	One service shall be only transferred via a single 3GPP Access for both UL and DL direction.

### 6.X.3	Impacts on services, entities and interfaces

UDM：

-	enhanced to support Alternative SUPI for each UE subscription

-	enhanced to provide the SM context of SUPI towards the serving AMF of the associated SUPI.

AMF:

-	enhanced to select same SMF for secondary PDU session

-	selects the SMF supporting DualSteer based on DualSteer request indication

SMF:

-	enhanced to associated two PDU Sessions of two UEs based on subscription received from UDM

-	enhanced to provide DualSteer rule to UE and UPF

DualSteer Device

-	Trigger the secondary PDU Session establishment via UE2

-	The secondary PDU Session uses same PDU Session ID as the first PDU Session.

-	Include the DualSteer request in the PDU Session Establishment Request message.

-	support the DualSteer rule handling.

UPF

-	support the DualSteer rule handling.

PCF:

-	Provide DualSteer rule to SMF

* * * End of Changes * * * *