SA WG2 Meeting #S2-162	S2-2405403

15th -19th April 2024, Changsha, China	(rev of S2-2405166)

# Title:	TR 23.700-63, Solution #1 update

# Source:	Vodafone, Nokia, Samsung, China Mobile, DISH Network, Deutsche Telekom, Ericsson, ZTE

# Document for:	Approval

Agenda Item:	19.11

Abstract:	This pCR proposes an update of solution 1 for KI#3

# 1	Background

Solution#1 in TR 23.700-63 describes the information that is expected to be included by an AF at the time of  requesting insertion/detection of specific headers/tags at the user plane.

The actual header(s)/tag(s) were unclearly described in the solution and could be interpreted as being part of the metadata proposed and/or referenced by the identifier, what may lead to complexity at the time of stage 3 implementation.This pCR proposes the actual header(s)/tag(s) as part of the list of parameters included by the AF, in a conditional way, to consider use cases in which the AF and app provider dynamically agree e.g. detection of a particular header/tag to be followed by a notification.

Additionally, the example related to PCF extracting protocol information from the metadata is removed, to avoid adding complexity to the solution.

The revised pCR incorporates the proposals from S2-2404122 and S2-2404940, as well as some paragraphs and notes from S2-2404499 to complement the direct reporting option.

It also formats the subclauses for notifying, since two proposed ways of reporting are captured.

# 2	Proposal

It is proposed to agree the text below for inclusion into TR 23.700-63.

* * * * First Change * * * *

## 6.1	Solution #1: Provisioning of information for header handling

### 6.1.1	Description

Network operators can reach agreements with Application Service Providers to handle traffic specific to their applications in a particular way and/or under specific conditions, in terms of SLAs between both business parties.

Automation capabilities of 5G for network slicing, charging, interactions with AFs, use of analytics, etc permit MNOs to engage in agreements with Application service providers in a dynamic way compared to previous technologies and to provide relevant configurations for devices and network nodes using rules and policies to support such agreements.

One way of implementing agreements with an ASP is by exchanging in-band information included in the relevant protocols. Client, server or proxies in the traffic path can insert specific information or use specific protocols that imply a particular behaviour for the receiving entity. An example of insertion of information in Release 18 is the use of ECN for L4S to permit rate adaptation for a particular flow.

Release 18 specifications have also included functionality for Service Function Chaining capabilities so that an Application Function can request a particular steering of user plan traffic towards specific service functions in the N6-LAN. Additionally, in earlier releases, the enrichment of packet headers was possible in the uplink direction by including specifically the IMEI as part of the header. This capability has evolved in 5G to be more generic and make use of containers in FAR rules, however, it is still not available for request from the AF/operator platform and no functionality exists for notification upon detection of headers.

Recently, different standards organizations are engaged in developing protocols and market is developing mechanisms that permit the network to recognise the content so specific handling can be provided, while keeping the content encrypted.

The solution leverages existing functionality to address mechanisms that facilitate SLAs, in an environment where the variety of mechanisms and protocols keep on growing, using in-band information specific to the particular agreement:

-	Header/tag(s) handling request in N6 or in N3 and reporting.

The existing functionality for AF traffic influencing, together with use of PFDs as needed, is used as baseline for the solution proposed. For the discovery of UPF(s) enhanced to handle header/tags insertion/detectionThe following UPF capability is added in UPF profile stored in NRF:

-	Specific traffic detection and handling.

Different use cases may require procedures at different levels. The HTTP traffic is being reduced while encrypted protocols grow, so any potential insertion or detection would need to be at different layers, mainly transport and IP. To make the mechanism generic for different cases, it is proposed to use a rule referred to by an AF.

* * * * Next Change * * * *

### 6.1.2	Procedures

#### 6.1.2.1	Insertion/detection request

The proposed rule shall include:

| Input parameters from AF |
| --- |
| Header/Tag information (NOTE 3) | Identifier | Example: tagID (1) pointing to preconfigured Tag Type= RAT and Tag Value to be included by 5GC nodes |
|  | Tag Type + Tag Value | Example: Tag Type=FQDN, Tag Value=domain.com |
| Header/Tag Actions | Action | Values: Insert, Detect, Remove, Replace |
|  | Condition | Values: Always, at initiation, during certain period |
|  | Direction | Values: UL, DL |
| Header/Tag Handling Instructions | Reference | Example: RuleID (1) poiting to preconfigured information in UPF for protocol info, encryption handling, etc |
|  | Additional Data | Non-standard info used by AF to complement the preconfigured ruleID |
| Reporting Instructions (NOTE 1) | Type of report | Values: Direct, Indirect, No report (NOTE 1) |
|  | Condition for reporting | Values: Threshold based, Periodical with periodicity, etc |
|  | Reporting correlation identifier | Correlation ID (NOTE 2) |
|  | Reporting-to address | UPF event consumer URI (NOTE 2) |

Table 1 – Input parameters from AF

NOTE 1: The condition for reporting and reporting correlation apply when type of report is direct or indirect. Whether to include an explicit “no report” is left for stage 3.

NOTE 2: Nnef_TrafficInfluence includes already a Notification Target Address that could be used as the UPF event consumer URI. A correlationID would need to be added. In Nnef_TrafficInfluence these parameters are to report on user plane events. It remains to be seen if these existing parameters can be used also for the header handling reporting.

For the Reporting Instructions, there are two options for the AF to indicate whether direct reporting is required (i.e. using UPF exposure service):

-	Option 1: Report Correlation ID and UPF event consumer notification endpoint. The AF provides these attributes to indicate its preference to receive Session Reports directly from the UPF Exposure Service (see option 1 in Section 6.1.2.2.2) instead of default N4 based reporting described in Section 6.1.2.2.1

-	Option 2: the AF provides Notification Target Address (+ Notification Correlation ID) attributes to request to receive Session Reports, and direct indication to request that they are sent directly with UPF Exposure Service.

Editor’s Note: Only one of the above options, with its associated procedures in the following chapters, will be taken for conclusion.

The header/tag handling instructions are assumed as pre-agreed information between the parties (the operator and third party application provider) to include header/tags handling related information (e.g. protocol layer, type of encryption, etc), which is pre-configured in the UPF. This parameter contains a reference to the pre-configured info as well as, optionally, additional data that the AF provides to complement the pre-configured information. This additional data is not standardised, but only interpreted by UPF based on SLA and implementation.

NOTE 3: Headers/Tags types and values can be conditionally included by the AF (according to the use case). When those are not included, the Identifier requested points to a preconfigured Header/Tag type whose value is to be determined by the PCF, SMF or UPF depending on the data from network and/or policy information.

Leveraging on the NF service Nnef_TrafficInfluence, and following the description in clauses 5.6.7 and 5.6.16 of TS 23.501, an AF may request the SMF, via NEF and PCF, handling some header/tag to the protocol at the user plane for:

-	a particular S-NSSAI/DNN; and

-	a particular application; and/or

-	a particular UE/group of UEs or any UE.

The information in table 1 is provided in the relevant Nnef_TrafficInfluence operation (create/update/delete) by the AF. The AF request may not always need to be linked to an ongoing PDU session. The request can be applied to the ongoing or future PDU session.

The following sequence is extracted from clause 4.3.6.2 of TS 23.502 [3] to apply for this solution:

Figure 6.1.2-1: Nnef_TrafficInfluence operation (clause 4.3.6.2 of TS 23 502 [3])

In step 1, the AF inserts the rule contents, including the information that is relevant for the parties (as metadata). The request may target “any UE”.

In step 2, NEF confirms the AF request is authorised based on local configuration, and then will store/update the received data in the UDR for data set pointing to application data.

At notification from UDR, PCF verifies the content of the header/tag identifier (or the header/tag type and value) and the header/tag handling instructions  as the pre-agreed information between the parties and transforms it in the relevant information to be inserted/detected (i.e.. deriving header/tag type and value from the header/tag identifier, etc.). It will be included in the PCC rule together with the handling instructions reference, the additional data contents (if provided), and the direction for handling. If the AF requests reporting on header/tag detection/replacing/removal, the PCF includes in the PCC rule(s) the information required for reporting the event, including indicating whether duplicate reporting is needed.

NOTE 4: Duplicate reporting does not assume to provide two simultaneous notifications to the AF. Duplicate reporting refers to UPF reporting directly to the AF, if AF has requested so, and reporting to SMF via N4, in case SMF needs to perform some additional actions.

In step 5, the PCF determines if existing PDU Sessions are potentially impacted by the AF request. For each of these PDU Sessions, the PCF updates the SMF with corresponding new policy information about the PDU Session.

For future PDU Sessions, PCF delivers policy information during SM policy establishment.

In step 6, in case the AF request results in the selection/addition/removal/replacing of a UPF in the data path, the SMF discovers the UPF(s) as described in TS 23.501 with the UPF capability of specific header/tag detection and handling, then the following options exist:

OPTION 1

SMF installs PDR/FAR and URR including new Report Correlation ID (if reporting required) rules using N4 procedures into the UPF and if Report Correlation ID exists, then the SMF subscribes (on behalf of the AF) to the UPF Exposure Service’s Traffic Influence Reporting event (see Section 6.1.2.2.2) using this ID and UPF event consumer notification endpoint that was provided together with the ID. Further some additional action maybe included for SMF to perform in case of detection of particular header/tag.

OPTION 2

-	The SMF installs in UPF PDRs with associated FARs including the Header handling Rule. The Header handling Rule provides UPF with instructions for what to report, reporting conditions and when Direct Reporting applies, contact information:

-    When Direct reporting applies, the Notification Target Address (+ Notification Correlation ID) is included in FAR. When notification triggers are met, UPF sends Nupf_EventExposure notification for a new Event. This new event is subscribed by SMF on behalf of AF using FAR.

-    When N4 reporting is required, SMF associates a URR to the PDR, the report trigger being that FAR header handling notification conditions are met.  The N4 report could be sent in addition to or instead of the Nupf Event Exposure notify.

This option is also further described in Section 6.1.2.2.2

* * * * Next Change * * * *

#### 6.1.2.2	Header/tag reporting/notification

When a detection action is requested by the AF, SMF and UPF are instructed to report information included by the client or server side under the SLA. The instruction for detecting a header/tag may or may not be associated with an insertion/removal/modification/replacement.

The AF may decide whether the Nnef_TrafficInfluence_Notify service or Nupf_EventExposure service is to be expected for the reporting/notification of detected header/tags, according to the settings the AF makes as described in clause 6.1.2.1

When the notification/reporting is done via Nnef_TrafficInfluence_Notify, the procedure in TS 23.502 clause 4.4.2.2 is applicable to this solution upon detection in the UPF of a PDR associated to a URR.

Figure 6.1.2.2-1 N4 Session Report (TS 23.502 [3] clause 4.4.2.2)

When UPF detects the header/tag requested by the AF, the UPF notifies with N4 Session Report to the SMF. The N4 session report include the information related to the header/tag that has been detected.

Alternatively, the AF can indicate its preference to use direct reporting based on UPF Exposure Service by

- Option 1, including both Report Correlation ID and UPF event consumer notification URI values in Traffic Influence header handing rule described in Section 6.1.2.1. In this case, the procedure is described in clause 6.1.2.2.2.

- Option 2, including Notification Target Address (+ Notification Correlation ID) attributes to request to receive Session Reports, and direct indication to request that they sent directly with UPF Exposure Service

If the detection action is associated with an insertion/removal, modification or replacement,

- Option 1, if Report Correlation ID value was not defined, then the UPF  uses N4 Session report to notify the SMF. The N4 session report  include instead information about the header/tag detected and the action performed on it.

- Option 2, if URR reporting trigger is set to be that, during execution of the header handling Rule in the FAR (on same PDR), the conditions for notification are met. UPF uses N4 Session report to notify to the SMF. The N4 session report includes information of the action, detected header and sent header. This is further described in clause 6.1.2.2.2

##### 6.1.2.2.1	Header/tag reporting/notification leveraging Nnef_TrafficInfluence_Notify

The following simplified sequence, derived from clause 4.3.6.3 of TS 23.502 [3], is to apply for this solution upon notification from the UPF:

Figure 6.1.2.2.1-1: Notification of header detection to AF using Nnef_TrafficInfluence service

Based on the configuration by AF, upon receiving N4 Session Report from SMF, SMF may use Nsmf_EventExposure_Notify operation to expose relevant information to the NEF/AF (e.g. Header/Tag detected). SMF may notify PCF using the existing Npcf services for event reporting.

After the step 2b, the actions the AF may execute are not depicted; those will depend on the agreement with the MNO.

After the Step 3a, the actions the PCF may execute are not depicted and may depend on the SLA between AF and MNO.

NOTE 5:	Reporting detection of a header for Any UE or for some popular applications can cause UPF to issue lots of reports and consequently high signaling load. Requesting reporting of a header/tag detection in UEs traffic needs to be considered with care. If high signaling load is concerned, then alternative solution using direct reporting from UPF to AF can be used, instead of N4 based reporting.

* * * * Next Change * * * *

##### 6.1.2.2.2	Header/tag reporting/notification leveraging UPF Exposure Service

There are two possible options:

OPTION 1

The AF can include Report Correlation ID and UPF event consumer notification URI values in the Traffic Influence rule in the request of new Nnef_TrafficInfluence service and after that the same ID can be used in subscribing new Traffic Influence Reporting event of UPF Exposure Service to receive direct Session Reports from the UPF.

In the UPF, for each triggered report event (Step1 in Figure 6.1.2.2-1) with the URR without Report Correlation ID specified, the default actions, i.e., reporting over N4, apply. But if the Report Correlation ID is found, then the UPF checks whether the Report Correlation ID value has Traffic Influence Reporting event subscriptions and if so, then the direct reporting is used towards the AF instead. If no subscription is found, then the reporting is ignored.

New Traffic Influence Reporting event for UPF Exposure Service is defined in Table 1. If the AF has indicated its preference to receive Session Reports directly from the UPF, then the SMF can discover the UPF Exposure Service details from the NRF and subscribes to the UPF on behalf of the AF (like described in Figure 4.15.4.5.2-1 “Subscription to UPF event exposure service for certain UE(s) via SMF” in TS 23.502)  by sending a UPF event exposure subscribe request (HTTP request like defined in TS 29.564 [x]) where the existing URR is referred by the given Reporting Correlation ID. If no URRs with the given ID is found, then the subscription fails, and respective HTTP error status is returned as described by Step2b in Figure 5.2.2.2.2-1 “Subscription creation“ in TS 29.564 [x]. If URR(s) with the given ID is(are) found, then the subscription is created and the related URR(s) will result in Session reports to be sent as direct notifications to the consumer AF as shown in Figure 5.2.2.3.2-1 “UPF sends notification on subscribed events” in TS 29.564 [x].

Table 2: Traffic Influence Reporting event.

| Description | This event provides Traffic Influence reporting directly for the subscriber instead of using N4 signaling. |
| --- | --- |
| Subscription type | Subscription to UPF/Nupf_EventExposure Subscribe |
| Subscription inputs to UPF | Required: - UPF event consumer notification URI. - Reporting Correlation ID. |
| Report type | Continuous (event triggered) Report. |

OPTION 2

The AF that wants to receive direct notifications indicates so in the Nnef_TrafficInfluence request and AF includes then Notification Target Address (+ Notification Correlation ID). PCF includes this information with the Header handling Rule in the corresponding PCC Rule sent to SMF.

PCF can include a new Policy Control Request Trigger to request SMF to send the notifications that it receives from UPF to PCF.

NOTE: 	Triggers are not sent per PCC Rule, therefore, when trigger is activated, the PCF is requesting to receive all notification reports that SMF receives from UPF. But the notification reports are sent to AF either by SMF or UPF, according to AF request

SMF translates the PCC Rule into the corresponding PDR(s) and includes the header handling Rule in the PDR:

-	If Direct notification has been requested in the PCC Rule, the Notification Target Address (+ Notification Correlation ID) are also included with the header handling Rule in the FAR associated to the PDR(s).

-	If SMF determines that the UPF notification report should be sent to SMF, SMF sends an associated URR. URR includes a new reporting trigger event that indicates UPF to send the report when a notification si triggered at  execution of the header handling Rule in the FAR associated to that same PDR.

-	SMF may send a URR to UPF because AF has not indicated direct reporting (notifications are to be sent to AF from SMF). But, even if UPF reports directly to AF, SMF may also send URR if SMF wants receive the notification reports for other purposes (e.g. to satisfy the PCF request).

UPF sends the header handling report notification in a new UPF event exposure event which can only be subscribed by SMF on behalf of the consumer.

* * * * Next Change * * * *

### 6.1.3	Impacts on services, entities and interfaces

-	NEF

-	Nnef_TrafficInfluence service, include the new Header handling and reporting information for a new event as described in 6.1.2.1) and handling new event in the Event ID reported to AF

-	UDR

-	Nudr_DataManagement service, adding new data subset in the Application data set.

-	PCF

-	PCC rule to add header handling information in the PCC based on request received a local  information and policies.

- 	NRF:

-	Storing new UPF capability in UPF profile.

-	Discovery of UPF(s) with the new UPF capability of header/tag detection and handling.

-	SMF

-	Discovery of UPF(s) with the new UPF capability of header/tag detection and handling.

-	Nsmf_EventExposure service, to include new event for notification to the AF

-	To depict PDR/FAR/URR rules handling for header/tag handling.

-	N4 updates

-	Impacts related to reporting over N4 (depending on the solution option selected)

-	Support Traffic Influence Reporting event subscriptions of the UPF Exposure Service on behalf of the AF.

-	UPF

-	N4 updates: Header handling capability, for insertion/modification/removal/replacement and/or detection

-	UPF Exposure Service supports new Traffic Influence Reporting event.

-	Support new Report Correlation ID field in URR and Traffic Influence Report handling.

* * * * End of Changes * * * *