SA WG2 Meeting #162	S2-2405099

15 April – 19 April, 2024, Changsha, China                                     (Revision of S2-2404452)

Source:	OPPO, InterDigital Inc.

Title:	Key Issue #8, New Solution: Identify Traffic Flows from the Tethered Devices

Document for:	Approval

Agenda Item:	19.3

Work Item / Release:	FS_XRM_Ph2/ Rel-19

Abstract of the contribution: This paper proposes a new solution for Key Issue #8.

# 1.	 Discussion

Key Issue #8 states:

This solution describes how an application on the UE provides information related to its tethered devices and the delay values associated with their tethered links to the AS, and how the delay values are used when setting the QoS parameters.

# 2. Proposals

It is proposed to adopt the following text in TR.23.700-70 v0.4.0.

*** First Change ***

ADD Solutions Table from section 6.0 here

*** Next Change (All New Text) ***

## 6.X	Solution #X: Identifying Traffic Flows from the Tethered Devices

### 6.X.1	Key Issue mapping

This solution addresses Key Issue #8, "Enhancement for UE with the tethered devices".

### 6.X.2	Description

In some XR services, the end device(s) used for consuming XRM services may not be the UE but the device(s) that are tethered to the UE. For example, AR glasses may be tethered to the UE for sending orientation related traffic.

Differentiated QoS handling is required for traffic from these tethered devices, not only accounting for traffic with different QoS requirements, but also accounting for the delay introduced by the tethered link. For example, when receiving traffic from tethered devices, the delay value associated with each flow is the sum of the delay associated with the tethered link and the delay associated with the connection between the UE and the AS. Therefore, flows that belong to tethered devices must be identified so that the additional delay value can be accounted for.

The main principle of the solution is that the UE Application uses SDP signalling to inform the AS which flows are associated with tethering delays. The UE Application also provides the device identifier that is associated with the flow to the AS. Then, when the AS configures QoS for the flows, the AS considers the additional tethering delay values when selecting a QoS Reference or QoS Parameters and provides device identifiers to the 5GC. The Packet filter provided by AF to CN is extended with one or multiple tethered device identifier(s).

NOTE 1:	The SDP signalling aspects of this solution require coordination with SA WG4.

NOTE 2:	The device identifier that is provide by the UE to the AS and by the AS to the 5GC only needs to be unique within the PDU Session. For example, it can be value that the UE associates with the device. The value does not need to be known to the tethered device.

### 6.X.3	Procedures

#### 6.X.3.1	AF/AS Based Procedure

Figure 6.x.3-1 is a procedure that is initiated based on an API invocation from the AF/AS.

Figure 6.x.3.1-1: Setting up QoS for Tethered Devices Based on AS/AF API Invocation

- The Application in the UE (e.g. the RTC endpoint) sends an SDP message to the AS with information related to delay values associated with traffic that comes from the tethered devices. This message can include the associated delay value and the packet filters that identify the RTP Session or stream that carries traffic from the tethered device. The packet filter includes one or multiple tethered device identifier(s).

- The AS invokes Nnef_AFsessionWithQoS_Create to configure QoS for the flow and provides the packet filter, and considers the delay value when selecting a QoS Reference or QoS Parameters.

- The NEF authorizes the request from the AS.

- The NEF sends the packet filter,  to the PCF.

- The PCF responds to the NEF.

- The NEF responds to the AS.

- The SMF Receives PCC Rules from the PCF. The PCC Rules include the QoS Parameters that are authorized for the service data flows.

- The SMF responds to the PCF.

- The SMF sends QoS Rules to the UE. The QoS Rules include the packet filter which is extended with identities of the tethered devices. The UE can use the identities to map uplink traffic from the tethered devices onto the correct QoS Flow.

After the procedure of Figure 6.x.3.2-1 , for UL traffic, UE performs traffic filtering with the received QoS rule(s). UE evaluates UL packets considering the IP/UDP traffic header and also considering the tethered device who provides the traffic to UE.

NOTE: 	How UE gets the tethered device identifier of the tethered devices behind the UE is not in the scope of 3GPP.

NOTE:     How UE measures the delay values associated with traffic that comes from the tethered devices is not in the scope of 3GPP

### 6.X.4	Impacts on services, entities and interfaces

- 	UE Application:

-	Provides delay values and device identifiers that are associated with flows that belong to tethered devices to the AS in an SDP message.

-	AS:

-	Receives the delay values and device identifiers that are associated with flows that belong to tethered devices to the AS in an SDP message.

-	PCF:

-	Receives the device identifiers and packet filters from the AF (possibly via the NEF) or from the SMF.

-	Generates PCC Rules with Packet Filters that include device identifiers.

-	SMF:

-	Receives PCC Rules with Packet Filters that include device identifiers.

-	Generates QoS Rules with Packet Filters that include device identifiers.

-	UE:

-	Receives QoS Rules with Packet Filters that include device identifiers.

-	Filters uplink traffic based on the with Packet Filters including device identifiers in the QoS Rules.

*** End of Changes ***

# Text boxes

In some XR services, the end point for those XRM service is not the UE but is the tethered device behind the UE, e.g. AR glasses tethering the cell phone. The traffic from tethered devices may require differentiated QoS handling.

This key issue aims at addressing the following points:

-	Study whether and how to identify traffic flows from the tethered devices behind the UE from the uplink traffic (e.g. traffic from different tethered devices may be mapped to different QoS Flows to enable QoS differentiation).

NOTE: 	At the conclusion phase, it will be determined whether the solution is also applicable to 5G RG.