3GPP TSG-SA3 Meeting #115	S3-24xxxx

# Athens, Greece, 26th February - 1st March 2024							rev- S3-240359

# Source:	Nokia, Nokia Shanghai Bell, CableLabs

# Title:	pCR on Non3GPPMob_Sec  TR Scope

# Document for:	Approval

Agenda Item:	5.8

# 1	Decision/action requested

It is requested to approve the chapter 4 content.

# 2	References

[x] 3GPP TR 33.702: "Study on Security for mobility over non-3GPP access to avoid full primary authentication."

# 3	Rationale

This pCR introduces the scope section of the FS_Non3GPPMob_Sec study.

# 4	Detailed proposal

**** START OF CHANGE ****

# 1	Scope

The following objectives will be studied in this study:

- Study the security aspects and procedure enhancements needed to support UE connecting to a new target TNAP within the same TNGF without performing full primary authentication.

- Study the security aspects and procedure enhancements needed to support AUN3 connecting to a new target RG under the same WAGF without performing full primary authentication.

- Study the security aspects and procedure enhancements needed to support N5CW devices connecting to a new target Trusted WLAN AP within the same TWIF without performing full primary authentication.

- Study the security aspects and procedure enhancements needed to support UE connecting to a new WLAN AP that shares the same NSWOF without performing full primary authentication.

This study does not cover actual mobility, where call/session continuity is maintained. I.e. when UE/device is moving from one AP/TNAP/TWAP to another, connectivity can break, and then UE will reconnect.

**** END OF CHANGE ****