3GPP TSG-SA3 Meeting #115	S3-24xxxx

Athens, Greece, 26th February - 1st March 2024					rev- S3-240361

# Source:	Nokia, Nokia Shanghai Bell, CableLabs, LG Electronics, Huawei, HiSilicon

# Title:	pCR on KI on AUN3 device connecting to the new 5G-RG

# Document for:	Approval

Agenda Item:	5.8

# 1	Decision/action requested

It is requested to approve the chapter 4 content.

# 2	References

[x] 3GPP TR 33.702: "Study on Security for mobility over non-3GPP access to avoid full primary authentication."

# 3	Rationale

This pCR introduces the KI for  FS_Non3GPPMob_Sec study.

# 4	Detailed proposal

**** START OF CHANGE ****

## 5.x	Key issue #x: Security aspect of AUN3 device connecting to a new 5G-RG within the same W-AGF.

### 5.x.1	Key issue details

When AUN3 device moves from 5G-RG1 and 5G-RG2, where both 5G-RG are nearby or overlapping, the AUN3 device connectivity can break while connecting to the new 5G-RG2. Additionally, AUN3 also goes through another full primary authentication procedure, even though both 5G-RGs connects to the same W-AGF.

A new full primary authentication may lead to additional signalling and may cause latency in the AUN3 device connection. If we skip the full primary authentication, it provides connection time optimisation, but then the security aspect of the AUN3 device to target 5G-RG should be studied.

### 5.x.2	Threats

Not applicable.

### 5.x.3	Potential security requirements

The 5GS should support a mechanism to establish secure connection for the AUN3 device switching from one 5G-RG to another 5G-RG within the same W-AGF without performing full primary authentication.

While switching from one 5G-RG to another 5G-RG within the same W-AGF, the interface between AUN3 device and the new 5G-RG shall be confidentiality, integrity, and replay protected.

**** END OF CHANGE ****