3GPP TSG-SA3 Meeting #115	S3-24xxxx

Athens, Greece, 26th February - 1st March 2024					rev- S3-240362

# Source:	Nokia, Nokia Shanghai Bell, CableLabs, LG Electronics,

# Title:	pCR on KI on N5CW device connecting to the new TWAP

# Document for:	Approval

Agenda Item:	5.8

# 1	Decision/action requested

It is requested to approve the chapter 4 content.

# 2	References

[x] 3GPP TR 33.702: "Study on Security for mobility over non-3GPP access to avoid full primary authentication."

# 3	Rationale

This pCR introduces the KI for  FS_Non3GPPMob_Sec study.

# 4	Detailed proposal

**** START OF CHANGE ****

## 5.x	Key issue #x: Security aspect of N5CW device connecting to a new TWAP within the same TWIF.

### 5.x.1	Key issue details

When the N5CW device moves from TWAP1 to TWAP2, where both TWAPs are nearby or overlapping, the N5CW device connectivity can break while connecting to the new TWAP. Additionally, the N5CW device also goes through another full primary authentication procedure, even though both TWAPs connect to the same TWIF.

A new full primary authentication may lead to additional signalling and may cause latency in the N5CW device connection. If we skip the full primary authentication, it provides connection time optimisation, but then the security aspect of the N5CW device to target TWAP should be studied.

### 5.x.2	Threats

Not applicable.

### 5.x.3	Potential security requirements

The 5GS should support a mechanism to establish secure connection for the N5CW device switching from one TWAP to another TWAP within the same TWIF without performing full primary authentication.

While switching from one TWAP to another TWAP within the same TWIF, the interface between the N5CW device and the new TWAP shall be confidentiality, integrity, and replay protected.

**** END OF CHANGE ****