3GPP TSG-SA3 Meeting #115	S3-24xxxx

Athens, Greece, 26th February - 1st March 2024					rev- S3-240363

# Source:	Nokia, Nokia Shanghai Bell, CableLabs, Huawei, HiSilicon

# Title:	pCR on KI on UE connecting to the new WLAN AP under the same NSWOF

# Document for:	Approval

Agenda Item:	5.8

# 1	Decision/action requested

It is requested to approve the chapter 4 content.

# 2	References

[x] 3GPP TR 33.702: "Study on Security for mobility over non-3GPP access to avoid full primary authentication."

# 3	Rationale

This pCR introduces the KI for  FS_Non3GPPMob_Sec study.

# 4	Detailed proposal

**** START OF CHANGE ****

## 5.x	Key issue #x: Security aspect of UE connecting to a new WLAN AP connected via the same NSWOF.

### 5.x.1	Key issue details

When UE moves from WLAN AP1 to WLAN AP2, where both WLAN APs are nearby or overlapping, the UE connectivity can break while connecting to the new WLAN AP. Additionally, UE also goes through another full primary authentication procedure at the NSWOF as defined in annex S of TS 33501[y], even though both WLAN APs connect to the same NSWOF.

A new full primary authentication may lead to additional signalling and may cause latency in the UE connection. This is inefficient and disrupts the user experience. If we skip the full primary authentication, it provides connection time optimisation, but then the security aspect of the UE to target WLAN should be studied.

### 5.x.2	Threats

Not applicable.

### 5.x.3	Potential security requirements

The 5GS should support a mechanism to authenticate the UE switching from one WLAN AP to another WLAN AP connected to the same NSWOF without performing full primary authentication.

**** END OF CHANGE ****