3GPP TSG-SA3 Meeting #115 	S3-240872

Athens, Greece, 26 Feb – 1 March 2024                                                  Revision of S3-240727

# Source:	Indian Institute of Technology Bombay

# Title:	SMSF Specific Security requirement and test case for draft TS 33.529

# Document for:	Approval

Agenda Item:	4.4

# 1	Decision/action requested

SA3 is kindly requested to approve the new requirement and test case in draft 33.529 v0.3.0 Security Assurance Specification for SMSF

# 2	References

[1]	3GPP TS 33.529 “Security Assurance Specification (SCAS) for the Short Message Service Function (SMSF)  network product class” v0.3.0

# 3	Rationale

This contribution proposes to add new requirement and a test case in the TS draft [1] for protection of the non-SBI Diameter-based SGd interface for communication to and from SMSF with IP-SM-GW/GMSC/SMS- router.

# 4	Detailed proposal

*************** Start of the 1st Change ****************

# 2	References

The following documents contain provisions which, through reference in this text, constitute provisions of the present document.

-	References are either specific (identified by date of publication, edition number, version number, etc.) or non-specific.

-	For a specific reference, subsequent revisions do not apply.

-	For a non-specific reference, the latest version applies. In the case of a reference to a 3GPP document (including a GSM document), a non-specific reference implicitly refers to the latest version of that document in the same Release as the present document.

[1]	3GPP TR 21.905: "Vocabulary for 3GPP Specifications".

[2]	3GPP TS 33.117: "Catalogue of general security assurance requirements".

[3]	3GPP TS 33.501: "Security architecture and procedures for 5G system".

[4]	3GPP TR 33.926: "Security Assurance Specification (SCAS) threats and critical assets in 3GPP network product classes".

[5] 					3GPP TS 23.040: "Technical realization of the Short Message Service (SMS) ".

[n]			3GPP TS 33.210: “ Network Domain Security (NDS): IP network layer security”

[o]			3GPP TS 33.310: “ Network Domain Security (NDS): Authentication Framework”

[p]			IETF RFC 6733: “Diameter Base Protocol”

*************** End of the 1st Change ****************

*************** Start of the 2nd Change ****************

# 3	Definitions of terms, symbols and abbreviations

## 3.1	Terms

For the purposes of the present document, the terms given in  TR 21.905 [1] and the following apply. A term defined in the present document takes precedence over the definition of the same term, if any, in  TR 21.905 [1].

Service center (SC): Defined in TS 23.040 [5].

Short message (SM):  Defined in TS 23.040 [5].

Diameter application nodes: Network entities, i.e., SMSC, IP-SM-GW, SMS-Router in SMS application case, that implement the Diameter protocol to establish connection with other nodes implementing Diameter protocol.

*************** End of the 2nd Change ****************

*************** Start of the 3rd Change ****************

#### 4.2.7	Security functional requirements on the SMSF– Non Service-Based Interfaces

4.2.7.1 Protection on SGd Diameter Interface between SMSF and the Diameter Application Node

Requirement Name: Protection data and information on SGd

Requirement Reference: TS 33.501 [3], clause 9.5, TS 33.210 [n], clause 6.2, TS 33.310 [o], clause 6.1.3a

Requirement Description: TS 33.501 [3] mentions that protection of Diameter interface shall be supported according to NDS/IP as specified in 33.210 [n], unless security is provided by other means e.g., physical security. For authentication between SMSF and Diameter application node over diameter interface, mutual authentication based on client and server certificates is performed, if using TLS. Certificate based authentication follows the profiles given in TS 33.210 [n] clause 6.2, and TS 33.310 [o] clause 6.1.3a, with the restriction that it shall be compliant with the profile given by Diameter Base Protocol as defined in RFC 6733 [p], except the cipher suites. A SEG may be used to terminate the NDS/IP IPsec tunnels.

Threat References: tba

Test Case:

Test Name: TC_Protect_Diameter_SGd

Purpose: To verify the mechanisms implemented to protect data and information in transfer to and from the SMSF's Diameter protocol-based SGd interface.

Note: This test case applies to the Network function with SGd Diameter Interface.

Preconditions:

Network product documentation containing information about supported NDS/IP protocols is provided by the vendor.

A Diameter Application Node peer implementing the security protocol configured by the vendor shall be available.

SMSF documentation, stating which security protocols for protection of data in transit are implemented and which profiles in TS 33.310 [o] and TS 33.210 [n] are applicable, is provided by the vendor. The tester shall base the tests on the profile defined by 3GPP in Clause 6.2 of TS 33.310 [o].

For TLS/DTLS, the tester shall base the tests on the profile defined by 3GPP in Clause 6.1.3a of TS 33.310 [o] and Clause 6.2 of TS 33.210 [n], with the restriction that it shall be compliant with the profile given by Diameter Base Protocol as defined in RFC 6733 [p], except the cipher suites.

For IKE and IPsec, the tester shall base the tests on the profile defined by 3GPP in TS 33.210 [n].

Procedure and execution steps, expected results, expected format of evidence:

These are the same as for the test case in TS 33.117, clause 4.2.3.2.4, excluding execution step 4, and the profiles as mentioned in requirement description shall be followed in pre-conditions.

*************** End of the 3rd Change ****************