3GPP TSG-SA3 Meeting #115	S3-240946

Athens, Greece, 26th February - 1st March 2024 						revision of S3-240615

# Source:	Nokia, Nokia Shanghai Bell

# Title:	new key issue on IMS DC capability exposure

# Document for:	Approval

Agenda Item:	5.2

# 1	Decision/action requested

Approve the KI added to TR 33.790

# 2	References

[1]	3GPP TR 23.700-77 Study on system architecture for next generation real time communication services Phase 2

[2]	3GPP TR 33.790 Study on the security support for the Next Generation Real Time Communication services phase 2

# 3	Rationale

The SA2 study scope includes the enhancement for exposure of IMS capability/event in the context of IMS data channel session and made well progress in last two meetings on the work tasks. Two key issues (KI#1, 2) are identified in the TR 23.700-77 to support IMS event and capability exposure in the context of data channel (DC) communication/session.

•	Key Issue #1: Extensible IMS mechanism supporting IMS events in the context of DC communication.

•	Key issue #2: Impact on IMS architecture, interfaces, and procedures to support IMS capability exposure in the context of IMS data channel session.

Accordingly, seven solutions are documented in the TR 23.700-77 to address the KIs.

•	Solution #1: Architectural Enhancements in Support of exposure of IMS events using HSS Subscription

•	Solution #2: Event subscription and notification enhancements for DC applications

•	Solution #3: Subscription and Notification for DC Events

•	Solution #4: Event subscription and notification of IMS DC for related subscribers

•	Solution #5: IMS event subscription mechanism

•	Solution #6: IMS capability exposure architecture

•	Solution #7: Solution for IMS capability exposure via DC3/DC4

In DC service exposure solutions in TR 23.700-77v030, it requires NEF to securely expose DC services to DC AF/AS, e.g.:

-	NEF authorizes AF request and provides response.

-	Network Exposure Function (NEF): It shall securely expose IMS capability and events provided by DCSF to DCAS exposure and exposes new services to external AF.

-	Editor’s Note:	How NF that subscribed to HSS is authenticated and authorized by IMS is FFS.

From security point of view, without proper security control, the IMS DC services may be illegally used by malicious application function/server (AF/AS), and cause compromising on confidentiality, integrity, availably and privacy of IMS system and end users, e.g.:

-	Event of DC establish, terminate, DC application download, etc., may be exposed to unexpected 3rd party DC AS without aware of the end user.

-	Caller/Called Id of a DC session is disclosed to unexpected 3rd party AF/AS.

-	Subscriber's favourite (applications) and habit could be disclosed to and inferred by unexpected 3rd party AF/AS

-	The malicious AF may update/terminate an ongoing DC, and cause interruption on the IMS communication of an end user (Denial of Service, DoS).

-	The malicious AF may manipulation DC to push unwanted services to the user, e.g. AF manipulates the bootstrap DC to download unwanted applications without awareness of the user/UE.

-	The malicious AF may manipulation DC to over-consume the IMS and network resources with or without awareness of the user/UE.

The contribution proposes a new KI on security aspects of IMS DC capability/event exposure (KI#1, 2 of TR 23.700-77).

# 4	Detailed proposal

All content in the change part is new.

***************  Start of 1st change  ************

## 5.X	Key Issue #X: security and privacy aspects of IMS DC capability exposure

### 5.X.1	Key issue details

Two key issues are identified in the TR 23.700-77 to support IMS event and capability exposure in the context of data channel (DC) communication/session. Please refer to KI#1, 2, and relevant solutions 1-7.

From security point of view, without proper security control, the IMS DC services may be illegally used by malicious application function/server (AF/AS), e.g.:

-	Event of DC establish, terminate, DC application download, etc., may be exposed to unexpected 3rd party DC AS without aware of the end user.

-	The malicious AF may update/terminate an ongoing DC, and cause interruption on the IMS communication of an end user (Denial of Service, DoS).

-	The malicious AF may manipulation DC to push unwanted services to the user, e.g. AF manipulates the bootstrap DC to download unwanted applications without awareness of the user/UE.

-	The malicious AF may manipulation DC to over-consume the IMS and network resources with or without awareness of the user/UE.

Secondly, there could be a privacy compromise of the user. i.e.

-	Caller/Called Id of a DC session is disclosed to unexpected 3rd party AF/AS.

-	Subscriber's favorite (applications) and habit could be disclosed to and inferred by unexpected 3rd party AF/AS.

### 5.X.2	Security threats

•	Privacy of IMS data channel user could be leaked with exposing personal data to unexpected 3rd party AS/AF.

•	DoS attack could be launched with data channel communication being interrupted/modified by illegal AS/AF.

•	DoS attack could be launched towards UE and IMS system with downloading unwanted application(s) to UE(s) and establishing unwanted DCs for UE(s) by illegal AS/AF, hence exhaust either media or transport resources or both.

### 5.X.3	Potential security requirements

•	The IMS system shall provide capability to support authentication and authorization of data channel application server/function (DC AS/AF) when exposes DC capability/event to the AS/AF.

•	The IMS system shall provide capability to protect the privacy of DC user when exposes DC event to an AS/AF.

***************  End of change  ************