3GPP TSG-SA3 Meeting #115	draft_S3-240334-r1

Athens, February 26 - March 01, 2024

# Source:	Lenovo, Motorola Mobility, AT&T, Charter Communications, Johns Hopkins University APL

# Title:	Security Assumptions for TR 33.794

# Document for:	Approval

Agenda Item:	5.1

# 1	Decision/action requested

This pCR proposes security assumptions to be considered for the TR 33.794.

# 2	References

[1]	3GPP SP-231784, 'New Study on enablers for Zero Trust Security'.

[2]	3GPP TR 33.794, 'New Study on enablers for Zero Trust Security', Release 19.

[3]	3GPP TR 33.894, ''Study on applicability of the zero trust security principles in mobile networks'', Release 18.

# 3	Rationale

This contribution provides security assumptions related to WT1 and WT2 [1] to be considered for the study [2] based on the progress of the security analysis and findings from TR 33.894 [3].

# 4	Detailed proposal

SA3 is kindly requested to agree the pCR below to TR 33.794.

*****Start of Change 1*****

# 2	References

The following documents contain provisions which, through reference in this text, constitute provisions of the present document.

-	References are either specific (identified by date of publication, edition number, version number, etc.) or non-specific.

-	For a specific reference, subsequent revisions do not apply.

-	For a non-specific reference, the latest version applies. In the case of a reference to a 3GPP document (including a GSM document), a non-specific reference implicitly refers to the latest version of that document in the same Release as the present document.

[1]	3GPP TR 21.905: "Vocabulary for 3GPP Specifications".

[2]	3GPP TR 33.894, 2023 September, V18.0.0: "Study on applicability of the zero trust security principles in mobile networks", Release 18.

[3]	3GPP SP-231784, 'New Study on enablers for Zero Trust Security'.

*****End of Change 1*****

*****Start of Change 2*****

# 4	Security Assumptions

This section describes the potential security assumptions to be considered for the study specific to the Work Tasks (WT) [2]. The security aspects identified with respect to the zero trust security tenets in the context of the 5GC SBA in TR 33.894 [3] are still relevant and applicable for this study.

Assumption #1: Based on Work Task 1 (i.e., Data exposure for security evaluation and monitoring) the operator has deployed a security function (e.g., SIEM or SOAR).

- The Security function that performs the security evaluation and monitoring resides in the operator’s domain (i.e., external to the 3GPP network) and it is considered as a trusted entity. This security function and its application logic are upto the operator’s implementation, and it can be outside the scope of 3GPP.

Reuse existing network function such as NWDAF to expose the identified and collected data to the Operator’s Security Function.

Editor’s Note: Additional security assumption(s) (if any) related to ‘Data exposure for security evaluation and monitoring’ to be considered is FFS.

Assumption #2: For Work Task 2 (i.e., Security mechanism for dynamic policy enforcement), the dynamic security policy enforcement is configured and controlled by the operator based on operator’s policy.

NOTE: There may be a need to standardize how the operator’s Security Function (e.g., SIEM/SOAR) will be able to interface into the NF(s) to take action if any required is FFS for SA5.

Editor’s Note: The list of scenarios in SBA where dynamic security policy enforcement can address potential threat is FFS.

Editor’s Note: Which existing network function(s) is suitable to consume the results of Security evaluation and monitoring to apply dynamic security policy enforcement is FFS.

Editor’s Note: Additional aspects for security assumption(s) (if any) related to ‘Security mechanism for dynamic policy enforcement’ to be considered is FFS.

*****End of Change 2*****