3GPP TSG-SA3 Meeting #115	draft_S3-240336-r1

Athens, February 26 - March 01, 2024

# Source:	Lenovo, Motorola Mobility, AT&T, Charter Communications, Nokia, Nokia Shanghai Bell

# Title:	Data related to massive number of Service Messages

# Document for:	Approval

Agenda Item:	5.1

# 1	Decision/action requested

This pCR describes a potential data to be considered for data collection and exposure to clause 5.1.X of the TR 33.794.

# 2	References

[1]	3GPP SP-231784, 'New Study on enablers for Zero Trust Security'.

[2]	3GPP TR 33.794, 'New Study on enablers for Zero Trust Security', Release 19.

[3]	Enisa Threat Landscape For 5G Networks ENISA Threat Landscape For 5G Networks, 2020, https://www.enisa.europa.eu/publications/enisa-threat-landscape-report-for-5g-networks.

# 3	Rationale

Core SBA NF flooding can lead to Denial of Service in the core network [3] which clarifies that, Nefarious activity/abuse of assets, with flooding of core network components can cause Denial of service threat leading to potential impacts such as service unavailability, outage etc. The main affected asset in this case are the network services in the context of SBA. Therefore, this contribution proposes to consider the network service message flooding usecase to identify and expose related data to enable ‘Denial Service attempts identification’ for TR 33.794 [2] related to WT1 [1].

# 4	Detailed proposal

SA3 is kindly requested to agree the pCR below to TR 33.794.

*****Start of Change*****

### 5.1.X	Data exposure Use case #X: Massive number of SBI  Messages

#### 5.1.X.1	Description

A core SBA NF that receives a massive number of service API invocations that intends to exhaust the network resource may lead to degradation or complete shutdown of NF thus resulting in a Denial of Service (DoS). But there can be normal cases, where the service provider may still receive larger number of service requests (e.g., due to legitimate service need). Here it is important to identify if the massive number of service invocation is due to a legitimate service need or due to malicious attack attempt (like DoS or DDoS if multiple service consumer is observed to send massive number of service requests). Based on operator policy the NF can be configured with allowed maximum number of service requests/invocations for a service consumer in a normal case (e.g., for a time-period). If the number of service invocations by any service consumer exceeds this operator’s configured level, then it can be identified as flooding event and the related data can be collected, logged, and exposed to the operator’s security function to enable security evaluation and monitoring.

#### 5.1.X.2	Data to be exposed

The data to be exposed includes data on service requests exceeding preconfigured limits and the information on NF(s) identification (e.g., NF ID(s)) which attempted the massive number of service invocations.

Additional data which can be exposed:

Periodically collected security counters like below can be used to statistically evaluate the service message flows between NFs. If these counters are collected, these can be used to analyse possible DoS attacks with sources from external interfaces. The periodicity of such counter collections can be configurable.

- Number of times API invocations exceeded thresholds.

- NF IDs of top “N1” sources of API invocations (Example: N1=3, configurable)

- NF IDs of top “N2” recepients of API invocations (Example: N2=3, configurable)

*****End of Change*****