# 3GPP TSG-SA3 Meeting #115	draft_S3-240646-r1

# Athens, Greece, 26th February - 1st March 2024	revision of S3-240646, S3-240442, S3-240467,

# S3-240478, S3-240623, S3-240700, S3-240781, S3-240807, S3-240645, S3-240808

# Source:	CATT, China Telecomunication Corp., ZTE Corporation, OPPO, Intel Technology Poland SP Zoo, Samsung, Beijing Xiaomi Mobile Software, Nokia, Nokia Shanghai Bell

# Title:	pCR to TR33.700-29 New key issue for authentication and authorization in S&F Satellite Operation

Agenda Item:	5.7

# 1	Decision/action requested

Approve the pCR below

# 2	References

# 3		Rationale

Propose a new key issue for the authentication and authorization in Store and Forward Satellite Operation.

# 4	Detailed proposal

#### *** BEGIN CHANGES ***

# 2	References

The following documents contain provisions which, through reference in this text, constitute provisions of the present document.

-	References are either specific (identified by date of publication, edition number, version number, etc.) or non-specific.

-	For a specific reference, subsequent revisions do not apply.

-	For a non-specific reference, the latest version applies. In the case of a reference to a 3GPP document (including a GSM document), a non-specific reference implicitly refers to the latest version of that document in the same Release as the present document.

[1]	3GPP TR 21.905: "Vocabulary for 3GPP Specifications".

[i1]	3GPP TR 23.700-29: "Study on integration of satellite components in the 5G architecture Phase 3".

…

[x]	<doctype> <#>[ ([up to and including]{yyyy[-mm]|V<a[.b[.c]]>}[onwards])]: "<Title>".

#### *** NEXT CHANGE ***

## 5.X	Key issue #X: Authentication and authorization in Store and Forward Satellite Operation

### 5.X.1	Key issue details

In clause 4 of TR 23.700-29 [i1], there is following description about the Store and Forward Satellite Operation:

"The following architecture assumptions are applied to the study:

…

-	Store and Forward Satellite Operation assumes that UE-satellite-ground network connectivity can be intermittent as defined in clause 3.1.

-	Store and Forward Satellite Operation shall work without ISL.

…"

This means that the core network is unavailable when the satellite attempts to authenticate and authorize a UE in Store and Forward Satellite Operation.

From a security perspective, whether a UE can use Store and Forward Satellite service should be assured by the 3GPP system (satellite). On the contrary, whether the 3GPP system (satellite) can provide Store and Forward Satellite service should be assured by UE.

This key issue is to study the authentication, authorization, secure data transmission and privacy protection in Store and Forward Satellite Operation.

### 5.X.2	Security threats

An attacker may impersonate a UE. If the satellite is unable to verify whether the UE has been authenticated and authorized, the attackers can initiate many false data transmission requests to the satellite, thereby preventing the satellite from providing services to legitimate UEs, leading to a denial of service.

An attacker may impersonate a satellite. If the UE is unable to verify whether the satellite has been authenticated and authorized to provide store and forward services, the attacker can force the UE to camp on the fake satellite and send data to it. The attacker subsequently discards the data, resulting in a denial of service.

Attackers may manipulate the data transmitted between UE and satellites, thereby interfering with normal data communication.

Attackers may eavesdrop on the transmitted data and further use it for inappropriate purposes.

Attackers may replay intercepted data, thereby affecting the expected action state of data communication.

UE identification information can be used to track the UE, thus violating the UE's privacy information.

### 5.X.3	Potential security requirements

The 3GPP system shall support UE authentication and authorization in the Store and Forward Satellite Operation.

The 3GPP system shall support network authentication in the Store and Forward Satellite Operation.

The 3GPP system shall support means to provide confidentiality, integrity, and replay protection for user-plane and control-plane messages between UE and 3GPP system in the Store and Forward Satellite Operation.

The 3GPP system shall provide means for mitigating trackability and linkability attacks on the UE in the Store and Forward Satellite Operation.

#### *** END OF CHANGES ***