# 3GPP TSG-SA3 Meeting #115	draft_S3-240646-r6

# Athens, Greece, 26th February - 1st March 2024	revision of S3-240646, S3-240442, S3-240467,

# S3-240478, S3-240623, S3-240700, S3-240781, S3-240807, S3-240645, S3-240808, S3-240603

# Source:	CATT, China Telecomunication Corp., ZTE Corporation, OPPO, Intel Technology Poland SP Zoo, Samsung, Beijing Xiaomi Mobile Software, Nokia, Nokia Shanghai Bell, Ericsson

# Title:	pCR to TR33.700-29 New key issue for authentication and authorization in S&F Satellite Operation

Agenda Item:	5.7

# 1	Decision/action requested

Approve the pCR below

# 2	References

# 3		Rationale

Propose a new key issue for the authentication and authorization in Store and Forward Satellite Operation.

# 4	Detailed proposal

#### *** BEGIN CHANGES ***

# 2	References

The following documents contain provisions which, through reference in this text, constitute provisions of the present document.

-	References are either specific (identified by date of publication, edition number, version number, etc.) or non-specific.

-	For a specific reference, subsequent revisions do not apply.

-	For a non-specific reference, the latest version applies. In the case of a reference to a 3GPP document (including a GSM document), a non-specific reference implicitly refers to the latest version of that document in the same Release as the present document.

[1]	3GPP TR 21.905: "Vocabulary for 3GPP Specifications".

[i1]	3GPP TR 23.700-29: "Study on integration of satellite components in the 5G architecture Phase 3".

…

[x]	<doctype> <#>[ ([up to and including]{yyyy[-mm]|V<a[.b[.c]]>}[onwards])]: "<Title>".

#### *** NEXT CHANGE ***

## 5.X	Key issue #X: Authentication and authorization in Store and Forward Satellite Operation

### 5.X.1	Key issue details

In clause 4 of TR 23.700-29 [i1], there is following description about the Store and Forward Satellite Operation:

"The following architecture assumptions are applied to the study:

…

-	Store and Forward Satellite Operation assumes that UE-satellite-ground network connectivity can be intermittent as defined in clause 3.1.

-	Store and Forward Satellite Operation shall work without ISL.

…"

From a security perspective, whether a UE can use Store and Forward Satellite service should be assured by the 3GPP system (On the contrary, whether the 3GPP system  can provide Store and Forward (S&F) Satellite service should be assured by UE.

In S&F satellite operations, architectural assumption is that the UE-satellite-ground network connectivity is intermittent. It is assumed that a service link connection between the UE-satellite is available and stable. This implies that the satellite-ground feeder link connection between the satellite and the ground network is intermittent.

S&F satellite operational mode is relevant for delay tolerant and non-real time communications via LEO/MEO space segment. This implies that S&F is not relevant for delay intolerant communications.

3GPP Network Functions and/or Network Elements which are located on a satellite may communicate with the ground infrastructure of 3GPP system over an intermittently available feeder link connection between the satellite and the ground network.

During the feeder link’s intermittent unavailability, the following risks arise.

1.	The EPS/5G AKA procedure may not get fully completed or is partially completed. It results into incomplete procedure for  authentication procedure between the network and the UE.

2.	The Security Mode Command (SMC) procedure for Non-Access Stratum (NAS) may not fully complete because the NAS connection between UE and MME/AMF may have been interrupted. In turn it results into incomplete security capabilities negotiation between the UE and the EPS/5GC network.

This key issue is to study the authentication, authorization, risks to data security in Store and Forward Satellite Operation.

### 5.X.2	Security threats

An attacker may impersonate a UE. If the 3GPP system is unable to verify whether the UE has been authenticated and authorized in Store and Forward Satellite service, the attackers can initiate many false data transmission requests to the 3GPP system, thereby preventing the 3GPP system from providing Store and Forward Satellite services to legitimate UEs, leading to a denial of service.

An attacker may impersonate a 3GPP system. If the UE is unable to verify whether the 3GPP system has been authenticated and authorized to provide store and forward services, the attacker can force the UE to camp on the fake 3GPP system and send data to it. The attacker subsequently discards the data, resulting in a denial of service.

Attackers may manipulate the data transmitted between UE and 3GPP system in Store and Forward Satellite service, thereby interfering with normal data communication.

Attackers may eavesdrop on the transmitted data and further use it for inappropriate purposes.

Attackers may replay intercepted data, thereby affecting the expected action state of data communication.

### 5.X.3	Potential security requirements

The EPS shall support authentication procedure between UE and EPS in the case of NTN Store and Forward architecture for NB-IoT.

The 3GPP system shall support means to provide confidentiality, integrity, and replay protection for user-plane and control-plane messages between UE and 3GPP system in the Store and Forward Satellite Operation.

#### *** NEXT CHANGE ***

## 5.X	Key issue #X: Privacy aspects in Store and Forward Satellite Operation

### 5.X.1	Key issue details

In clause 4 of TR 23.700-29 [i1], there is following description about the Store and Forward Satellite Operation:

"The following architecture assumptions are applied to the study:

…

-	Store and Forward Satellite Operation assumes that UE-satellite-ground network connectivity can be intermittent as defined in clause 3.1.

-	Store and Forward Satellite Operation shall work without ISL.

…"

In S&F satellite operations, architectural assumption is that the UE-satellite-ground network connectivity is intermittent. It is assumed that a service link of the UE-satellite is available and stable. S&F satellite operational mode is relevant for delay tolerant and non-real time communications via LEO/MEO space segment. For UE to avail delay tolerant and non-real time communications, the NTN payload comprising 3GPP Network Functions/Network Elements communicates with the ground infrastructure of 3GPP network over an intermittently available feeder link.

This key issue is to study the privacy aspects related to data exchanged between UE and 3GPP system in Store and Forward Satellite Operation.

### 5.X.2	Security threats

UE identification information can be used to track the UE, thus violating the UE's privacy information.

### 5.X.3	Potential security requirements

The 3GPP system shall provide means for mitigating trackability and linkability attacks on the UE in the Store and Forward Satellite Operation.

#### *** END OF CHANGES ***

# Comments

[Ericsson] SA3 cannot make such assertion about unavailability of core network. Only assumption SA3 can take is captured in architectural assumptions in 23.700-29. The assumption that applies is that ground connectivity is intermittent. It may or may not result into disconnect with core, because if subset of core NF are onboard satellite, then core is available. I have inserted text to 'generalize' that ground connectivity is intermittent (without referring to core).

5G NTN is not authenticating/authorizing satellites, but the NTN payload (3GPP NF)

Should we split privacy in a separate Key Issue ? It maybe good to have clarity in the KI-solution mapping.