3GPP TSG-SA3 Meeting #115 	draft-S3-240809-r1

Athens, Greece, 26 Feb - 01 March 2024

Source:	                       Nokia, Nokia Shanghai Bell, Philips International B.V., Lenovo

Title:	Key issue on secured information exchange at satellite level(UE-SAT-UE)

Document for:	Approval

Agenda Item:	5.7

# 1	Decision/action requested

It is proposed to approve the key issue

# 2	References

[1]	S3-235103 New SID on study on security Aspects of 5G Satellite Access.

[2]	TS 33.501 Security architecture and procedures for 5G system.

[3]             TS 23.501 System architecture for the 5GS system.

[4]             TS 23.502 Procedure for the 5G system(5GS).

# 3	Rationale

Current 5G 3gpp security specification [2][3][4] describes the architectural and security flows by adapting the NR satellite access to existing different 5GS procedures.

One of the objectives from Rel-19 study S3-235103[1] is to study the impacts to the current 5GS system when supporting mechanishm to authorize the UE -Satellite – UE communication enhancements in existing deployments without feeder links to Gateway or to the core network, there is service continuity. Below key issue proposes to study this further related to security and privacy issues.

# 4	Detailed proposal

*** 1st CHANGE ***

## X.1	Key issue # X: Security and Privacy for UE-Satellite-UE communication

### X.1.1	Key issue details

UE-satellite-UE communication refers to the communication between UEs (roaming as well as home UEs) under the coverage of one or more serving satellites without the user plane traffic going through the ground network. It is expected that a link to the ground, via ISL to another satellite with a link to a ground gateway, or via multiple other satellites using ISLs to another satellite with a link to ground gateway or direct from the serving satellite to a ground gateway, is always available.

SA2 is studying the potential architectural enhancements to support UE-satellite-UE communication, including minimum necessary set of 5GC network functions and IMS components (if any) onboard the satellite(s), including:

- How to ensure routing of user plane traffic (for MMTEL and MC applications) remains in the satellite

- Potential impacts on IMS procedures and functions to manage UE-satellite-UE communication

The SA2 TR discussed three different options of UE-Satellite-UE communication for multimedia telephony services over IMS, in all cases the control signalling path is going over the IMS in the mobile network on the ground:

- Both UEs are in the same cell, media path is switched at the satellite,

- Both UEs are in the same cell, media path is switched between two or more satellites via Inter Satellite link(s),

- Both UEs are in different cells, media path is switched between two or more satellites via Inter Satellite link(s).

It must be assured that the media is not accessible with respect to spoofing of the UE to Satellite communication and that the media is not hijacked to a malicious 3rd party UE.

From SA3 point of view, the 3GPP system needs to be able to ensure the protection (i.e., confidentiality, integrity, and replay protection) of information exchanged between peer UEs and/or between UEs and satellite. Failure to protect the confidentiality and integrity of the exchanged information can compromise the 5GS and make it vulnerable to several attacks such as impersonation attack, unauthorized disclosure, and modification of information, etc.

### X.1.2	Threats

If the IMS communication is not confidentiality and replay protected, an attacker may eavesdrop on the communication and the exchanged privacy sensitive parameters (e.g., identifiers) and/or replay messages exchanged between UEs and/or between UEs and satellite.

Failure to protect the integrity of information exchanged between peer UEs and/or between UEs and satellite can make the 5GS vulnerable against unauthorized modification of information.

### X.1.3	Potential security requirements

The 3GPP system shall support a means to provide confidentiality, integrity, and replay protection for information exchanged between UEs over satellite.

The 3GPP system shall provide means to protect the privacy sensitive information of peer UEs during UE-satellite-UE communication.

*** END OF 1st CHANGE***