3GPP TSG-SA3 Meeting #115	draft_S3-240898-r1 was S3-240334-r1

Athens, February 26 - March 01, 2024

# Source:	Lenovo, Motorola Mobility, AT&T, Charter Communications, Johns Hopkins University APL

# Title:	Security Assumptions for TR 33.794

# Document for:	Approval

Agenda Item:	5.1

# 1	Decision/action requested

This pCR proposes security assumptions to be considered for the TR 33.794.

# 2	References

[1]	3GPP SP-231784, 'New Study on enablers for Zero Trust Security'.

[2]	3GPP TR 33.794, 'New Study on enablers for Zero Trust Security', Release 19.

[3]	3GPP TR 33.894, ''Study on applicability of the zero trust security principles in mobile networks'', Release 18.

# 3	Rationale

This contribution provides security assumptions related to WT1 and WT2 [1] to be considered for the study [2] based on the progress of the security analysis and findings from TR 33.894 [3].

# 4	Detailed proposal

SA3 is kindly requested to agree the pCR below to TR 33.794.

*****Start of Change 1*****

# 2	References

The following documents contain provisions which, through reference in this text, constitute provisions of the present document.

-	References are either specific (identified by date of publication, edition number, version number, etc.) or non-specific.

-	For a specific reference, subsequent revisions do not apply.

-	For a non-specific reference, the latest version applies. In the case of a reference to a 3GPP document (including a GSM document), a non-specific reference implicitly refers to the latest version of that document in the same Release as the present document.

[1]	3GPP TR 21.905: "Vocabulary for 3GPP Specifications".

[2]	3GPP TR 33.894, 2023 September, V18.0.0: "Study on applicability of the zero trust security principles in mobile networks", Release 18.

[3]	3GPP SP-231784, 'New Study on enablers for Zero Trust Security'.

*****End of Change 1*****

*****Start of Change 2*****

# 4	Security Assumptions

This section describes the potential security assumptions to be considered for the study specific to the objectives[2]. The security aspects identified with respect to the zero trust security tenets in the context of the 5GC SBA in TR 33.894 [3] are still relevant and applicable for this study.

Assumption #1: Based on Objective 1 (i.e., Data exposure for security evaluation and monitoring) the operator has deployed a Security Function.

- The Security function that performs the security evaluation and monitoring resides in the operator’s domain (i.e., external to the 3GPP network) and it is considered as a trusted entity. This Security function and its application logic are upto the operator’s implementation, and it can be outside the scope of 3GPP.

Editor’s Note:  Reusing existing network function such as NWDAF to expose the identified and collected data to the Operator’s Security function is FFS.

Assumption #2: For Objective 2 (i.e., Security mechanism for dynamic policy enforcement), the dynamic security policy enforcement is configured and controlled by the operator based on operator’s policy.

Editor’s Note: Which existing network function(s) is suitable to consume the results of Security evaluation and monitoring to apply dynamic security policy enforcement is FFS.

*****End of Change 2*****