3GPP TSG-SA3 Meeting #115	draft_S3-240903-r2

Athens, February 26 - March 01, 2024											revision of S3-240335

# Source:	Lenovo, Motorola Mobility, AT&T, Charter Communications, Johns Hopkins University APL

# Title:	Scope for TR 33.794

# Document for:	Data related to Malformed Message

Agenda Item:	5.1

# 1	Decision/action requested

This pCR describes a potential data to be considered for data collection and exposure to clause 5.1.X of the TR 33.794.

# 2	References

[1]	3GPP SP-231784, 'New Study on enablers for Zero Trust Security'.

[2]	3GPP TR 33.794, 'New Study on enablers for Zero Trust Security', Release 19.

[3]	3GPP TR 33.894, ''Study on applicability of the zero trust security principles in mobile networks'', Release 18.

[4]	3GPP TS 33.501, ''Security architecture and procedures for 5G system''.

[5]	Enisa Threat Landscape For 5G Networks ENISA Threat Landscape For 5G Networks, 2020, https://www.enisa.europa.eu/publications/enisa-threat-landscape-report-for-5g-networks.

[6] 	CrashNRF, https://github.com/IdahoLabResearch/5GAD?tab=readme-ov-file#crashnrf.

[7]	Malformed Message based attack, Security for 5G, Tel Aviv University, https://www.dspcsp.com/tau/5G/11-security.pdf.

[8]	AMF crash with malformed message, ''https://github.com/free5gc/free5gc/issues/198''.

# 3	Rationale

Sending malformed messages to NF has the potential to crash the NFs [5,6,7,8] as elaborated with NRF crash [6] and AMF crash [8] examples. TS 33.501 in different scenarios other than SBA, has already considered the issue of malformed messages into account and has a limited standard way of handling malformed message such as the references listed below.

TS 33.501, Clause 5.9.3.2, states, ‘The SEPP shall discard malformed N32 signaling messages.’.

TS 33.501, Clause 5.9.3.4, states, ‘The IPUPS shall discard malformed GTP-U messages.’.

In case of SBA, malformed messages received over SBI can have the potential adverse effect to the receiving NFs (e.g., a malformed message sent with to malicious intentions  could result in a security exploit (e.g., with buffer overflow, malicious code execution etc.)). Meanwhile simply dropping the malformed message cannot help to identify the potential threats and context i.e., which NF sends the malformed message and why does it send such a malformed message, which services it is targeting, and so on. Therefore, this pCR propose (for TR 33.794 [2], related to WT1 [1]) to collect the event data on malformed message  received by a NF over SBI, log it, and to expose the malformed message event data (e.g., information on the occurrence of malformed message recepetion) to the operator security function (e.g., SIEM/SOAR) to enable the security evaluation and monitoring process.

# 4	Detailed proposal

SA3 is kindly requested to agree the pCR below to TR 33.794.

*****Start of Change*****

### 5.1.X	Data exposure Use case #X: Information on Malformed Message

#### 5.1.X.1	Description

Malformed messages (i.e., SBI message violations) may be received by a NF over an SBI from another NF (e.g., due to malicious intentions or due to mere error). The malformed message(s) sent with malicious intentions have the potential to cause failure/malfunction of NF(s). In various other cases there are requirements to handle such malformed message(s) (such as in TS 33.501, Clause 5.9.3.2, states, ‘The SEPP shall discard malformed N32 signaling messages’, and Clause 5.9.3.4, states, ‘The IPUPS shall discard malformed GTP-U messages’). In the case of SBA, simply dropping a malformed message cannot help to identify the threat surface and its context i.e., which NF sends the malformed message and why does it send such a malformed message, which services it is targeting, etc. Identifying the potential threat rather than dropping the malformed message(s) can prevent further attacks on the rest of the network (e.g., another NF).3GPP specified service-based interface message inputs and outputs described in TS 29.500 can be considered as normal messages. If a Service based interface message violates the specified input or output (i.e., SBI message violation), that message can be considered as malformed message and the related event data can be collected, logged, and exposed (based on operator policy) to the Operator’s security function residing external to the 3GPP network to enable security evaluation and monitoring.

Editor's Note: The additional definition of malformed messages if any needed is FFS

Editor's Note:

#### 5.1.X.2	Data to be exposed

The data relevant to be exposed includes event data on the received malformed message, and the NF identification information (e.g., NF ID) of the sender of the malformed message.

Editor’s Note: For this usecase, exactly which data are exposed is FFS.

*****End of Change*****

# Comments

Needs to be adapted to the new skeleton

Let us see the stable skeleton

This is a bit misleading and gives the impression that dropping such messages is not a good security practice. EN on this part of the justification needs to be reformulated

That's not intended, stage 3 is cited to consider on what is correctly formed and what is different than the 3GPP specified format is malformed. Please also check TS 33.501 on current usage of malformed message, currently let us not deviate much beyond 3GPP scope. If you want to have a placeholder still, I tried to reformulate.

The actual information which relevant for identifying the NF and its intention could be also tampered with/malformed. EN on the definition of malformed messages.

Post successful TLS mutual auth, the id of NF will be available.

Not relevant, please see TS 33.501, currently there is no mitigation available for SBA internal interactions. If you think, there is a mitigation step available, kindly share the TS 33.501 reference? We can add that too! Further like said several time, dropping is good, but that is not sufficient, please look into the T4,5,6, and 7 evaluations.