# 3GPP TSG-SA3 Meeting #115	draft_S3-240934-r17

# Athens, Greece, 26th February - 1st March 2024	revision of S3-240646, S3-240442, S3-240467,

# S3-240478, S3-240623, S3-240700, S3-240781, S3-240807, S3-240645, S3-240808, S3-240603

# Source:	CATT, China Telecommunication Corp., ZTE Corporation, OPPO, Intel Technology Poland SP Zoo, Samsung, Beijing Xiaomi Mobile Software, Nokia, Nokia Shanghai Bell, Ericsson, Interdigital

# Title:	pCR to TR33.700-29 New key issue for security protection in S&F Satellite Operation

Agenda Item:	5.7

# 1	Decision/action requested

Approve the pCR below

# 2	References

# 3		Rationale

Propose a new key issue for the authentication and authorization in Store and Forward Satellite Operation.

# 4	Detailed proposal

#### *** BEGIN CHANGES ***

# 2	References

The following documents contain provisions which, through reference in this text, constitute provisions of the present document.

-	References are either specific (identified by date of publication, edition number, version number, etc.) or non-specific.

-	For a specific reference, subsequent revisions do not apply.

-	For a non-specific reference, the latest version applies. In the case of a reference to a 3GPP document (including a GSM document), a non-specific reference implicitly refers to the latest version of that document in the same Release as the present document.

[1]	3GPP TR 21.905: "Vocabulary for 3GPP Specifications".

[i1]	3GPP TR 23.700-29: "Study on integration of satellite components in the 5G architecture Phase 3".

…

[x]	<doctype> <#>[ ([up to and including]{yyyy[-mm]|V<a[.b[.c]]>}[onwards])]: "<Title>".

#### *** NEXT CHANGE ***

## 5.X	Key issue #X: Security Protection in Store and Forward Satellite Operation

### 5.X.1	Key issue details

In clause 4 of TR 23.700-29 [i1], there is following description about the Store and Forward Satellite Operation:

"The following architecture assumptions are applied to the study:

…

-	Store and Forward Satellite Operation assumes that UE-satellite-ground network connectivity can be intermittent as defined in clause 3.1.

-	Store and Forward Satellite Operation shall work without ISL.

…"

From a security perspective, whether a UE can use Store and Forward Satellite service should be assured by the 3GPP network.

In S&F satellite operations, architectural assumption is that the UE-satellite-ground network connectivity is intermittent. 3GPP Network Functions and/or Network Elements which are located on a satellite may communicate with the ground infrastructure of 3GPP network over an intermittently available feeder link connection between the satellite and the ground network. S&F satellite operational mode is relevant for delay tolerant and non-real time communications via LEO/MEO space segment.

During the feeder link’s intermittent unavailability, the following risks arise.

1.	The EPS/5G AKA procedure may not get fully completed or is partially completed. It results into incomplete procedure for mutual authentication between the network and the UE.

2.	The Security Mode Command (SMC) procedure for Non-Access Stratum (NAS) may not fully complete because the NAS connection between UE and MME/AMF may have been interrupted. In turn it results into incomplete security capabilities negotiation between the UE and the EPS/5GC network.

This key issue is to study the authentication, authorization and data security in Store and Forward Satellite Operation.

### 5.X.2	Security threats

Editor’s Note: the feasibility of the denial of service (i.e. caused by false user-plane data or control-plane data) is FFS.

Editor’s Note: whether the availability issue is a security threat is FFS.

Editor’s note: The risk of resource depletion of 3GPP system due to UE's incomplete AKA procedure is dependent on agreed architecture solution direction of S&F KI in SA2.

Due to the nature of the S&F mode during the feeder link’s intermittent unavailability, the following threats can manifest themselves:

- When the UE and 3GPP network cannot mutually authenticate, such condition may cause availability issue.

- Without the authentication, confidentiality, integrity, and anti-replay protection there will be no security protection of the communication between UE, on board satellite 3GPP systems and ground-based 3GPP systems.

### 5.X.3	Potential security requirements

The 3GPP system shall support mutual authentication between the UE and the 3GPP network in the Store and Forward Satellite Operation.

The 3GPP system shall support means to provide confidentiality, integrity, and anti-replay protection for user-plane and control-plane messages between UE and the 3GPP network in the Store and Forward Satellite Operation.

Editor’s Note: whether there are more security requirements is FFS.

#### *** END OF CHANGES ***

# Comments

This statement is not needed because of previous statement. Redundant.

3GPP systems on-board satellite, ground-based 3GPP systems, and UE are in scope of 3GPP "trust model". Endpoints are still 3GPP and UE, not satellite (vehicle, control bus).

This is not an impersonation, but rather an unauthenticated DOS attack on mobile service availability. Unauthenticated UE cannot by definition impersonate anything.

How can the attacker impersonate a satellite?

It is hard to imagine that without AKA and SMC completion there could be any registration and transmission of data. The described attack won’t be possible.

Without AKA and SMC completion there won’t be any registration and transmission of data. The described attack won’t be possible.

Without AKA and SMC completion there won’t be any registration and transmission of data. The described attack won’t be possible.

Covered already by EN that says "whether there are more security threats is FFS."

Without AKA and SMC completion there won’t be any registration and transmission of data. The described attack won’t be possible.

Without AKA and SMC completion there won’t be any registration and transmission of data. The described attack won’t be possible.