3GPP TSG-SA3 Meeting #115 	S3-240944

Athens, Greece, 26th February - 1st March 2024                        is revision of S3-240716

# Source:	China Mobile, Ericsson, Nokia, Nokia Shanghai Bell

# Title:	Key issue of third party specific user identities

# Document for:	Approval

Agenda Item:	5.2

# 1	Decision/action requested

This contribution is the proposal of the key issue of third party specific user identities.

# 2	References

[1]	3GPP TR 23.700-77: "Study on system architecture for next generation real time communication services; Phase 2".

# 3	Rationale

This contribution is the proposal of the key issue of the third party specific user identities.

# 4	Detailed proposal

**** START of 1st CHANGE ****

## 5.1	Key issue #1: Third party specific user identities

### 5.1.1	Key issue details

According to TR 23.700-77 [X], there are scenarios that the third party subscribers use third party IDs (e.g., enterprise employee ID, IMS avatar id, etc). The IMS network can present the third party ID to the callee during subsequent calling process. The third party subscriber can access the IMS network directly or via a SIP trunk as well.

From the security point of view, the enhanced IMS network shall be able to support the identity verification and authorization of third-party user during an IMS call.

### 5.1.2	Threats

A malicious UE can use IDs belonging to others or forged IDs to initiate IMS calls in the IMS network;

A malicious UE can use an ID that no longer belongs to it to initiate IMS calls in the IMS network (e.g., the user use the ID allocated by a particular company even after leaving it).

The ID's transfer between IMS networks may be manipulated by intermediary network entities. Consequently, the callee may receive a wrong ID.

### 5.1.3	Potential security requirements

The IMS system shall be able to coordinate with the third party to verify and authorize the third-party specific user identities.

The IMS network shall be able to support the integrity protection of the third-party specific user identities on the originating side and terminating side.

Editor’s Note: The KI may be updated according to SA2’s progress.

**** END of 1st CHANGE ****

**** START of 2nd CHANGE ****

# 2	References

The following documents contain provisions which, through reference in this text, constitute provisions of the present document.

-	References are either specific (identified by date of publication, edition number, version number, etc.) or non-specific.

-	For a specific reference, subsequent revisions do not apply.

-	For a non-specific reference, the latest version applies. In the case of a reference to a 3GPP document (including a GSM document), a non-specific reference implicitly refers to the latest version of that document in the same Release as the present document.

[1]	3GPP TR 21.905: "Vocabulary for 3GPP Specifications".

[X]	3GPP TR 23.700-77: ""Study on system architecture for next generation real time communication services - phase 2".

**** END of 2nd CHANGE ****