3GPP TSG-SA3 Meeting #116	S3-241805r1

Jeju, South Korea,  20th - 24th May 2024

# Source:	Nokia

# Title:	pCR on conclusion for KI2

# Document for:	Approval

Agenda Item:	5.8

# 1	Decision/action requested

It is requested to approve the chapter 4 content.

# 2	References

[x] 3GPP TR 33.702: "Study on Security for mobility over non-3GPP access to avoid full primary authentication."

# 3	Rationale

# 4	Detailed proposal

**** START OF CHANGE ****

# 7	Conclusions

Editor’s Note: This clause contains the agreed conclusions that will form the basis for any normative work.

## 7.x	Key issue #2: Security aspect of AUN3 device connecting to a new 5G-RG within the same W-AGF.

The following conclusion is applicable:

- AMF and AUN3 device derive the same temporary number independently, which can be used by AUN3 device to connect to the next RG.

- AUN3 device and AMF, via the target RG, authenticate each other via this temporary number and optionally message exchange between them.

- AUN3 device and AMF derive the target RG keys and secure the communication.

**** END OF CHANGE ****