3GPP TSG-SA3 Meeting #116	draft_S3-242133-r1

Jeju, South Korea,  20th - 24th May 2024

# Source:	Xiaomi

# Title:	33.700-32: Update to Key Issue #3

# Document for:	Approval

Agenda Item:	5.10

# 1	Decision/action requested

SA3 is kindly asked to approve the update to key issue #3 in TR 33.700-32.

# 2	References

[1]	3GPP TR 23.700-32 v0.3.0	Study on User Identities and Authentication Architecture

[2]	3GPP TR 33.700-32 v0.1.0	Study on security aspects of User Identities and Authentication

# 3	Rationale

According to TR 23.700-32 [1] clause 5.4.1, non-3GPP devices behind one gateway UE or 5G-RG need to be identifiable to the network, so that the traffic to/from the UE or 5G-RG associated with the non-3GPP devices can be controlled and charged individually by the network operator. The network uses the non-3GPP device identifier defined in TR 33.700-32 [2] to identify a non-3GPP device, while the non-3GPP device uses only the subscription of the gateway UE or 5G-RG to access the 5GC as per TR 23.700-32 [1]. It means that the access level authentication of the non-3GPP device is based on UE subscription identifier rather than the non-3GPP device identifier, and only the gateway UE or 5G-RG is visible to the network. To make the non-3GPP device behind the gateway UE or 5G-RG visible to the network and identifiable, the non-3GPP device identifier defined in TR 33.700-32 [2] and corresponding credential need to be used by the network to ensure the authenticity of the identified device.

The current definition of non-3GPP device identifier does not reflect its usage. There could be multiple identifiers in a non-3GPP device used for different purposes. Current definition does not clarify for what purpose the identifier is used by the network. Without such clarification, it is unclear how the identifier is used in the study.

This pCR proposes to update the corresponding definition in TR 33.700-32 [2].

# 4	Detailed proposal

*************** Start of the 1st Change ****************

## 3.1	Terms

For the purposes of the present document, the terms given in 3GPP TR 21.905 [1], TR 23.700-32 [2], and the following apply. A term defined in the present document takes precedence over the definition of the same term, if any, in 3GPP TR 21.905 [1].

Non-3GPP device identifier: an identifier of a non-3GPP device connecting to network via a UE or 5G-RG. It is used by the network to identify the non-3GPP device for controlling and charging the traffic of the non-3GPP devices to/from the connected UE or 5G-RG. It is also used for the network to ensure the authenticity of the identified non-3GPP devices.

Editor’s Note: the non-3GPP device identifier and user identifier may be updated according to the progress in TR 23.700-32 [2].

*************** End of the Change ****************