3GPP TSG-SA3 Meeting #116	draft_S3-242319-r1

Jeju, South Korea,  20th - 24th May 2024

# Source:	Xiaomi

# Title:	New sol for KI#2_User plane data protection mechanism between UE and UPF

# Document for:	Approval

Agenda Item:	5.15

# 1	Decision/action requested

It is proposed to approve this pCR.

# 2	References

[1]	3GPP TR 33.754 Study on security aspects for Multi-Access(DualSteer + ATSSS Ph-4)

# 3	Rationale

It is proposed to approve the new solution for key issue#2.

# 4	Detailed proposal

*** Start of the 1st Change ***

## 6.Y	Solution #Y: User plane data protection mechanism between UE and UPF

### 6.Y.1	Introduction

This solution addresses KI#2.

TLS embedded in MPQUIC [X]  is used to protect the user plane data between UE and the UPF.

### 6.Y.2	Solution details

When MPQUIC is used, TLS embedded in MPQUIC [X] is used to provide integrity protection, replay protection and confidentiality protection for the user plane data protection between the UE and the UPF.

### 6.Y.3	Evaluation

TBA

*** Start of the 2nd Change ***

# 2	References

The following documents contain provisions which, through reference in this text, constitute provisions of the present document.

-	References are either specific (identified by date of publication, edition number, version number, etc.) or non-specific.

-	For a specific reference, subsequent revisions do not apply.

-	For a non-specific reference, the latest version applies. In the case of a reference to a 3GPP document (including a GSM document), a non-specific reference implicitly refers to the latest version of that document in the same Release as the present document.

[1]	3GPP TR 21.905: "Vocabulary for 3GPP Specifications".

[2]	3GPP TR 23.700-54 "Study on Multi-Access (DualSteer and ATSSS_Ph4)".

[3]		     3GPP TS 33.501: " Security architecture and procedures for 5G system"

[4]	3GPP TS 23.501: "System architecture for the 5G System (5GS) "

[X]	RFC 9001: "Using TLS to Secure QUIC"

*** End of Changes ***