3GPP TSG-SA3 Meeting #116	draft_S3-242540-r1

Jeju, South Korea,  20th - 24th May 2024

# Source:	ZTE

# Title:	New solution for KI#2

# Document for:	Approval

Agenda Item:	5.9

# 1	Decision/action requested

This contribution proposes to add a new solution for KI#2 Authorization for 5G Ambient IoT services

# 2	References

# 3	Rationale

The contribution proposes to add a new solution for KI#2 Authorization for 5G Ambient IoT services.

# 4	Detailed proposal

It is suggested to approve the following change.

*************** Start of the change ****************

## 6.Y	Solution #Y:PCF based Service Authorization and Provisioning to UE

### 6.Y.1	Introduction

This solution address the KI#2 Authorization for 5G Ambient IoT services.

### 6.Y.2	Solution details

This solution propose to reuse the existing mechanism for 5G Prose U2N relay as specified in TS 23.304[x] with following changes:

A UE acting as an intermediate node is registered with 5GC using the existing mechanism, with some enhancements to indicate its capability of acting as an intermediate node, and is authorized as an intermediate node (UE) during the registration procedure.

For PCF based Service Authorization and Provisioning to UE, the Registration procedures as defined in clause 4.2.2.2 of TS 23.502 [x], UE Policy Association Establishment procedure as defined in clause 4.16.11 of TS 23.502 [x] and UE Policy Association Modification procedure as defined in clause 4.16.12 of TS 23.502 [x] apply with the following additions:

-	If the UE indicates AIoT Capability in the Registration Request message and if the UE is authorized to use 5G AIoT service based on subscription data, the AMF selects the PCF which supports AIoT Policy/Parameter provisioning and establishes a UE policy association with the PCF for AIoT Policy/Parameter delivery.The AMF reports the authorized AIoT Capability to the selected PCF, which may determine the AIoT Policy/Parameter based on the UE's authorized AIoT Capability.

### Editor’s Note: it is FFS which 5G NF performs the authorization of the intermediate UE and this needs to align with SA2 6.Y.3	Evaluation

TBD

*************** End of the change ****************