# 3GPP TSG-SA3 Meeting #116	draft_S3-242593-r1

# Jeju, South Korea,  20th - 24th May 2024	revision of S3-242088

# Source:	vivo

# Title:	New solution to KI3 privacy of data and sample alignment

Document for:	Approval

Agenda Item:	5.13

# 1	Decision/action requested

Approve the pCR on new solution of key issue#3.

# 2	References

# 3		Rationale

This contribution proposes a new solution to address  the key issue #3 “Privacy of VFL between VFL members”.

The solution proposes to use NEF to do sample alignment so that the external AF will not know internal sample ID list.

Please note that the plantUML code of the figure could run in https://www.plantuml.com/

# 4	Detailed proposals

Start of Change

## 6.Y	Solution #Y: Privacy of data and sample alignment

## 6.Y.1	Introduction

The solution addresses the key issue #3 “Privacy of VFL between VFL members”.

The solution proposes to use NEF to do sample alignment so that the external AF will not know internal sample ID list.

### 6.Y.2	Solution details

Figure 6.Y.2-1 Procedure of Privacy of data and sample alignment

- VFL Server has already completed VFL clients discovery.

NOTE:	Authorization procedure of VFL clients discovery is not in scope of this solution.

- VFL Sever sends Sample alignment request including its sample ID list 1 to NEF, the sample ID list contain UE ID list (e.g. SUPI, GPSI).

- NEF sends Sample alignment request to the VFL clients in the same VFL group.

- VFL Clients reply Sample alignment response to the NEF. The Sample alignment response includes sample ID list 2 and 3.

- The NEF determines the common sample ID list 4 based on the common part of all the sample ID list from VFL Server and Clients. In case of AF as VFL server, the NEF may do ID conversion to translate GPSI to SUPI through UDM. In case of NWDAF as VFL server, the NEF may do ID conversion to translate SUPI to GPSI through UDM.

- The NEF sends notify message to VFL server and clients including the common sample ID list 4.

Editor’s Note: Which entity will do sample alignment is ffs and will be based on SA2’s progress.

### 6.Y.3	Evaluation

The solution addresses the key issue #3.

The solution proposes to use NEF to do sample alignment so that the external AF will not know internal sample ID list.

End of Change