3GPP TSG-SA3 Meeting #116	draft_S3-242614-r1

Jeju, Korea  20 - 24 May 2024                                revision of S3-242075

# Source:	China Telecom

# Title:	New Solution for KI #3 of TR 33.700-32

# Document for:	Approval

Agenda Item:	5.10

# 1	Decision/action requested

This contribution propose a new solution to address the KI#3 of TR 33.700-32.

# 2	References

[1]	3GPP TR 33.700-32: " Study on security aspects of User Identities and Authentication".

# 3	Rationale

This contribution propose a new solution to address the KI#3 of TR 33.700-32, i.e. Authentication and Authorization of one or more non-3GPP devices behind one gateway UE or 5G-RG.

# 4	Detailed proposal

It is suggested to approve the following change.

*************** Start of the change ****************

## 6.Y	Solution #Y: Authentication and Authorization procedure of N3D behind gateway UE or 5G-RG

### 6.Y.1	Introduction

This solution addresses the Key Issue #3 (as defined in clause 5.3) .

This solution proposes to support the authentication and authorization of one or more Non-3GPP Device behind gateway UE or 5G-RG by enhancing the EAP based authentication procedure by an external DN-AAA server as specified in clause 11.1 of TS 33.501 [X] . It is assume there is a Non-3GPP deviece profile stored in Core network, e.g. UDM.

Editor’s Note: Whether this solution alignment with SA2 conclusions is ffs.

### 6.Y.2	Authentication Procedure

The authentication and authorization procedure of Non-3GPP Device behind gateway UE or 5G-RG as follow:

Figure 6.Y.2-1 Authentication and Authorization procedure of Non-3GPP Device behind gateway UE or 5G-RG

0. The UE/5G-RG registers with the network performing primary authentication.

1. The Non-3GPP Device and the UE/5G-RG successfully established direct connection.

NOTE 1: How to establish direct connection is out of 3GPP scope.

2. During direct connection establishment procedure, the UE/5G-RG identify the Non-3GPP Device and confirm its Non-3GPP Device identifier.

NOTE 2: How to identify a Non-3GPP Device based will be specified by SA2.

3. The UE/5G-RG send a PDU Session Establishment or Modification Request to SMF via AMF, which contains the Non-3GPP Device identifier confirmed in step 2.

4. Upon receiving the PDU Session Establishment or Modification Request message, the SMF shall obtains the subscription data of the UE/5G-RG and the profile of the Non-3GPP Deivce from the UDM. The SMF shall checks the subscription data whether the secondary authentication for UE/5G-RG as specified in clause 11.1 of TS 33.501 [X] is required, and whether the UE/5G-RG is allowed to provide current service, and check the profile of the Non-3GPP Deivce whether the Non-3GPP Device identifier links to the subscription data of the UE or 5G-RG. If not allowed and/or not linked, the SMF will reject UE/5G-RG’s request via SM-NAS signalling and skip rest of the procedure.

NOTE 3: The SMF shall first perform the secondary authentication for UE/5G-RG if required.

5. The SMF shall trigger EAP Authentication of the Non-3GPP Device to obtain authorization from an external DN-AAA server by sending a EAP authentication request message, which contains the Non-3GPP Device identifier.

6. The DN-AAA server and the UE shall exchange EAP messages via the UPF and UE/5G-RG, as required by the EAP method. In addition, it may send additional authorization information as defined in TS 23.501 clause 5.6.6.

7. After the successful completion of the authentication procedure, DN-AAA server shall send EAP Success message to the SMF. This message contains the Non-3GPP Device identifier and a MSK (optional).

8. The SMF shall store the authentication and authorization result of Non-3GPP Device and add the Non-3GPP Device identifier to the SM context of the UE/5G-RG and mark as authorized by requested service.

9. The SMF may notify the authentication and authorization result of Non-3GPP Device to UDM and/or specific NF where store the profile of the Non-3GPP Deivce. The SMF then may request the session policy associate with the Non-3GPP Device from PCF.

Editor’s Note: What the Non-3GPP Device profile contains and where the Non-3GPP Device Profile is stored is FFS and will be defined by SA2.

10. The SMF shall perform rest of the PDU Session Establishment or Modification procedure.

11. The SMF send a NAS SM PDU Session Establishment or Modification Accept message to the UE/5G-RG via the AMF. This message shall include EAP success message to be sent to the UE/5G-RG and the Non-3GPP Device. The SMF shall also include a MSK (if received in step 7) in NAS SM message.

12. The UE/5G-RG shall store the authentication and authorization result of the Non-3GPP Device to do some operation like access control, e.g. restrict the number of devices activated simultaneously. The UE/5G-RG shall store the MSK and associated Non-3GPP Device identifier if received in NAS SM message.

13. The UE/5G-RG may Establish/Re-establish the security protection for direct connection with the Non-3GPP Device based on the received MSK. After successful complete the step 3-12, the UE/5G-RG start to forward the traffic from the Non-3GPP Device to network.

### 6.Y.3	Re-Authentication procedure

Figure 6.Y.3-1 Re-Authentication procedure of Non-3GPP Device behind gateway UE or 5G-RG

0. The UE/5G-RG registers with the network performing primary authentication.

1. The authentication and authorization procedure of Non-3GPP Device was successfully executed.

2a.	The SMF decides to initiate Re-Authentication procedure of the Non-3GPP Device.

2b-1. The DN AAA server decides to initiate Re-Authentication of the Non-3GPP Device.

2b-2. The DN AAA shall send a Re-Authentication request to the SMF via UPF. The Re-authentication request contains the Non-3GPP Device identifier and other parameters as specified in clause 11.1.3 of TS 33/501 [x].

3-4. The SMF shall send an EAP Request/Identity message to the UE/5G-RG, which contain the Non-3GPP Device identifier. Upon received this message, the UE/5G-RG stop forwarding the traffic of the Non-3GPP Device to network, and responds an EAP Response/Identity message to the SMF, which contain the Non-3GPP Device identifier.

5-13. Execute the same operation as step 5-13 in clause 6.Y.2.

### 6.Y.3	Authentication and Authorization revocation

At any time, the DN-AAA server may revoke the authentication and authorization for a PDU Session associated with the Non-3GPP Device, and according to the request from the DN-AAA server, the SMF may modify or release the PDU Session associated with the Non-3GPP Device.

### 6.Y.4	Evaluation

TBD

*************** End of the change ****************