## Slide 1: Discussion on management enhancements related to NR MIMO
Source: China Unicom

## Slide 2
Background
With the rapid emergence of new services such as UAV and NTN scenarios , an efficient and flexible NR MIMO management mechanism is essential to support 3-D coverage optimization and frequent modifcation.
NTN scenario：Satellites move rapidly and beam switching is more frequent.The ground base station beam in fixed, when the beam coverage area changes, it can cause multiple UEs within the beam coverage area to simultaneously avoid beam switching.
Fig1 UAV scenario
UAV scenario：Change from the 1-beam/7-beam for the ground coverage to a 4+3 stereo beam for both ground coverage and aerial coverage.
Fig3 Major activities assurance scenario
Major activities assurance scenario:A large stadium has multiple areas, and the distribution of users unpredictedly varies when hosting large competitions or concerts within a day.
Fig2 NTN scenario
From:3GPP 38.821 V0 (03)Solutions for NR to support non-terrestrial networks (NTN)
Notes: 3GPP NTN在R17\R18采用了透明转发架构示例：卫星快速移动，波束切换更频繁，而地面固定波束场景，当波束覆盖区域发生变化，会导致波束覆盖区域内多个UE同时省波束切换
﻿

## Slide 3
Background
As the NR construction increases cost for operators , it is necessary to balance capex and opex in development. On the basis of traditional coverage optimization goals, an efficient and flexible NR MIMO management mechanism is essential to support and improve both radio resource and energy efficiency.
Beam power optimization to support energy optimization
Fig4 Illustration of SSB beams covering full cell coverage area
Fig5 Illustration of SSB beams modifying to meet the UE centralized coverage with MDAS recommendation
Beamforming and SSB optimization to support radio resource efficiency
Figure4 depicts SSB beams covering full cell coverage area. Figure 5 depicts SSB beams modifying to meet the UE centralized coverage after updating the coverage shape for target cell of gNodeB using the recommendation by MDAS.
It is necessary to consider using MDAS to improve radio resource usage. MnS consumer could request MDAS to acquire beam-level management data and recommend coverage shape based on analysis.
To reduce energy consumption, SSB beams which are not required based on traffic demand can be modified or deactivated. For example, as depicted in Figure 7, if the expected traffic (hotspot area) can be covered by 3 beams, then the remaining beams can be deactivated. This energy saving techniques depend on the accuracy of where the expected traffic demand comes from geographically, so that it can be correlated with SSB beam coverage areas.
From:1、3GPP TR 28.886 Add solution for radio resource optimization based on per SSB usage
2、3GPP TR 28.866 Energy Saving based on throughput requirements
Fig6 Illustration of SSB beams covering full cell coverage area. | Fig7 Illustration of reduced number of SSB beams covering only hotspot area.

## Slide 4
Background
Massive MIMO sub-features have been proposed and studied in O-RAN, which have not been studied in 3GPP.
O-RAN Massive MIMO optimization as follows:
Massive MIMO Grid-of-Beams Beamforming (GoB BF) optimization
Massive MIMO Non-GoB Beamforming (Non-GoB BF) optimization
MIMO optimization via MIMO DL Tx power optimization, MU-MIMO pairing, and MIMO mode selection
Initial access (SS Burst Set) configuration optimization
From:《O-RAN.WG2.TS.Use-Case-Requirements-R004-v10.04》O-RAN Massive MIMO optimization
Massive MIMO optimization is one of the top priority use cases in O-RAN. Massive MIMO optimization is one of the top priority use cases in O-RAN. Several massive MIMO sub-features have been proposed and studied during the massive MIMO pre-normative study, which is documented in the O-RAN.WG1.MMIMO-USE-CASES-TR-v01.00, including the potential data requirements for each of the sub-use cases.
Fig8 Massive MIMO Grid-of-Beams Beamforming (GoB BF) optimization

## Slide 5
Detailed proposal
WT-1: Analyze and identify NR MIMO network management enhancement requirements for different scenarios. This work task includes:
• Identify different scenarios for NR MIMO management enhancement:
    - 3-D Coverage optimization to support UAV and NTN scenarios
    - Beamforming and SSB optimization to support radio resource efficiency
    - Beam power optimization to support energy optimization
• Identify whether and how existing 5G management Specifications can support these identified scenarios.
WT-2: Investigate potential enhancements of configuration and performance management to support fine-grained and flexible evaluation and optimization.
WT-3: Coordination with O-RAN Alliance: Investigate whether and how existing use cases, requirements and solutions of Massive MIMO optimization from O-RAN can apply to existing NR MIMO management.
The study could be structured around two main work tasks (WTs) focuses on potential management enhancements related to NR MIMO, including:

## Slide 6
Conclusion
China Unicom proposes to initiate a research program (SID) in SA5 to investigate potential use cases, requirements, and solutions to enhance existing NR MIMO-related management.O-RAN has conducted relevant study on Massive MIMO optimization. SA5 has already investigate some use cases on beam management, but the flexible and efficient capabilities are still needed to for further study.
China Unicom kindly requests the discussion and approval of the accompanying documents to proceed with this initiative.