3GPP TSG-SA5 Meeting #154 	S5-241836

Changsha, China, 15 - 19 April 2024

Title:	LS on 3GPP Reservation of Edge Resources and Correlation information for API volume based charging

Response to:	LS to 3GPP_Reservation of Edge Resources (S5-241341) & LS to 3GPP_Correlation information for API volume based charging (S5-241342)

Release:	-

Work Item:	-

Source:	3GPP SA5

To:	GSMA OPAG

Cc:	3GPP SA2, 3GPP SA6, 3GPP SA, GSMA OPG

Contact person:	Maryse Gardella

Maryse.gardella@matrixx.com

Send any reply LS to:	3GPP Liaisons Coordinator, mailto:3GPPLiaison@etsi.org

Attachments:	None

# 1	Overall description

3GPP SA5 thanks GSMA OPAG for both their LSs (LSs OPAG_94_Doc_08/S5-241341and  OPAG_94_Doc_07/S5-241342/) on charging considerations in the context of their Operator Platform.

3GPP SA5 charging has discussed the two LSs and would like to provide preliminary feedback and ask for additional information to GSMA OPAG.

Regarding the LS to 3GPP_Reservation of Edge Resources (OPAG_94_Doc_08/S5-241341):

The scenario of charging "API Invocation from application provider to the Operator Platform for edge resources reservation", based on criteria such as Virtual CPU usage, Virtual memory usage… is currently not supported by 3GPP SA5 Charging specifications.

3GPP TS 32.257 "Telecommunication management; Charging management; Edge computing domain charging" specifies charging solutions in the edge computing area, including for edge resources actual usage (mean virtual CPU usage, mean virtual memory usage…), however they do not address the scenario for edge resources reservation, and more investigation would be needed to introduce appropriate ones. Regarding the LS to 3GPP_Correlation information for API volume based charging (OPAG_94_Doc_07/S5-241342):

3GPP SA5 understands the "CAMARA Quality on Demand API" is one example used by GSMA OPAG to describe their need for correlation for charging purpose, between API Invocation to the Operator Platform for certain category of services, and these services actual usage in the Operator’s Network, considering the NEF as the typical entry point in the Mobile Operator’s Network. Based on this, 3GPP SA5 would like to know which NEF services amongst those specified by 3GPP SA2 in TS 23.502 "Technical Specification Group Services and System Aspects; Procedures for the 5G System (5GS); Stage 2" are being considered by GSMA OPAG in this context. This would help to further investigate, in collaboration with 3GPP SA2 and possibly with SA6, on whether capabilities are specified or not for such correlation, so they could be considered under the charging framework by 3GPP SA5 if needed.

3GPP SA5 NEF charging is available under 3GPP TS 32.254: "Telecommunication management; Charging management; Exposure function Northbound Application Program Interfaces (APIs) charging".

3GPP SA5 has been notified by GSMA OPG (under LS on GSMA OPG PRDs publication (OPG_172_Doc_03/S5-241339)), about the newly available GSMA PRD OPG.07 Southbound Interface Charging Function APIs (SBI-CHF), referred-to in both LSs. This GSMA PRD will also be taken into consideration in further exchanges on these charging related topics.

# 2	Actions

To GSMA OPAG:

ACTION: 	3GPP SA5 kindly requests GSMA OPAG to take the above information into account.

# 3	Dates of next TSG SA WG 5 meetings

SA5#155		27 May - 31 May 2024		Jeju, Korea

SA5#156		19 August - 23 August 2024	Maastricht, Netherlands