3GPP TSG-SA5 Meeting #154 	S5-241963

Changsha, China, 15 - 19 April 2024

# Source:	China Mobile

# Title:	pCR 28.869 Add Background of VNF generic OAM functions

# Document for:	Approval

Agenda Item:	6.19.6

# 1	Decision/action requested

The group is asked to discuss and approval.

# 2	References

[1]	3GPP TR 28.869 v0.1.0 Study on cloud aspects of management and orchestration.

# 3	Rationale

The framework of this TR 28.869 is mainly divided into three parts. Considering the relative independence of these three parts and their different backgrounds, especially considering the basic research of VNF generic OAM functions in R18, in order to let readers understand the background more clearly and quickly, this contribution proposes to add background of VNF generic OAM functions in 4.X.

# 4	Detailed proposal

It proposes to make the following changes to TR 28.869 [1].

1st Change

# 2	References

The following documents contain provisions which, through reference in this text, constitute provisions of the present document.

-	References are either specific (identified by date of publication, edition number, version number, etc.) or non-specific.

-	For a specific reference, subsequent revisions do not apply.

-	For a non-specific reference, the latest version applies. In the case of a reference to a 3GPP document (including a GSM document), a non-specific reference implicitly refers to the latest version of that document in the same Release as the present document.

[1]	3GPP TR 21.905: "Vocabulary for 3GPP Specifications".

[X1]                     ETSI GR NFV-EVE 019: "Network Functions Virtualisation (NFV) ;Architectural Framework;Report on VNF generic OAM functions".

[X2]                     3GPP TR 28.834: "Study on management of cloud-native Virtualized Network Functions (VNF)".

[X3]                     ETSI GS NFV-IFA 049 "Network Functions Virtualisation (NFV) Release 5; Architectural Framework; VNF generic OAM functions".

[X4]                     SP-230764 New WID on Management of cloud-native Virtualized Network Functions

# 4	Concepts and background

Editor's Note: This clause introduces the concepts and the background information including the relevant work done by other SDOs or industry organizations.

#### 4.X Background of VNF generic OAM functions

ETSI GR NFV-EVE 019 [X1] defines and analyses the type of OAM functions for VNFs that can be generalized and be provided as a "generic function". It also describes potential solutions regarding the VNF generic OAM functions architectural framework and the interactions with the other entities in the NFV ecosystem.

3GPP TR 28.834“Study on management of cloud-native Virtualized Network Functions (VNF)”[X2] in Release 18 studies potential use cases, requirements and solutions for the management of cloud-native virtualized network functions and the impacts on the 3GPP management system. It also includes some use cases related to VNF generic OAM functions, but the relevant specific solutions were not studied thoroughly due to the fact that the corresponding ETSI GS NFV-IFA 049[X3] was not published prior to the completion of the TR 28.834. As a result, the scope of Rel-18 “WID on management of cloud-native Virtualized Network Functions” [X4] did not include enhancements related to VNF generic OAM functions.

ETSI GS NFV-IFA 049 [X3] specifies the VNF generic OAM functions framework and also specifies the functional requirements and the interface requirements for VNF generic OAM functions. Considering that ETSI GS NFV-IFA 049 has been published, clause 5.1 of  this Rel-19 TR studies the use of VNF generic OAM functions from the perspective of 3GPP management system.

End of Changes