3GPP TSG-SA5 Meeting #154 	S5-241531

Changsha, China, 15 - 19 April 2024

# Source:	China Mobile,ZTE

# Title:	pCR 28.869 Add use case for Log aggregator function and Log analyser function

# Document for:	Approval

Agenda Item:	6.19.6

# 1	Decision/action requested

The group is asked to discuss and approval.

# 2	References

[1]	3GPP TR 28.869 v0.1.0 Study on cloud aspects of management and orchestration.

# 3	Rationale

The contribution proposes to add a new use case for Log aggregator function and Log analyser function.

# 4	Detailed proposal

It proposes to make the following changes to TR 28.869 [1].

1st Change

# 2	References

The following documents contain provisions which, through reference in this text, constitute provisions of the present document.

-	References are either specific (identified by date of publication, edition number, version number, etc.) or non-specific.

-	For a specific reference, subsequent revisions do not apply.

-	For a non-specific reference, the latest version applies. In the case of a reference to a 3GPP document (including a GSM document), a non-specific reference implicitly refers to the latest version of that document in the same Release as the present document.

[1]	3GPP TR 21.905: "Vocabulary for 3GPP Specifications".

[x]                     ETSI GS NFV-IFA 049: "Network Functions Virtualisation (NFV) Release 5; Architectural Framework; VNF generic OAM functions specification"..

# 5	Use cases, potential requirements, and potential solutions

## 5.1	Use of VNF generic OAM functions

Editor's Note: This clause describes the use cases, issues, requirements, and solutions related to WT-1.

### 5.1.x	Use case #X：Log management for the cloud-native VNFs using generic OAM functions

#### 5.1.x.1	Description

This use case is about the log management for the cloud-native VNF using the “VNF Log aggregator function” and “VNF Log analyser function” which are part of the generic OAM functions proposed in ETSI GS NFV-IFA 049 [x].

The VNF Log aggregator function can store and process the logs from the VNF/VNFC/NFVI/NFV-MANO.

When the operator needs the retrieval of logs through 3GPP management system, the 3GPP management system sends requests to the Log aggregator function for retrieval of the logs. The VNF Log aggregator function can store and process the logs from the VNF/VNFC/NFVI/NFV-MANO and after receive the requests from 3GPP management, the Log aggregator function selects the logs based on the request message. The 3GPP management system can receive the selected logs result from VNF log aggregator function and the operator can have the log information requested.

When the operator needs to obtain log analysis results through the 3GPP management system, the 3GPP management system can configure the VNF Log analyser function to process and evaluate the logs provided by the Log aggregator. Then the 3GPP management system can receive the notification results from the VNF log analyser function.

In this use case, the 3GPP management system can use the Log aggregator function and Log analyser function to retrieve and process logs of multiple cloud-native VNFs in a more unified way. For example, that can reduce the duplication of work in the fault management of the 3GPP management system.

#### 5.1.x.2	Potential requirements

REQ-LOG GOF-1:The 3GPP management system should have the capability to request the VNF Log aggregator function for the the retrieval of logs.

REQ-LOG GOF-2:The 3GPP management system should have the capability to receive retrieval results of logs from the VNF Log aggregator function.

REQ-LOG GOF-3:The 3GPP management system should have the capability to configure the VNF Log analyser function..

REQ-LOG GOF-4:The 3GPP management system should have the capability to subscribe the notification results from  the VNF Log analyser function.

REQ-LOG GOF-5:The 3GPP management system should have the capability to receive the notification results from the VNF Log analyser function.

#### 5.1.x.3	Potential solutions

#### 5.1.x.4	Evaluation of solutions

End of Changes