3GPP TSG-SA5 Meeting #154 	S5-241968d1

Changsha, China, 15 - 19 April 2024

# Source:	ZTE Corporation

# Title:	pCR TR 28.869 Use case on Software modification management for the cloud-native VNF using generic OAM functions

# Document for:	Approval

Agenda Item:	6.19.6

# 1	Decision/action requested

The group is asked to discuss and approval.

# 2	References

- ETSI GS NFV-IFA 049: "Network Functions Virtualisation (NFV) Release 4; Architectural Framework; VNF generic OAM functions specification"

- 3GPP TR 28.869: "3rd Generation Partnership Project; Technical Specification Group Services and System Aspects; Study on cloud aspects of management and orchestration (Release 19) "

- ETSI GS NFV-IFA 013: " Network Function Virtualisation (NFV); Release 4; Management and Orchestration; Os-Ma-nfvo reference point - Interface and Information Model Specification "

- 3GPP TR 28.525: "3rd Generation Partnership Project; Technical Specification Group Services and System Aspects; Telecommunication management; Life Cycle Management (LCM) for mobile networks that include virtualized network functions; Requirements"

# 3	Rationale

ETSI has published ETSI GS NFV-IFA 049 [1] which specifies the VNF Generic OAM functions framework as part of NFV Release 4. There is a need to study the potential impacts on 3GPP management system for the cloud-native VNF in use cases which make use of the VNF generic OAM functions specified in ETSI.

For VNF software update, the use cases for the operation of VNF software update performed by the EM have been described in clause 5.4.4 of TR 28.525 [4]. In latest published IFA 049 [1], showed in figure, another use case is that the VNF Generic OAM functions are introduced and can be responsible for VNF software update. For new use case, the potential impact on 3GPP management system should be studied.

# 4	Detailed proposal

1st Change

# 5	Use cases, potential requirements, and potential solutions

## 5.1	Use of VNF generic OAM functions

Editor's Note: This clause describes the use cases, issues, requirements, and solutions related to WT-1.

### 5.1.x	Use case #x: Software modification management for the cloud-native VNF using generic OAM functions

#### 5.1.x.1	Description

For VNF software update, the use cases for the operation of VNF software update performed by the EM have been described in clause 5.4.4 of TR 28.525 [4]. In latest published IFA 049 [1], another use case is that the VNF Generic OAM functions are introduced and can be responsible for VNF software update. For new use case, the potential impact on 3GPP management system should be studied.

The software modification management is used to implement the software upgrade of cloud-native VNFs using "Upgrade VNF function " which is one of the generic OAM functions proposed in IFA 049 [1] and  can handle software update of a VNF/VNFC instances.

The network operator has requirements to provide new services by upgrading new software version of cloud-native VNFs. When upgrading cloud-native VNFs, the 3GPP management system can request the Upgrade VNF function to perform the operation of software upgrade,  the Upgrade VNF function performs upgrading the new software of cloud-native VNF instances handling in coordination with NFV-MANO in order to run with new software version on cloud-native VNF instances. After completing the operation, the Upgrade VNF function should notify back to 3GPP management system about the completion of the upgrade action,

In this case, the 3GPP management system can use the Upgrade VNF function to deliver software upgrade requirements of cloud-native VNFs in a unified way. The network operator can provide new services via this upgrade process by the 3GPP system network.

#### 5.1.x.2	Potential requirements

REQ-CVNF_SM_CON-1  The 3GPP management system should be able to request software upgrade of cloud-native VNFs to the Upgrade VNF function.

REQ-CVNF_SM_CON-2  The 3GPP management system should be able to receive responses from the Upgrade VNF function about the results of completion of the cloud-native VNF software upgrade.

#### 5.1.x.3	Potential solutions

#### 5.1.x.4	Evaluation of solutions

End of changes