3GPP TSG-SA5 Meeting #154 	S5-241969d1

Changsha, China, 15 - 19 April 2024

# Source:	ZTE Corporation

# Title:	pCR TR 28.869 Use case on Notification management for the cloud-native VNF using generic OAM functions

# Document for:	Approval

Agenda Item:	6.19.6

# 1	Decision/action requested

The group is asked to discuss and approval.

# 2	References

- ETSI GS NFV-IFA 049: "Network Functions Virtualisation (NFV) Release 4; Architectural Framework; VNF generic OAM functions specification"

- 3GPP TR 28.869: "3rd Generation Partnership Project; Technical Specification Group Services and System Aspects; Study on cloud aspects of management and orchestration (Release 19) "

# 3	Rationale

ETSI has published ETSI GS NFV-IFA 049 [1] which specifies the VNF Generic OAM functions framework as part of NFV Release 4. There is a need to study the potential impacts on 3GPP management system for the cloud-native VNF in use cases which make use of the VNF generic OAM functions specified in ETSI.

# 4	Detailed proposal

1st Change

# 5	Use cases, potential requirements, and potential solutions

## 5.1	Use of VNF generic OAM functions

Editor's Note: This clause describes the use cases, issues, requirements, and solutions related to WT-1.

### 5.1.x	Use case #x: Notification management for the cloud-native VNF using generic OAM functions

#### 5.1.x.1	Description

The notification management is used to implement the notification management for cloud-native VNFs using " Notification manager function" which is one of the generic OAM functions proposed in IFA 049 [1] and can handle  notifications sent by other VNF generic OAM functions, such as alerts. The notification manager function manages the notifications, e.g. deduplication, grouping, and routes the notifications to the intended receiver, e.g. the Operator, NFV-MANO.

The 3GPP management system has the capability to subscribe receiving notifications from the notification manager with the necessary subscription information. When the VNF generic OAM function detects an event related to cloud-native VNFs, and sends a notification to the notification manager, the notification manager function are expected to forward the specific notification to the 3GPP management based on subscription information.

In this case, the 3GPP management system can subscribe receiving notifications of the subscribed events related to the cloud-native VNFs to the network operator.

#### 5.1.x.2	Potential requirements

REQ-CVNF _NM_CON-1  The 3GPP management system should be able to subscribe receiving notifications from the notification manager with the required subscription information.

REQ-CVNF_NM_CON-2  The 3GPP management system should be able to receive the notification from the notification manager.

#### 5.1.x.3	Potential solutions

#### 5.1.x.4	Evaluation of solutions

End of changes