3GPP TSG-SA5 Meeting #154 	S5-241980

Changsha, China, 15 - 19 April 2024

# Source:		China Mobile Com. Corporation

# Title:	pCR TR 28.914 Enhancements of Intent Life Cycle Management

# Document for:	Approval

Agenda Item:	6.19.3

# 1	Decision/action requested

The group is asked to discuss and agree on the proposal.

# 2	References

[1]	Study on intent driven management service for mobile network phase 3 v0.0.0

[2]	SP-231737 "Study on intent driven management services for mobile network phase 3"

[3]	3GPP TS 28.312: "Management and orchestration; Intent driven management services for mobile networks"

# 3	Rationale

In Appendix B.1 of 28.312, it is stated that the intent lifecycle consists of the following phases: Detection, Investigation, Definition, Distribution, and Operation, and the processing flow of each phase is described in detail. However, for the existing processes of each phase, further enhancements can be made from several aspects, including but not limited to the following.

This contribution related to WT-3.2 Intent handling state management.

# 4	Detailed proposal

1st Change

# 5	Use cases

## 5.X Use case#<X>: Enhancements of Intent Life Cycle Management

### 5.X.1 Description

In Appendix B.1 of 28.312, it is stated that the intent lifecycle consists of the following phases: Detection, Investigation, Definition, Distribution, and Operation, and the processing flow of each phase is described in detail. However, for the existing processes of each phase, further enhancements can be made from several aspects, including but not limited to the following.:

- In the detection phase, it is mentioned that "Through intent reports, the MnS Consumer is able to react to intent handling outcomes in the MnS producer." This part needs further enhancement to illustrate the specific reactions the MnS Consumer will take based on different intent reports (intentFulfilmentReport, intentConflictReport, intentFeasibilityCheckReport).

- In the investigation phase, no solution is provided for when the intent content (a list of expectations) is not feasible. This part needs further enhancement to identify subsequent steps when the intent is not feasible, such as reevaluation, seeking alternative solutions, or adjusting intent expectations.

- In the distribution phase, the existing description mentions that "MnS Consumer contacts a MnS producer in order to create a new intent object or modify or change an existing one." However, what needs to be created here is the intent instance, so the "intent object" in the above description should be revised to "intent instance".

- In the operation phase, the existing description lacks detailed processing flow for intent instance updates and deletions. This part requires further enhancement by adding corresponding processing procedures.

Editor’s Note: The requirements and solutions will be added in the future.

End of change