3GPP TSG-SA5 Meeting #154 	S5-241998

# Changsha, CHINA, 15 Apr - 19 Apr 2024					                     revision of S5-241248

# Source:	Huawei

# Title:	New Use case on New measurement method of VNF energy consumption

# Document for:	Approval

Agenda Item:	6.19.20

# 1	Decision/action requested

The group is asked to discuss and agree on the proposal.

# 2	References

[1]		3GPP SP-231723: Study on energy efficiency and energy saving aspects of 5G networks and services

[2]		TR 28.880 0.1.0: Study on energy efficiency and energy saving aspects of 5G networks and services

[3]		S5-241338: LSreply_to_3GPP_SA5_on_metrics_to_estimate_containerized_VNF

# 3	Rationale

Amongst other study objectives in [1], WT-1.1 addresses the issue about the estimation of VNF energy consumption:

“

WT-1: Left-over SA5 topics from Rel-18

WT-1.1 Study new or enhanced Energy Consumption (EC) and Energy Efficiency (EE) KPIs and measurements, e.g. for new types of network slices, RAN sharing, etc.

”.

To address this, this contribution proposes to introduce a new key issue in TR 28.880 [2].

As described in [3], it indicates that

“In addition, as part of the development of the FEAT29 on “Green NFV”, new measurements are being defined regarding actual energy consumption of virtualized resources and containerized workloads, in clauses 7.1 and 7.4 of the same ETSI GS NFV-IFA 027 draft version, respectively. As these measurements are expected to provide more accurate energy consumption associated to VNF/VNFC, there is an expectation that there will be no need for 3GPP SA5 of having to compute estimate values, and instead leverage the energy consumption measurements directly associated to VNF/VNFC.”

The estimated measurement of energy consumption of VNF/VNFC has a lot of drawbacks (e.g., not easy to calculate all the virtual compute resource instances information running on the same NFVI Node).

It is suggested to use actual energy consumption measurement in Rel 19 by using the way as provided in ETSI GS NFV-IFA 027.

# 4	Detailed proposal

This document proposes the following changes in TR 28.880 [2].

1st Change

# 2	References

The following documents contain provisions which, through reference in this text, constitute provisions of the present document.

-	References are either specific (identified by date of publication, edition number, version number, etc.) or non-specific.

-	For a specific reference, subsequent revisions do not apply.

-	For a non-specific reference, the latest version applies. In the case of a reference to a 3GPP document (including a GSM document), a non-specific reference implicitly refers to the latest version of that document in the same Release as the present document.

[1]	3GPP TR 21.905: "Vocabulary for 3GPP Specifications".

[a]	3GPP TS 28.554: "Management and orchestration; 5G end to end Key Performance Indicators (KPI)".

[b]	ETSI GS NFV-IFA 027 V5.1.1 (2024-4): "Network Functions Virtualisation (NFV) Release 5; Management and Orchestration; Performance Measurements Specification".

Editor’s note: reference [b] is not published yet, will be published soon.

Next Change

## 5.x	Use case #<x>: Actual energy consumption of VNF/VNFC

### 5.x.1	Description

For Energy Consumption (EC) of VNF/VNFCs only estimated measurement is supported as defined in clauses 6.7.3.1.2 and 6.7.3.1.3 of TS 28.554 [a]). The way to calculate the estimated VNF/VNFC energy consumption requires obtaining the sum of the vCPU mean usage of all virtual compute resource instances running on the same NFVI Node during the same observation period, all separately provided by NFV MANO (see clause 7.1.2 of ETSI GS NFV-IFA 027 [b]).

The issue is that there is no easy way to obtain all virtual compute resource instances information running on the same NFVI Node and measure the vCPU mean usage for all of them. The measurement method as described in clause 7.1.2 of ETSI GS NFV-IFA 027 [b] does not support setting the measurement scope on the same NFVI Node. Some other mechanism to know all the virtual compute resource instances information running on the same NFVI Node is required.

As described in clause 7.1.18 and clause 7.4.12 of ETSI GS NFV-IFA 027 [b], the actual energy consumption of virtual compute and OS container workload is provided. As an enhancement, this use case is to study:

a) potential enhancements to existing Energy Consumption (EC) of VM-based VNF/VNFCs measurement and

b) potential extension to Energy Consumption (EC) of containerized VNF/VNFCs measurement.

### 5.x.2		Potential Requirements

REQ-ENHANCEMENT-MEAS-01: The 3GPP management system should have a capability to provide the actual energy consumption of VM-based VNF/VNFCs.

REQ-ENHANCEMENT-MEAS-02: The 3GPP management system should have a capability to provide the actual energy consumption of containerized VNF/VNFCs.

End of change