3GPP TSG-SA5 Meeting #154 	S5-242004

# Changsha, China, 15-19 Apr. 2024

# Source:	Huawei

# Title:	New Use Case on exposure of energy related information

# Document for:	Approval

Agenda Item:	6.19.20

# 1	Decision/action requested

The group is asked to discuss and agree on the proposal.

# 2	References

[1]		3GPP TS 22.261: Service requirements for the 5G system; Stage 1

[2]		3GPP TR 23.700-66: Study on Energy Efficiency and Energy Saving

[3]		3GPP SP-231723: Study on energy efficiency and energy saving aspects of 5G networks and services

[4]		3GPP TR 28.880 0.1.0: Study on energy efficiency and energy saving aspects of 5G networks and services

# 3	Rationale

TS 22.261 [1] clause 6.15a makes the following statements:

“

6.15a	Energy Efficiency as a Service Criteria

6.15a.1	Description

Climate change and the rising consumption of energy motivate increased energy efficiency. Energy efficiency is a strategic priority for telecom operators around the world.

Energy efficiency as a service criteria allows services to be delivered with diverse energy efficiency and energy consumption policies. Energy consumption and efficiency information and network energy states can be exposed to third parties and energy consumption can be constrained.

Energy related information can include ratio of renewable energy and carbon emission information when available. Calculation of energy related information as described in the following requirements is done by means of averaging or applying a statistical model. The requirements do not imply that some form of 'real time' monitoring is required.

”.

TR 23.700 [2] clause 5.1 describes the following key issue:

“

5.1	Key Issue #1: Network energy related information exposure

5.1.1	Description

Subject to operator policy, network energy related information (e.g. energy consumption related information, energy efficiency related information, renewable energy and carbon emission related information) may be exposed by the network to the authorized consumers.

To support network energy related information exposure, the following aspects are to be studied:

-	Whether and what network energy related information can be exposed.

-	At what granularity (e.g. per network slice, UE, NF, PDU Session, QoS flow, etc) the network energy related information can be exposed.

-	How the network energy related information is exposed.

-	How and what network energy related information from the Network entities (i.e. RAN nodes, 5GC NFs) can be obtained in order to support network energy related information exposure.

NOTE 1:	Existing mechanism and information (e.g. information collected by OAM as defined in TS 28.310 [7]) are reused when possible.

NOTE 2:	The study will address use cases corresponding to the identified consolidated requirements as described in clause 6.4 of TR 22.882 [5]. The network energy related information to be exposed, the authorized consumer, and how the information is exposed depend on the use case. Solutions should identify related use cases which will be addressed.

”.

SA2 is also studying several potential solutions where the OAM should be able to expose energy related information to the 5G core network; several 5GC NFs are potential candidates for consuming energy related information exposed by the OAM. See clause 6 of TR 23.700-66 [2].

Amongst other study objectives in [3], WT-2 scope includes working on comprehensive use cases and solutions involving e.g. the 5G core network and the OAM:

“

- WT-2: New Rel-19 topics from other SA WGs

- WT-2.1 Consideration of energy consumption measurement/estimation at various granularities

- WT-2.2 Study whether and how mapping measured or estimated energy consumption measurements on to carbon emissions is possible. Study the estimation of carbon emissions efficiency and how to achieve carbon emissions saving in the 5G system. Additionally, whether and how renewable energy consumption information can be obtained will be studied

- WT-2.3 Study the support of different energy states of network elements and network functions. SA5 may have to provide OAM support

NOTE: the exact scope of WoP#2 may have to be adjusted depending on ongoing Rel-19 SA1 work item (EnergyServ) and SA2 study item (FS_CNEES) outcomes.

”.

To address how energy related information can be exposed to authorized consumers (including 5GC NFs, AF, etc.), this contribution proposes to introduce a new use case in TR 28.880 [4].

# 4	Detailed proposal

This document proposes the following changes in TR 28.880 [4].

1st Change

# 2	References

The following documents contain provisions which, through reference in this text, constitute provisions of the present document.

-	References are either specific (identified by date of publication, edition number, version number, etc.) or non-specific.

-	For a specific reference, subsequent revisions do not apply.

-	For a non-specific reference, the latest version applies. In the case of a reference to a 3GPP document (including a GSM document), a non-specific reference implicitly refers to the latest version of that document in the same Release as the present document.

[1]	3GPP TR 21.905: "Vocabulary for 3GPP Specifications".

[a]	3GPP TS 22.261: "Service requirements for the 5G system; Stage 1".

[b]	ETSI GS OEU 020 V1.1.1 (2020-03): "Operational energy Efficiency for Users (OEU); Carbon equivalent Intensity measurement; Operational infrastructures; Global KPIs; Global KPIs for ICT Sites".

[c]	ETSI EN 303 472 V1.0.0 (2018-06): "Environmental Engineering (EE); Energy Efficiency measurement methodology and metrics for RAN equipment".

[d]	3GPP TS 28.552: "Management and orchestration; 5G performance measurements".

[e]	3GPP TS 28.554: "Management and orchestration; 5G end to end Key Performance Indicators (KPI)".

Next Change

# 5	Use cases

## 5.X	Use case X: Exposure of carbon and renewable energy related information

### 5.X.1	Description

In this use case, authorized consumers collect, from the 3GPP management system, various per 5GC NF and per gNB energy related information, e.g. (non-exhaustive list):

- energy consumption measurements and/or KPIs

- energy saving state

- carbon and renewable energy related information:

- carbon emission information

- carbon emission efficiency

- renewable energy factor.

.

### 5.X.2	Potential requirements

REQ-Energy_info_exposure-CON-1: The 3GPP management system should enable authorized consumers to collect per 5GC NF information such as e.g. energy consumption measurements and/or KPIs, energy saving state, carbon and renewable energy related information i.e. carbon emission information, carbon emission efficiency and renewable energy factor.

REQ-Energy_info_exposure-CON-2: The 3GPP management system should enable authorized consumers to collect per gNB information such as e.g. energy consumption measurements and/or KPIs, energy saving state, carbon and renewable energy related information i.e. carbon emission information, carbon emission efficiency and renewable energy factor, .

### 5.X.3	Potential solutions

#### 5.X.3.1	Potential solution #1: Based on PerfMetricJob

##### 5.X.3.1.1	Introduction

##### In this potential solution, authorized consumers collect, from the 3GPP management system, energy related information by means of performance metrics jobs. In this case, an authorized consumer requests the 3GPP management system to create a PerfMetricJob instance in order to collect per 5GC NF and per gNB energy information.5.X.3.1.2	Description

The authorized Management Service consumer requests the 3GPP management system (as Management Service producer) to create a PerfMetricJob instance, with the following input parameters:

- performanceMetrics, to indicate the expected performance metrics, i.e. measurements defined in TS 28.552 (e.g. PEE.Energy) and/or KPIs defined in TS 28.554 (e.g. ECNF)

- granularityPeriod, to indicate the granularity period to be applied to produce expected performance metrics

- objectInstances, to indicate (if present) the object instances for which performance metrics are expected (e.g. it may contain a (list of) gNB Distinguished Name(s))

- rootObjectInstances, to indicate (if present) the subtrees whose root objects are identified by this parameter, for which performance metrics are expected (e.g. it may contain a (list of) SubNetwork Distinguished Name(s))

- reportingCtrl, to indicate the method and associated control parameters for reporting the produced measurements to the consumer. Three methods are available:

- file-based reporting with selection of the file location by the 3GPP management system (producer),

- file-based reporting with selection of the file location by the 5GC NF (consumer),

- stream-based reporting.

It should be noted that the creation of PerfMetricJob instances by MnS consumers (e.g. a 5GC NF) is optional; when not supported, PerfMetricJob instances may be created and deleted by the system or be pre-installed.

#### 5.X.3.2	Potential solution #2: Based on ManagementDataCollection

##### 5.X.3.2.1	Introduction

In this potential solution, authorized consumers collect, from the 3GPP management system, energy related information by means of management data services. In this case, the authorized consumer requests the 3GPP management system to create a ManagementDataCollection instance in order to collect per 5GC NF and per gNB energy information.

##### 5.X.3.2.2	Description

The authorized Management Service consumer requests the 3GPP management system (as Management Service producer) to create a ManagementDataCollection instance, with the following input parameters:

- managementData: to indicate the management data which shall be reported. This may either include a list of data categories (e.g. "ENERGY_EFFICIENCY"), or a list of management data identified with their name (e.g. PEE.Energy or ECNF)

- targetNodeFilter: to indicate the target object instance(s) producing the required management data. As it is likely that the 5GC NF (as consumer) may not have detailed knowledge of the network, it may not be able to identify the exact object instance producing the required management data. In this case, the consumer can request management data produced by certain object instance(s) based on:

- a particular location (e.g. list of TAI, a list of cells (identified either by NG-RAN CGI, E-UTRAN CGI or UTRAN CGI) or by a geographical area), and/or

- the domain of the object instances (e.g. CN or RAN), and/or

- the type of traffic handled by the object instances (CP or UP)

- collectionTimeWindow: to indicate the time window for which the management data should be reported

- reportingCtrl: to indicate the method and associated control parameters for reporting the produced management data to the consumer (i.e. the 5GC NF). Three methods are available:

- file-based reporting with selection of the file location by the 3GPP management system (producer)

- file-based reporting with selection of the file location by the 5GC NF (MnS consumer)

- stream-based reporting

- dataScope: to indicate whether the management data should be reported per S-NSSAI or per 5QI or per PLMN, if applicable.

### 5.X.4	Evaluation of potential solutions

Editor's Note:	This clause provides the evaluation of potential solutions.

End of change